## Slide 1: ECE 463/563 Microprocessor Architecture
Instruction-Level Parallelism (ILP)
and Its Exploitation:
H&P Chapter 3
Prof. Eric Rotenberg

## Slide 2: “issue”
The term “issue” refers to advancing an instruction to the execute stage when all of its source operands are ready. We say, for example, “issue to a function unit”.
In-order issue:
  Instructions issue strictly in program order
  A younger instruction cannot issue before an older instruction
Out-of-order (OOO) issue:
  Instructions may issue out of program order
  Younger instructions may issue before older instructions

## Slide 3: Outline
From in-order issue to out-of-order issue:
  Issue Queue (IQ)
Speculation and register renaming:
  Reorder Buffer (ROB)

## Slide 4: Key for RISC ISA Pseudo-assembly
KEY:
add rd, rs1, rs2 // RF[rd] = RF[rs1] + RF[rs2]
load rd, #d(rs1) // RF[rd] = MEM[ RF[rs1] + d ]
store #d(rs1), rs2 // MEM[ RF[rs1] + d ] = RF[rs2]

## Slide 5: Review of Data Hazards
A data hazard exists when two dependent instructions are in the pipeline at the same time
  Three types of data dependencies: true, anti-, output
Read-after-write (RAW) hazard
  Stems from a true dependence
  add R1, R2, R3
  add R4, R1, R5
Write-after-read (WAR) hazard
  Stems from an anti-dependence
  add R1, R2, R3
  add R2, R4, R5
Write-after-write (WAW) hazard
  Stems from an output dependence
  add R1, R2, R3
  add R1, R4, R5

## Slide 6: From in-order to OOO
Limitation of our simple 5-stage pipeline
  Blocking Execute Stage
    Single universal unpipelined ALU
      EX stage blocks for a multi-cycle instruction
    MEM stage
      Cache-missed load or store in MEM stage blocks ALU-type instructions in EX stage
    These are structural hazards
  The blocking Execute Stage obscures key distinction between in-order issue and OOO issue
    How data hazards are handled (RAW, WAR, and WAW)
    Structural hazard supersedes data hazards

## Slide 7: From in-order to OOO (cont.)
A more aggressive in-order scalar pipeline
  Non-blocking Execute Stage
    Removes structural hazards
  Highlight the nature of “in-order issue” policy
    An instruction stalls if it has a RAW hazard with a preceding instruction
      That’s o.k. (it must)
    All instructions after it also stall
      This is the “in-order issue” policy, and where the problem lies
  Stepping-stone for OOO implementation

## Slide 8: From in-order to OOO (cont.)
Out-of-order scalar pipeline
  An instruction stalls if it has a RAW hazard with a preceding instruction
    That’s o.k. (it must)
  Independent instructions after it do not stall: they may issue out of program order
  Two alternatives for handling WAR and WAW hazards:
    Like in-order, stall the instruction and all instructions after it
    Eliminate WAR and WAW hazards with register renaming

## Slide 9: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem

## Slide 10: In-order Scalar Pipeline
Scalar:
fetch 1 instr/cycle
decode 1 instr/cycle
issue 1 instr/cycle to a function unit
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
Assumptions:

## Slide 11: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
Execute stage:
Contains multiple function units (FUs) to support different instruction classes.
Multi-cycle function units are pipelined (e.g., Complex ALU, Mem).
Therefore: may observe multiple instructions executing concurrently, yet only 1 new instruction may begin executing in a cycle (scalar issue).
Assumptions:

## Slide 12: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
Assumptions:
Issue logic:
RAW hazard: Instruction stalls if its source register(s) are not ready.
WAW hazard: Non-blocking Execute Stage plus different FU latencies introduce out-of-order writeback. O.K. if writes are to different registers. Not O.K. if writes are to the same register. Instruction stalls if its destination register is “busy”, i.e., conflicts with destination register of older instruction in Execute Stage.
WAR hazard: Not a problem in in-order pipelines. In-order issue ensures read by first instruction happens before write by second instruction.

## Slide 13: RAW example
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
Issue logic:
RAW hazard: Instruction stalls if its source register(s) are not ready.
WAW hazard: Non-blocking Execute Stage plus different FU latencies introduce out-of-order writeback. O.K. if writes are to different registers. Not O.K. if writes are to the same register. Instruction stalls if its destination register is “busy”, i.e., conflicts with destination register of older instruction in Execute Stage.
WAR hazard: Not a problem in in-order pipelines. In-order issue ensures read by first instruction happens before write by second instruction.
mul r3, r1, r2
add r5, r3, r4

## Slide 14: WAW example
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
Issue logic:
RAW hazard: Instruction stalls if its source register(s) are not ready.
WAW hazard: Non-blocking Execute Stage plus different FU latencies introduce out-of-order writeback. O.K. if writes are to different registers. Not O.K. if writes are to the same register. Instruction stalls if its destination register is “busy”, i.e., conflicts with destination register of older instruction in Execute Stage.
WAR hazard: Not a problem in in-order pipelines. In-order issue ensures read by first instruction happens before write by second instruction.
mul r3, r1, r2
add r3, r4, r5

## Slide 15: WAR example
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
Issue logic:
RAW hazard: Instruction stalls if its source register(s) are not ready.
WAW hazard: Non-blocking Execute Stage plus different FU latencies introduce out-of-order writeback. O.K. if writes are to different registers. Not O.K. if writes are to the same register. Instruction stalls if its destination register is “busy”, i.e., conflicts with destination register of older instruction in Execute Stage.
WAR hazard: Not a problem in in-order pipelines. In-order issue ensures read by first instruction happens before write by second instruction.
mul r3, r1, r2
add r5, r3, r4
add r3, r6, r7

## Slide 16
Scenario 1
i1: load r2, #0(r1)
i2: add r4, r3, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
Scenario 1: load miss followed by independent instructions

## Slide 17: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |  |  | 
i1 |  |  |  |  |  |  |  |  |  |  |  |  | 
i2 |  |  |  |  |  |  |  |  |  |  |  |  | 
i3 |  |  |  |  |  |  |  |  |  |  |  |  | 
I4 |  |  |  |  |  |  |  |  |  |  |  |  | 
 | rdy
r0 | 1
r1 | 1
r2 | 1
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
Scoreboard
Register File
tag (wakeup)
data
i1: load r2, #0(r1)
i2: add r4, r3, #1
i3: add r6, r5, #2
i4: add r7, r6, #3

## Slide 18: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
i1: load r2, #0(r1)
i2: add r4, r3, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |  |  | 
i1 | FE |  |  |  |  |  |  |  |  |  |  |  | 
i2 |  |  |  |  |  |  |  |  |  |  |  |  | 
i3 |  |  |  |  |  |  |  |  |  |  |  |  | 
I4 |  |  |  |  |  |  |  |  |  |  |  |  | 
i1
D$
Mem
 | rdy
r0 | 1
r1 | 1
r2 | 1
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
Scoreboard
Register File
tag (wakeup)
data

## Slide 19: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |  |  | 
i1 | FE | DE |  |  |  |  |  |  |  |  |  |  | 
i2 |  | FE |  |  |  |  |  |  |  |  |  |  | 
i3 |  |  |  |  |  |  |  |  |  |  |  |  | 
I4 |  |  |  |  |  |  |  |  |  |  |  |  | 
i2
i1
i1: load r2, #0(r1)
i2: add r4, r3, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
D$
Mem
 | rdy
r0 | 1
r1 | 1
r2 | 1
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
Scoreboard
Register File
tag (wakeup)
data

## Slide 20: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |  |  | 
i1 | FE | DE | RR |  |  |  |  |  |  |  |  |  | 
i2 |  | FE | DE |  |  |  |  |  |  |  |  |  | 
i3 |  |  | FE |  |  |  |  |  |  |  |  |  | 
I4 |  |  |  |  |  |  |  |  |  |  |  |  | 
i3
i2
i1
i1: load r2, #0(r1)
i2: add r4, r3, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
D$
Mem
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
Scoreboard
Register File
r2,#0,#44
tag (wakeup)
data

## Slide 21: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |  |  | 
i1 | FE | DE | RR | EX@ |  |  |  |  |  |  |  |  | 
i2 |  | FE | DE | RR |  |  |  |  |  |  |  |  | 
i3 |  |  | FE | DE |  |  |  |  |  |  |  |  | 
I4 |  |  |  | FE |  |  |  |  |  |  |  |  | 
i4
i3
i2
i1
i1: load r2, #0(r1)
i2: add r4, r3, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
r2,#0,#44
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 0
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | -
r5 | #15
r6 | #-7
r7 | #345
Scoreboard
Register File
tag (wakeup)
data
r4,#33,#1

## Slide 22: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |  |  | 
i1 | FE | DE | RR | EX@ | EXD$ | …miss… |  |  |  |  |  |  | 
i2 |  | FE | DE | RR | EX |  |  |  |  |  |  |  | 
i3 |  |  | FE | DE | RR |  |  |  |  |  |  |  | 
I4 |  |  |  | FE | DE |  |  |  |  |  |  |  | 
i5
i4
i3
i2
i1: load r2, #0(r1)
i2: add r4, r3, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 0
r5 | 1
r6 | 0
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | -
r5 | #15
r6 | -
r7 | #345
Scoreboard
Register File
tag (wakeup)
data
i1
r2,@44
miss
r4
r4,#33,#1
r6,#15,#2

## Slide 23: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |  |  | 
i1 | FE | DE | RR | EX@ | EXD$ | …miss… |  |  |  |  |  |  | 
i2 |  | FE | DE | RR | EX | WB |  |  |  |  |  |  | 
i3 |  |  | FE | DE | RR | EX |  |  |  |  |  |  | 
I4 |  |  |  | FE | DE | RR |  |  |  |  |  |  | 
i6
i5
i4
i3
i1: load r2, #0(r1)
i2: add r4, r3, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 1
r5 | 1
r6 | 0
r7 | 0
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | #34
r5 | #15
r6 | -
r7 | -
Scoreboard
Register File
tag (wakeup)
data
i1
r2,@44
miss
r6,#15,#2
i2
r4,#34
r4,#34
r6
r7,r6,#3

## Slide 24: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |  |  | 
i1 | FE | DE | RR | EX@ | EXD$ | …miss… |  |  |  |  |  |  | 
i2 |  | FE | DE | RR | EX | WB |  |  |  |  |  |  | 
i3 |  |  | FE | DE | RR | EX | WB |  |  |  |  |  | 
I4 |  |  |  | FE | DE | RR | EX |  |  |  |  |  | 
i7
i6
i5
i4
i1: load r2, #0(r1)
i2: add r4, r3, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 0
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | #34
r5 | #15
r6 | #17
r7 | -
Scoreboard
Register File
tag (wakeup)
data
i1
r2,@44
miss
i3
r6,#17
r6,#17
r7,#17,#3
r7

## Slide 25: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |  |  | 
i1 | FE | DE | RR | EX@ | EXD$ | …miss… |  |  |  |  |  |  | 
i2 |  | FE | DE | RR | EX | WB |  |  |  |  |  |  | 
i3 |  |  | FE | DE | RR | EX | WB |  |  |  |  |  | 
I4 |  |  |  | FE | DE | RR | EX | WB |  |  |  |  | 
i8
i7
i6
i5
i1: load r2, #0(r1)
i2: add r4, r3, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
i1
r2,@44
miss
i4
r7,#20
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | #34
r5 | #15
r6 | #17
r7 | #20
Scoreboard
Register File
tag (wakeup)
data
r7,#20

## Slide 26: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |  |  | 
i1 | FE | DE | RR | EX@ | EXD$ | …miss… |  |  |  |  |  |  | 
i2 |  | FE | DE | RR | EX | WB |  |  |  |  |  |  | 
i3 |  |  | FE | DE | RR | EX | WB |  |  |  |  |  | 
I4 |  |  |  | FE | DE | RR | EX | WB |  |  |  |  | 
i9
i8
i7
i6
i1: load r2, #0(r1)
i2: add r4, r3, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
i1
r2,@44
miss
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | #34
r5 | #15
r6 | #17
r7 | #20
Scoreboard
Register File
tag (wakeup)
data
i5
r2

## Slide 27: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |  |  | 
i1 | FE | DE | RR | EX@ | EXD$ | …miss… |  |  |  | WB |  |  | 
i2 |  | FE | DE | RR | EX | WB |  |  |  |  |  |  | 
i3 |  |  | FE | DE | RR | EX | WB |  |  |  |  |  | 
I4 |  |  |  | FE | DE | RR | EX | WB |  |  |  |  | 
i1: load r2, #0(r1)
i2: add r4, r3, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
i1
r2,#666
 | rdy
r0 | 1
r1 | 1
r2 | 1
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | #666
r3 | #33
r4 | #34
r5 | #15
r6 | #17
r7 | #20
Scoreboard
Register File
tag (wakeup)
data
r2,#666
i10
i9
i8
i7
i6

## Slide 28
Scenario 2
Scenario 2: load miss, followed by dependent instruction, followed by independent instructions
i1: load r2, #0(r1)
i2: add r4, r2, #1
i3: add r6, r5, #2
i4: add r7, r6, #3

## Slide 29: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
i1: load r2, #0(r1)
i2: add r4, r2, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
i1 | FE |  |  |  |  |  |  |  |  |  |  |  | 
i2 |  |  |  |  |  |  |  |  |  |  |  |  | 
i3 |  |  |  |  |  |  |  |  |  |  |  |  | 
I4 |  |  |  |  |  |  |  |  |  |  |  |  | 
i1
 | rdy
r0 | 1
r1 | 1
r2 | 1
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
Scoreboard
Register File
tag (wakeup)
data

## Slide 30: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
i1 | FE | DE |  |  |  |  |  |  |  |  |  |  | 
i2 |  | FE |  |  |  |  |  |  |  |  |  |  | 
i3 |  |  |  |  |  |  |  |  |  |  |  |  | 
I4 |  |  |  |  |  |  |  |  |  |  |  |  | 
i2
i1
i1: load r2, #0(r1)
i2: add r4, r2, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
 | rdy
r0 | 1
r1 | 1
r2 | 1
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
Scoreboard
Register File
tag (wakeup)
data

## Slide 31: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
i1 | FE | DE | RR |  |  |  |  |  |  |  |  |  | 
i2 |  | FE | DE |  |  |  |  |  |  |  |  |  | 
i3 |  |  | FE |  |  |  |  |  |  |  |  |  | 
I4 |  |  |  |  |  |  |  |  |  |  |  |  | 
i3
i2
i1
i1: load r2, #0(r1)
i2: add r4, r2, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
Scoreboard
Register File
tag (wakeup)
data
r2,#0,#44

## Slide 32: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
i1 | FE | DE | RR | EX@ |  |  |  |  |  |  |  |  | 
i2 |  | FE | DE | RR |  |  |  |  |  |  |  |  | 
i3 |  |  | FE | DE |  |  |  |  |  |  |  |  | 
I4 |  |  |  | FE |  |  |  |  |  |  |  |  | 
i4
i3
i2
i1: load r2, #0(r1)
i2: add r4, r2, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 0
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | -
r5 | #15
r6 | #-7
r7 | #345
Scoreboard
Register File
tag (wakeup)
data
i1
r2,#0,#44
r4,r2,#1

## Slide 33: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
i4
i3
i2
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
i1 | FE | DE | RR | EX@ | EXD$ | …miss… |  |  |  |  |  |  | 
i2 |  | FE | DE | RR | RR |  |  |  |  |  |  |  | 
i3 |  |  | FE | DE | DE |  |  |  |  |  |  |  | 
I4 |  |  |  | FE | FE |  |  |  |  |  |  |  | 
i1: load r2, #0(r1)
i2: add r4, r2, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 0
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | -
r5 | #15
r6 | #-7
r7 | #345
Scoreboard
Register File
tag (wakeup)
data
i1
r2,@44
miss
r4,r2,#1

## Slide 34: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
i4
i3
i2
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
i1 | FE | DE | RR | EX@ | EXD$ | …miss… |  |  |  |  |  |  | 
i2 |  | FE | DE | RR | RR | RR | RR | RR | RR |  |  |  | 
i3 |  |  | FE | DE | DE | DE | DE | DE | DE |  |  |  | 
I4 |  |  |  | FE | FE | FE | FE | FE | FE |  |  |  | 
i1: load r2, #0(r1)
i2: add r4, r2, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 0
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | -
r5 | #15
r6 | #-7
r7 | #345
Scoreboard
Register File
tag (wakeup)
data
i1
r2,@44
miss
r2
r4,r2,#1

## Slide 35: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
i5
i4
i3
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
i1 | FE | DE | RR | EX@ | EXD$ | …miss… |  |  |  | WB |  |  | 
i2 |  | FE | DE | RR | RR | RR | RR | RR | RR | EX |  |  | 
i3 |  |  | FE | DE | DE | DE | DE | DE | DE | RR |  |  | 
I4 |  |  |  | FE | FE | FE | FE | FE | FE | DE |  |  | 
i2
i1: load r2, #0(r1)
i2: add r4, r2, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
 | rdy
r0 | 1
r1 | 1
r2 | 1
r3 | 1
r4 | 0
r5 | 1
r6 | 0
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | #666
r3 | #33
r4 | -
r5 | #15
r6 | -
r7 | #345
Scoreboard
Register File
tag (wakeup)
data
i1
r2,#666
r2,#666
r4,#666,#1
r4
r6,#15,#2

## Slide 36: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
i6
i5
i4
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
i1 | FE | DE | RR | EX@ | EXD$ | …miss… |  |  |  | WB |  |  | 
i2 |  | FE | DE | RR | RR | RR | RR | RR | RR | EX | WB |  | 
i3 |  |  | FE | DE | DE | DE | DE | DE | DE | RR | EX |  | 
I4 |  |  |  | FE | FE | FE | FE | FE | FE | DE | RR |  | 
i3
i1: load r2, #0(r1)
i2: add r4, r2, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
 | rdy
r0 | 1
r1 | 1
r2 | 1
r3 | 1
r4 | 1
r5 | 1
r6 | 0
r7 | 0
 | value
r0 | #10
r1 | #44
r2 | #666
r3 | #33
r4 | #667
r5 | #15
r6 | -
r7 | -
Scoreboard
Register File
tag (wakeup)
data
r6,#15,#2
i2
r4,#667
r4,#667
r6
r7,r6,#3

## Slide 37: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
i7
i6
i5
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
i1 | FE | DE | RR | EX@ | EXD$ | …miss… |  |  |  | WB |  |  | 
i2 |  | FE | DE | RR | RR | RR | RR | RR | RR | EX | WB |  | 
i3 |  |  | FE | DE | DE | DE | DE | DE | DE | RR | EX | WB | 
I4 |  |  |  | FE | FE | FE | FE | FE | FE | DE | RR | EX | 
i4
i1: load r2, #0(r1)
i2: add r4, r2, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
 | rdy
r0 | 1
r1 | 1
r2 | 1
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 0
 | value
r0 | #10
r1 | #44
r2 | #666
r3 | #33
r4 | #667
r5 | #15
r6 | #17
r7 | -
Scoreboard
Register File
tag (wakeup)
data
i3
r6,#17
r6,#17
r7,#17,#3
r7

## Slide 38: In-order Scalar Pipeline
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
i1 | FE | DE | RR | EX@ | EXD$ | …miss… |  |  |  | WB |  |  | 
i2 |  | FE | DE | RR | RR | RR | RR | RR | RR | EX | WB |  | 
i3 |  |  | FE | DE | DE | DE | DE | DE | DE | RR | EX | WB | 
I4 |  |  |  | FE | FE | FE | FE | FE | FE | DE | RR | EX | WB
i1: load r2, #0(r1)
i2: add r4, r2, #1
i3: add r6, r5, #2
i4: add r7, r6, #3
 | rdy
r0 | 1
r1 | 1
r2 | 1
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | #666
r3 | #33
r4 | #667
r5 | #15
r6 | #17
r7 | #20
Scoreboard
Register File
tag (wakeup)
data
i4
r7,#20
r7,#20
i8
i7
i6
i5

## Slide 39: Begin aside: WAW hazard example

## Slide 40: Aside: WAW hazard example (1)
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
iY
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
iX | FE | DE | RR | EX@ |  |  |  |  |  |  |  |  | 
iY |  | FE | DE | RR |  |  |  |  |  |  |  |  | 
 |  |  | FE | DE |  |  |  |  |  |  |  |  | 
 |  |  |  | FE |  |  |  |  |  |  |  |  | 
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
Scoreboard
Register File
tag (wakeup)
data
r2,#33,#1
iX: load r2, #0(r1)
iY: add r2, r3, #1
Already 0:
- pending producer in EX
- stall on WAW hazard
iX
r2,#0,#44

## Slide 41: Aside: WAW hazard example (2)
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
iY
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
iX | FE | DE | RR | EX@ | EXD$ | …miss… |  |  |  |  |  |  | 
iY |  | FE | DE | RR | RR | RR | RR | RR | RR |  |  |  | 
 |  |  | FE | DE | DE | DE | DE | DE | DE |  |  |  | 
 |  |  |  | FE | FE | FE | FE | FE | FE |  |  |  | 
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
Scoreboard
Register File
tag (wakeup)
data
iX
r2,@44
miss
r2
r2,#33,#1
iX: load r2, #0(r1)
iY: add r2, r3, #1

## Slide 42: Aside: WAW hazard example (3)
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
iX | FE | DE | RR | EX@ | EXD$ | …miss… |  |  |  | WB |  |  | 
iY |  | FE | DE | RR | RR | RR | RR | RR | RR | EX |  |  | 
 |  |  | FE | DE | DE | DE | DE | DE | DE | RR |  |  | 
 |  |  |  | FE | FE | FE | FE | FE | FE | DE |  |  | 
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | (#666)
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
Scoreboard
Register File
tag (wakeup)
data
r2
iX: load r2, #0(r1)
iY: add r2, r3, #1
iY
iX
r2,#666
r2,#666
r2,#33,#1
Keep 0, for iY

## Slide 43: Aside: WAW hazard example (4)
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
iX | FE | DE | RR | EX@ | EXD$ | …miss… |  |  |  | WB |  |  | 
iY |  | FE | DE | RR | RR | RR | RR | RR | RR | EX | WB |  | 
 |  |  | FE | DE | DE | DE | DE | DE | DE | RR | EX |  | 
 |  |  |  | FE | FE | FE | FE | FE | FE | DE | RR |  | 
 | rdy
r0 | 1
r1 | 1
r2 | 1
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | #34
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
Scoreboard
Register File
tag (wakeup)
data
iX: load r2, #0(r1)
iY: add r2, r3, #1
iY
r2,#34
r2,#34

## Slide 44: End aside: WAW hazard example

## Slide 45: In-order Issue Bottleneck
i2 must wait for i1
  i2 depends on i1
i3, i4 need not wait for i1, i2
  Independent
Yet i3, i4 also stall
  In-order issue translates to a structural hazard
  RR stage (issue stage) blocked by the stalled i2
OOO pipeline unblocks RR (issue) using a new instruction buffer for stalled data-dependent instructions
  Many names in the literature
  “reservation stations”, “issue buffer”, “issue queue”, “scheduler”, “scheduling window”

## Slide 46: Issue Queue
Stalled instructions do not impede instruction fetch
Younger ready instructions issue and execute out-of-order with respect to older non-ready instructions
Issue Queue opens up the pipeline to future independent instructions, to:
  Tolerate long latencies (cache misses, floating-point)
  Exploit instruction-level parallelism (ILP) (critical for superscalar)

## Slide 47: Out-of-Order Scalar Pipeline (vers. 1)
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
Insert instructions in-order
Remove instructions out-of-order
Issue Queue (IQ)
In-order fetch/dispatch engine
Out-of-order issue/execute engine

## Slide 48
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | rdy
r0 | 
r1 | 
r2 | 
r3 | 
r4 | 
r5 | 
r6 | 
r7 | 
 | value
r0 | 
r1 | 
r2 | 
r3 | 
r4 | 
r5 | 
r6 | 
r7 | 
Scoreboard
Issue Queue
Register File
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
tag (wakeup)
data

## Slide 49
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
i1: load r2, #0(r1) | FE |  |  |  |  |  |  |  |  |  |  |  |  |  | 
i2: add r4, r2, #1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
i3: add r6, r5, #2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
i4: add r7, r6, #3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | rdy
r0 | 1
r1 | 1
r2 | 1
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
Scoreboard
Issue Queue
Register File
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 |  |  |  |  | 
0 |  |  |  |  | 
0 |  |  |  |  | 
i1
tag (wakeup)
data

## Slide 50
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
i1: load r2, #0(r1) | FE | DE |  |  |  |  |  |  |  |  |  |  |  |  | 
i2: add r4, r2, #1 |  | FE |  |  |  |  |  |  |  |  |  |  |  |  | 
i3: add r6, r5, #2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
i4: add r7, r6, #3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | rdy
r0 | 1
r1 | 1
r2 | 1
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
Scoreboard
Issue Queue
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 |  |  |  |  | 
0 |  |  |  |  | 
0 |  |  |  |  | 
i2
tag (wakeup)
data
i1
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
Register File

## Slide 51
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
i1: load r2, #0(r1) | FE | DE | RR |  |  |  |  |  |  |  |  |  |  |  | 
i2: add r4, r2, #1 |  | FE | DE |  |  |  |  |  |  |  |  |  |  |  | 
i3: add r6, r5, #2 |  |  | FE |  |  |  |  |  |  |  |  |  |  |  | 
i4: add r7, r6, #3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
Scoreboard
Issue Queue
Register File
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 |  |  |  |  | 
0 |  |  |  |  | 
0 |  |  |  |  | 
i3
tag (wakeup)
data
i1
r2,#0,#44
i2

## Slide 52
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
i1: load r2, #0(r1) | FE | DE | RR | DI |  |  |  |  |  |  |  |  |  |  | 
i2: add r4, r2, #1 |  | FE | DE | RR |  |  |  |  |  |  |  |  |  |  | 
i3: add r6, r5, #2 |  |  | FE | DE |  |  |  |  |  |  |  |  |  |  | 
i4: add r7, r6, #3 |  |  |  | FE |  |  |  |  |  |  |  |  |  |  | 
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 0
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | -
r5 | #15
r6 | #-7
r7 | #345
Scoreboard
Issue Queue
Register File
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 |  |  |  |  | 
0 |  |  |  |  | 
0 |  |  |  |  | 
i4
tag (wakeup)
data
i2
r4,r2,#1
i1
r2,#0,#44
i3

## Slide 53
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
i1: load r2, #0(r1) | FE | DE | RR | DI | IS |  |  |  |  |  |  |  |  |  | 
i2: add r4, r2, #1 |  | FE | DE | RR | DI |  |  |  |  |  |  |  |  |  | 
i3: add r6, r5, #2 |  |  | FE | DE | RR |  |  |  |  |  |  |  |  |  | 
i4: add r7, r6, #3 |  |  |  | FE | DE |  |  |  |  |  |  |  |  |  | 
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 0
r5 | 1
r6 | 0
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | -
r5 | #15
r6 | -
r7 | #345
Scoreboard
Issue Queue
Register File
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
1 | r2 | 1 | #0 | 1 | #44
0 |  |  |  |  | 
0 |  |  |  |  | 
i1
tag (wakeup)
data
i1
i3
r6,#15,#2
i2
r4,r2,#1
i4

## Slide 54
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
i1: load r2, #0(r1) | FE | DE | RR | DI | IS | EX@ |  |  |  |  |  |  |  |  | 
i2: add r4, r2, #1 |  | FE | DE | RR | DI | IS |  |  |  |  |  |  |  |  | 
i3: add r6, r5, #2 |  |  | FE | DE | RR | DI |  |  |  |  |  |  |  |  | 
i4: add r7, r6, #3 |  |  |  | FE | DE | RR |  |  |  |  |  |  |  |  | 
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 0
r5 | 1
r6 | 0
r7 | 0
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | -
r5 | #15
r6 | -
r7 | -
Scoreboard
Issue Queue
Register File
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | r2 | 1 | #0 | 1 | #44
1 | r4 | 0 | r2 | 1 | #1
0 |  |  |  |  | 
i2
tag (wakeup)
data
i2
i4
r7,r6,#3
i3
r6,#15,#2
i1
r2,#0,#44

## Slide 55
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
i1: load r2, #0(r1) | FE | DE | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  |  |  |  | 
i2: add r4, r2, #1 |  | FE | DE | RR | DI | IS | IS |  |  |  |  |  |  |  | 
i3: add r6, r5, #2 |  |  | FE | DE | RR | DI | IS |  |  |  |  |  |  |  | 
i4: add r7, r6, #3 |  |  |  | FE | DE | RR | DI |  |  |  |  |  |  |  | 
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 0
r5 | 1
r6 | 0
r7 | 0
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | -
r5 | #15
r6 | -
r7 | -
Scoreboard
Issue Queue
Register File
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | r2 | 1 | #0 | 1 | #44
1 | r4 | 0 | r2 | 1 | #1
1 | r6 | 1 | #15 | 1 | #2
i2
i1
r2,@44
miss
tag (wakeup)
data
i2
i4
r7,r6,#3
i3
i3

## Slide 56
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
i1: load r2, #0(r1) | FE | DE | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  |  |  |  | 
i2: add r4, r2, #1 |  | FE | DE | RR | DI | IS | IS | IS |  |  |  |  |  |  | 
i3: add r6, r5, #2 |  |  | FE | DE | RR | DI | IS | EX |  |  |  |  |  |  | 
i4: add r7, r6, #3 |  |  |  | FE | DE | RR | DI | IS |  |  |  |  |  |  | 
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 0
r5 | 1
r6 | 0
r7 | 0
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | -
r5 | #15
r6 | -
r7 | -
Scoreboard
Issue Queue
Register File
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
1 | r7 | 0>1 | r6 | 1 | #3
1 | r4 | 0 | r2 | 1 | #1
0 | r6 | 1 | #15 | 1 | #2
i2
tag (wakeup)
data
r6
i4
i3
r6,#15,#2
i2
i4
i1
r2,@44
miss

## Slide 57
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
i1: load r2, #0(r1) | FE | DE | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  |  |  |  | 
i2: add r4, r2, #1 |  | FE | DE | RR | DI | IS | IS | IS | IS |  |  |  |  |  | 
i3: add r6, r5, #2 |  |  | FE | DE | RR | DI | IS | EX | WB |  |  |  |  |  | 
i4: add r7, r6, #3 |  |  |  | FE | DE | RR | DI | IS | EX |  |  |  |  |  | 
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 0
r5 | 1
r6 | 1
r7 | 0
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | -
r5 | #15
r6 | #17
r7 | -
Scoreboard
Issue Queue
Register File
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | r7 | 1 | #17 | 1 | #3
1 | r4 | 0 | r2 | 1 | #1
0 | r6 | 1 | #15 | 1 | #2
i2
i4
i3
r6,#17
r7,#17,#3
tag (wakeup)
data
r6,#17
r7
i2
i1
r2,@44
miss

## Slide 58
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
i1: load r2, #0(r1) | FE | DE | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  |  |  |  | 
i2: add r4, r2, #1 |  | FE | DE | RR | DI | IS | IS | IS | IS | IS |  |  |  |  | 
i3: add r6, r5, #2 |  |  | FE | DE | RR | DI | IS | EX | WB |  |  |  |  |  | 
i4: add r7, r6, #3 |  |  |  | FE | DE | RR | DI | IS | EX | WB |  |  |  |  | 
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 0
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | -
r5 | #15
r6 | #17
r7 | #20
Scoreboard
Issue Queue
Register File
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | r7 | 1 | #17 | 1 | #3
1 | r4 | 0 | r2 | 1 | #1
0 | r6 | 1 | #15 | 1 | #2
i2
i4
r7,#20
tag (wakeup)
data
r7,#20
i2
i1
r2,@44
miss

## Slide 59
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
i1: load r2, #0(r1) | FE | DE | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  |  |  |  | 
i2: add r4, r2, #1 |  | FE | DE | RR | DI | IS | IS | IS | IS | IS | IS |  |  |  | 
i3: add r6, r5, #2 |  |  | FE | DE | RR | DI | IS | EX | WB |  |  |  |  |  | 
i4: add r7, r6, #3 |  |  |  | FE | DE | RR | DI | IS | EX | WB |  |  |  |  | 
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 0
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | -
r5 | #15
r6 | #17
r7 | #20
Scoreboard
Issue Queue
Register File
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | r7 | 1 | #17 | 1 | #3
1 | r4 | 0>1 | r2 | 1 | #1
0 | r6 | 1 | #15 | 1 | #2
i2
tag (wakeup)
data
i2
r2
i1
r2,@44
miss

## Slide 60
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
i1: load r2, #0(r1) | FE | DE | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  | WB |  |  | 
i2: add r4, r2, #1 |  | FE | DE | RR | DI | IS | IS | IS | IS | IS | IS | EX |  |  | 
i3: add r6, r5, #2 |  |  | FE | DE | RR | DI | IS | EX | WB |  |  |  |  |  | 
i4: add r7, r6, #3 |  |  |  | FE | DE | RR | DI | IS | EX | WB |  |  |  |  | 
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | rdy
r0 | 1
r1 | 1
r2 | 1
r3 | 1
r4 | 0
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | #666
r3 | #33
r4 | -
r5 | #15
r6 | #17
r7 | #20
Scoreboard
Issue Queue
Register File
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | r7 | 1 | #17 | 1 | #3
0 | r4 | 1 | #666 | 1 | #1
0 | r6 | 1 | #15 | 1 | #2
tag (wakeup)
data
r2,#666
r2,#666
i1
i2
r4,#666,#1
r4

## Slide 61
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
i1: load r2, #0(r1) | FE | DE | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  | WB |  |  | 
i2: add r4, r2, #1 |  | FE | DE | RR | DI | IS | IS | IS | IS | IS | IS | EX | WB |  | 
i3: add r6, r5, #2 |  |  | FE | DE | RR | DI | IS | EX | WB |  |  |  |  |  | 
i4: add r7, r6, #3 |  |  |  | FE | DE | RR | DI | IS | EX | WB |  |  |  |  | 
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | rdy
r0 | 1
r1 | 1
r2 | 1
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | #666
r3 | #33
r4 | #667
r5 | #15
r6 | #17
r7 | #20
Scoreboard
Issue Queue
Register File
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | r7 | 1 | #17 | 1 | #3
0 | r4 | 1 | #666 | 1 | #1
0 | r6 | 1 | #15 | 1 | #2
tag (wakeup)
data
r4,#667
r4,#667
i2

## Slide 62
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
i1: load r2, #0(r1) | FE | DE | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  | WB |  |  | 
i2: add r4, r2, #1 |  | FE | DE | RR | DI | IS | IS | IS | IS | IS | IS | EX | WB |  | 
i3: add r6, r5, #2 |  |  | FE | DE | RR | DI | IS | EX | WB |  |  |  |  |  | 
i4: add r7, r6, #3 |  |  |  | FE | DE | RR | DI | IS | EX | WB |  |  |  |  | 
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | rdy
r0 | 1
r1 | 1
r2 | 1
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | #666
r3 | #33
r4 | #667
r5 | #15
r6 | #17
r7 | #20
Scoreboard
Issue Queue
Register File
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | r7 | 1 | #17 | 1 | #3
0 | r4 | 1 | #666 | 1 | #1
0 | r6 | 1 | #15 | 1 | #2
tag (wakeup)
data

## Slide 63: Two Problems with Vers. 1
Can’t recover from misspeculation
  Younger instructions are speculative with respect to older instructions
    There may be older predicted branches that haven’t executed yet
    Older instructions may raise exceptions, e.g., page faults
    Older load instructions may have executed speculatively with respect to prior unresolved stores (more later)
  No way to undo the effects of younger instructions if an older mispredicted branch, mispredicted load, or exception is detected late

## Slide 64
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
i1: load r2, #0(r1) | FE | DE | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  | WB |  |  | 
i2: bnez r2, i7 |  | FE | DE | RR | DI | IS | IS | IS | IS | IS | IS | EX |  |  | 
i3: add r6, r5, #2 |  |  | FE | DE | RR | DI | IS | EX | WB |  |  |  |  |  | 
i4: add r7, r6, #3 |  |  |  | FE | DE | RR | DI | IS | EX | WB |  |  |  |  | 
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | rdy
r0 | 1
r1 | 1
r2 | 1
r3 | 1
r4 | 1
r5 | 1
r6 | 1
r7 | 1
 | value
r0 | #10
r1 | #44
r2 | #666
r3 | #33
r4 | #7
r5 | #15
r6 | #17
r7 | #20
Scoreboard
Issue Queue
Register File
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | r7 | 1 | #17 | 1 | #3
0 | - | 1 | #666 | 1 | #0
0 | r6 | 1 | #15 | 1 | #2
tag (wakeup)
data
r2,#666
r2,#666
i1
i2
#666 != #0 branch to i7
mispredict
Can’t squash i3, i4: they are “long gone”
Misprediction detected!
Can’t recover original values of r6, r7.

## Slide 65: Two Problems with Vers. 1
Reverts to in-order when two producers have the same destination register (WAR and WAW hazards)
  Must stall younger producer in Register Read stage until older producer executes
  Let’s see what happens if we don’t…

## Slide 66
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
i1: load r2, #0(r1) | FE | DE | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  |  |  |  | 
i2: add r4, r2, #1 |  | FE | DE | RR | DI | IS | IS | IS |  |  |  |  |  |  | 
i3: add r2, r5, #2 |  |  | FE | DE | RR | DI | IS | EX |  |  |  |  |  |  | 
i4: add r7, r2, #3 |  |  |  | FE | DE | RR | DI | IS |  |  |  |  |  |  | 
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | rdy
r0 | 1
r1 | 1
r2 | 0
r3 | 1
r4 | 0
r5 | 1
r6 | 1
r7 | 0
 | value
r0 | #10
r1 | #44
r2 | -
r3 | #33
r4 | -
r5 | #15
r6 | #-7
r7 | -
Scoreboard
Issue Queue
Register File
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
1 | r7 | 0>1 | r2 | 1 | #3
1 | r4 | 0>1 | r2 | 1 | #1
0 | r2 | 1 | #15 | 1 | #2
i2
tag (wakeup)
data
r2
i4
i3
r2,#15,#2
Incorrect handling of WAW: i1 will overwrite i3, later.
What happens if we do not stall i3 in RR until i1 executes?
i1
r2,@44
miss
i2
i4
Correct wakeup: RAW
Incorrect wakeup: WAR

## Slide 67: Solution: Reorder Buffer (ROB)
The ROB allows for OOO execution, while at the same time supporting recovery from mispredictions and exceptions
The ROB implements Register Renaming
  Rename non-unique destination tags (architectural register specifiers) to unique destination tags (ROB tags)
  Source tags renamed as well, unambiguously linking consumers to their producers
  No in-order stall point due to WAR and WAW hazards, as they are eliminated post-renaming

## Slide 68: Operation with ROB
The “Register File” is replaced with an expanded set of registers split into two parts
  Architectural Register File (ARF): Contains values of architectural registers as if produced by an in-order pipeline. That is, contains committed (non-speculative) versions of architectural registers to which the pipeline may safely revert to if there is a misprediction or exception.
  Reorder Buffer (ROB): Contains speculative versions of architectural registers. There may be multiple speculative versions for a given architectural register.
ROB is a circular FIFO with head and tail pointers
  A list of oldest to youngest instructions in program order
  Instruction at ROB Head is oldest instruction
  Instruction at ROB Tail is youngest instruction
New Rename Stage (after Decode and before Register Read)
  The new instruction is allocated to the ROB entry pointed to by ROB Tail. This is also its unique “ROB tag”.
  Source register specifiers are renamed to the expanded set of registers, the ARF+ROB. Renaming pinpoints the location of the value: ARF or ROB, and where in the ROB (ROB tag of producer). Thus, renaming unambiguously links consumers to their producers.
  Destination register specifier is renamed to the instruction’s unique ROB tag.
  Rename Map Table (RMT) contains the bookkeeping for renaming. (Intel calls it the Register Alias Table (RAT).)
Register Read Stage
  Obtain source value from ARF or ROB (using renamed source)
  If renamed to ROB, ROB may indicate value not ready yet
    Producer hasn’t executed yet
    Keep renamed source as proxy for value
  A consumer instruction obtains its source values from ARF, ROB, and/or bypass, depending on situation:
    ARF: if producer of value has retired from ROB
    ROB: if producer of value has executed but not yet retired from ROB
    Bypass: if producer of value has not yet executed
Writeback Stage
  Instruction writes its speculative result OOO into ROB instead of ARF (at its ROB entry)
New Retire Stage safely commits results from ROB to ARF in program order
Misprediction/exception recovery
  Offending instruction posts misprediction or exception bit in its ROB entry OOO
  Wait until offending instruction reaches head of ROB (oldest unretired instruction)
  Squash all instructions in pipeline and ROB, and restore RMT to be consistent with an empty pipeline

## Slide 69
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | v | ROB tag
r0 |  | 
r1 |  | 
r2 |  | 
r3 |  | 
r4 |  | 
r5 |  | 
r6 |  | 
r7 |  | 
 | value
r0 | 
r1 | 
r2 | 
r3 | 
r4 | 
r5 | 
r6 | 
r7 | 
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 |  |  |  |  |  |  | 
rob4 |  |  |  |  |  |  | 
rob5 |  |  |  |  |  |  | 
rob6 |  |  |  |  |  |  | 
rob7 |  |  |  |  |  |  | 
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
tag (wakeup)
data
Rename
Retire
H
T

## Slide 70
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 0 | -
r3 | 0 | -
r4 | 0 | -
r5 | 0 | -
r6 | 0 | -
r7 | 0 | -
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 |  |  |  |  |  |  | 
rob4 |  |  |  |  |  |  | 
rob5 |  |  |  |  |  |  | 
rob6 |  |  |  |  |  |  | 
rob7 |  |  |  |  |  |  | 
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 |  |  |  |  | 
0 |  |  |  |  | 
0 |  |  |  |  | 
tag (wakeup)
data
Rename
Retire
H
T
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
i2: bnez r2, i7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
i3: add r2, r5, #2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
i4: add r7, r2, #3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
i1

## Slide 71
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 0 | -
r3 | 0 | -
r4 | 0 | -
r5 | 0 | -
r6 | 0 | -
r7 | 0 | -
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 |  |  |  |  |  |  | 
rob4 |  |  |  |  |  |  | 
rob5 |  |  |  |  |  |  | 
rob6 |  |  |  |  |  |  | 
rob7 |  |  |  |  |  |  | 
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 |  |  |  |  | 
0 |  |  |  |  | 
0 |  |  |  |  | 
tag (wakeup)
data
Rename
Retire
H
T
i2
i1
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
i2: bnez r2, i7 |  | FE |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
i3: add r2, r5, #2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
i4: add r7, r2, #3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 72
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 1 | rob3
r3 | 0 | -
r4 | 0 | -
r5 | 0 | -
r6 | 0 | -
r7 | 0 | -
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | - |  | r2 | 0 | 0 | 0 | i1
rob4 |  |  |  |  |  |  | 
rob5 |  |  |  |  |  |  | 
rob6 |  |  |  |  |  |  | 
rob7 |  |  |  |  |  |  | 
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 |  |  |  |  | 
0 |  |  |  |  | 
0 |  |  |  |  | 
tag (wakeup)
data
Rename
Retire
H
T
i3
i2
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN |  |  |  |  |  |  |  |  |  |  |  |  |  | 
i2: bnez r2, i7 |  | FE | DE |  |  |  |  |  |  |  |  |  |  |  |  |  | 
i3: add r2, r5, #2 |  |  | FE |  |  |  |  |  |  |  |  |  |  |  |  |  | 
i4: add r7, r2, #3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
i1
rob3,#0,r1

## Slide 73
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 1 | rob3
r3 | 0 | -
r4 | 0 | -
r5 | 0 | -
r6 | 0 | -
r7 | 0 | -
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | - |  | r2 | 0 | 0 | 0 | i1
rob4 | - |  | - | 0 | 0 | 0 | i2
rob5 |  |  |  |  |  |  | 
rob6 |  |  |  |  |  |  | 
rob7 |  |  |  |  |  |  | 
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 |  |  |  |  | 
0 |  |  |  |  | 
0 |  |  |  |  | 
tag (wakeup)
data
Rename
Retire
H
T
i4
i3
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN | RR |  |  |  |  |  |  |  |  |  |  |  |  | 
i2: bnez r2, i7 |  | FE | DE | RN |  |  |  |  |  |  |  |  |  |  |  |  | 
i3: add r2, r5, #2 |  |  | FE | DE |  |  |  |  |  |  |  |  |  |  |  |  | 
i4: add r7, r2, #3 |  |  |  | FE |  |  |  |  |  |  |  |  |  |  |  |  | 
i2
rob4,rob3,#0
i1
rob3,#0,#44

## Slide 74
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 1 | rob5
r3 | 0 | -
r4 | 0 | -
r5 | 0 | -
r6 | 0 | -
r7 | 0 | -
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | - |  | r2 | 0 | 0 | 0 | i1
rob4 | - |  | - | 0 | 0 | 0 | i2
rob5 | - |  | r2 | 0 | 0 | 0 | i3
rob6 |  |  |  |  |  |  | 
rob7 |  |  |  |  |  |  | 
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 |  |  |  |  | 
0 |  |  |  |  | 
0 |  |  |  |  | 
tag (wakeup)
data
Rename
Retire
H
T
i4
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN | RR | DI |  |  |  |  |  |  |  |  |  |  |  | 
i2: bnez r2, i7 |  | FE | DE | RN | RR |  |  |  |  |  |  |  |  |  |  |  | 
i3: add r2, r5, #2 |  |  | FE | DE | RN |  |  |  |  |  |  |  |  |  |  |  | 
i4: add r7, r2, #3 |  |  |  | FE | DE |  |  |  |  |  |  |  |  |  |  |  | 
i3
rob5,r5,#2
i2
rob4,rob3,#0
i1
rob3,#0,#44

## Slide 75
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 1 | rob5
r3 | 0 | -
r4 | 0 | -
r5 | 0 | -
r6 | 0 | -
r7 | 1 | rob6
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | - |  | r2 | 0 | 0 | 0 | i1
rob4 | - |  | - | 0 | 0 | 0 | i2
rob5 | - |  | r2 | 0 | 0 | 0 | i3
rob6 | - |  | r7 | 0 | 0 | 0 | i4
rob7 |  |  |  |  |  |  | 
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
1 | rob3 | 1 | #0 | 1 | #44
0 |  |  |  |  | 
0 |  |  |  |  | 
tag (wakeup)
data
Rename
Retire
H
T
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN | RR | DI | IS |  |  |  |  |  |  |  |  |  |  | 
i2: bnez r2, i7 |  | FE | DE | RN | RR | DI |  |  |  |  |  |  |  |  |  |  | 
i3: add r2, r5, #2 |  |  | FE | DE | RN | RR |  |  |  |  |  |  |  |  |  |  | 
i4: add r7, r2, #3 |  |  |  | FE | DE | RN |  |  |  |  |  |  |  |  |  |  | 
i4
rob6,rob5,#3
i3
rob5,#15,#2
i2
rob4,rob3,#0
i1
i1

## Slide 76
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 1 | rob5
r3 | 0 | -
r4 | 0 | -
r5 | 0 | -
r6 | 0 | -
r7 | 1 | rob6
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | - |  | r2 | 0 | 0 | 0 | i1
rob4 | - |  | - | 0 | 0 | 0 | i2
rob5 | - |  | r2 | 0 | 0 | 0 | i3
rob6 | - |  | r7 | 0 | 0 | 0 | i4
rob7 |  |  |  |  |  |  | 
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | rob3 | 1 | #0 | 1 | #44
1 | rob4 | 0 | rob3 | 1 | #0
0 |  |  |  |  | 
tag (wakeup)
data
Rename
Retire
H
T
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN | RR | DI | IS | EX@ |  |  |  |  |  |  |  |  |  | 
i2: bnez r2, i7 |  | FE | DE | RN | RR | DI | IS |  |  |  |  |  |  |  |  |  | 
i3: add r2, r5, #2 |  |  | FE | DE | RN | RR | DI |  |  |  |  |  |  |  |  |  | 
i4: add r7, r2, #3 |  |  |  | FE | DE | RN | RR |  |  |  |  |  |  |  |  |  | 
i4
rob6,rob5,#3
i3
rob5,#15,#2
i2
i2
i1
rob3,#0,#44

## Slide 77
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 1 | rob5
r3 | 0 | -
r4 | 0 | -
r5 | 0 | -
r6 | 0 | -
r7 | 1 | rob6
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | - |  | r2 | 0 | 0 | 0 | i1
rob4 | - |  | - | 0 | 0 | 0 | i2
rob5 | - |  | r2 | 0 | 0 | 0 | i3
rob6 | - |  | r7 | 0 | 0 | 0 | i4
rob7 |  |  |  |  |  |  | 
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | rob3 | 1 | #0 | 1 | #44
1 | rob4 | 0 | rob3 | 1 | #0
1 | rob5 | 1 | #15 | 1 | #2
tag (wakeup)
data
Rename
Retire
H
T
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  |  |  |  |  | 
i2: bnez r2, i7 |  | FE | DE | RN | RR | DI | IS | IS |  |  |  |  |  |  |  |  | 
i3: add r2, r5, #2 |  |  | FE | DE | RN | RR | DI | IS |  |  |  |  |  |  |  |  | 
i4: add r7, r2, #3 |  |  |  | FE | DE | RN | RR | DI |  |  |  |  |  |  |  |  | 
i4
rob6,rob5,#3
i2
i2
i1
rob3,@44
miss
i3
i3

## Slide 78
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 1 | rob5
r3 | 0 | -
r4 | 0 | -
r5 | 0 | -
r6 | 0 | -
r7 | 1 | rob6
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | - |  | r2 | 0 | 0 | 0 | i1
rob4 | - |  | - | 0 | 0 | 0 | i2
rob5 | - |  | r2 | 0 | 0 | 0 | i3
rob6 | - |  | r7 | 0 | 0 | 0 | i4
rob7 |  |  |  |  |  |  | 
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
1 | rob6 | 0>1 | rob5 | 1 | #3
1 | rob4 | 0 | rob3 | 1 | #0
0 | rob5 | 1 | #15 | 1 | #2
tag (wakeup)
data
Rename
Retire
H
T
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  |  |  |  |  | 
i2: bnez r2, i7 |  | FE | DE | RN | RR | DI | IS | IS | IS |  |  |  |  |  |  |  | 
i3: add r2, r5, #2 |  |  | FE | DE | RN | RR | DI | IS | EX |  |  |  |  |  |  |  | 
i4: add r7, r2, #3 |  |  |  | FE | DE | RN | RR | DI | IS |  |  |  |  |  |  |  | 
i2
i2
i1
rob3,@44
miss
i4
rob5
i3
rob5,#15,#2
i4
i5
add r4,r2,r7

## Slide 79
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 1 | rob5
r3 | 0 | -
r4 | 0 | -
r5 | 0 | -
r6 | 0 | -
r7 | 1 | rob6
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | - |  | r2 | 0 | 0 | 0 | i1
rob4 | - |  | - | 0 | 0 | 0 | i2
rob5 | #17 |  | r2 | 1 | 0 | 0 | i3
rob6 | - |  | r7 | 0 | 0 | 0 | i4
rob7 |  |  |  |  |  |  | 
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | rob6 | 1 | #17 | 1 | #3
1 | rob4 | 0 | rob3 | 1 | #0
0 | rob5 | 1 | #15 | 1 | #2
tag (wakeup)
data
Rename
Retire
H
T
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  |  |  |  |  | 
i2: bnez r2, i7 |  | FE | DE | RN | RR | DI | IS | IS | IS | IS |  |  |  |  |  |  | 
i3: add r2, r5, #2 |  |  | FE | DE | RN | RR | DI | IS | EX | WB |  |  |  |  |  |  | 
i4: add r7, r2, #3 |  |  |  | FE | DE | RN | RR | DI | IS | EX |  |  |  |  |  |  | 
i2
i2
i1
rob3,@44
miss
i3
rob5,#17
rob6,#17,#3
rob5,#17
rob6
i4
i5
add r4,r2,r7

## Slide 80
rob7,rob5,rob6
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 1 | rob5
r3 | 0 | -
r4 | 1 | rob7
r5 | 0 | -
r6 | 0 | -
r7 | 1 | rob6
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | - |  | r2 | 0 | 0 | 0 | i1
rob4 | - |  | - | 0 | 0 | 0 | i2
rob5 | #17 |  | r2 | 1 | 0 | 0 | i3
rob6 | #20 |  | r7 | 1 | 0 | 0 | i4
rob7 | - |  | r4 | 0 | 0 | 0 | i5
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | rob6 | 1 | #17 | 1 | #3
1 | rob4 | 0 | rob3 | 1 | #0
0 | rob5 | 1 | #15 | 1 | #2
tag (wakeup)
data
Rename
Retire
H
T
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  |  |  |  |  | 
i2: bnez r2, i7 |  | FE | DE | RN | RR | DI | IS | IS | IS | IS | IS |  |  |  |  |  | 
i3: add r2, r5, #2 |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT |  |  |  |  |  | 
i4: add r7, r2, #3 |  |  |  | FE | DE | RN | RR | DI | IS | EX | WB |  |  |  |  |  | 
i2
i2
i1
rob3,@44
miss
i4
rob6,#20
rob6,#20
i3
i5

## Slide 81
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 1 | rob5
r3 | 0 | -
r4 | 1 | rob7
r5 | 0 | -
r6 | 0 | -
r7 | 1 | rob6
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | - |  | r2 | 0 | 0 | 0 | i1
rob4 | - |  | - | 0 | 0 | 0 | i2
rob5 | #17 |  | r2 | 1 | 0 | 0 | i3
rob6 | #20 |  | r7 | 1 | 0 | 0 | i4
rob7 | - |  | r4 | 0 | 0 | 0 | i5
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | rob6 | 1 | #17 | 1 | #3
1 | rob4 | 0>1 | rob3 | 1 | #0
0 | rob5 | 1 | #15 | 1 | #2
tag (wakeup)
data
Rename
Retire
H
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  |  |  |  |  | 
i2: bnez r2, i7 |  | FE | DE | RN | RR | DI | IS | IS | IS | IS | IS | IS |  |  |  |  | 
i3: add r2, r5, #2 |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT |  |  |  |  | 
i4: add r7, r2, #3 |  |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT |  |  |  |  | 
i2
i2
i1
rob3,@44
miss
i4
i3
rob3
rob7,#17,#20
i5
T

## Slide 82
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 1 | rob5
r3 | 0 | -
r4 | 1 | rob7
r5 | 0 | -
r6 | 0 | -
r7 | 1 | rob6
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | #0 |  | r2 | 1 | 0 | 0 | i1
rob4 | - |  | - | 0 | 0 | 0 | i2
rob5 | #17 |  | r2 | 1 | 0 | 0 | i3
rob6 | #20 |  | r7 | 1 | 0 | 0 | i4
rob7 | - |  | r4 | 0 | 0 | 0 | i5
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | rob6 | 1 | #17 | 1 | #3
0 | rob4 | 1 | #0 | 1 | #0
0 | rob5 | 1 | #15 | 1 | #2
tag (wakeup)
data
Rename
Retire
H
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  | WB |  |  |  | 
i2: bnez r2, i7 |  | FE | DE | RN | RR | DI | IS | IS | IS | IS | IS | IS | EX |  |  |  | 
i3: add r2, r5, #2 |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT | RT |  |  |  | 
i4: add r7, r2, #3 |  |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT |  |  |  | 
i4
i3
rob7,#17,#20
i5
T
rob3,#0
rob3,#0
i1
i2
rob4,#0,#0
#0!=#0 is false, not-taken, no misp.

## Slide 83
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 1 | rob5
r3 | 0 | -
r4 | 1 | rob7
r5 | 0 | -
r6 | 0 | -
r7 | 1 | rob6
 | value
r0 | #10
r1 | #44
r2 | #0
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | #0 |  | r2 | 1 | 0 | 0 | i1
rob4 | - |  | - | 1 | 0 | 0 | i2
rob5 | #17 |  | r2 | 1 | 0 | 0 | i3
rob6 | #20 |  | r7 | 1 | 0 | 0 | i4
rob7 | - |  | r4 | 0 | 0 | 0 | i5
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
1 | rob7 | 1 | #17 | 1 | #20
0 | rob4 | 1 | #0 | 1 | #0
0 | rob5 | 1 | #15 | 1 | #2
tag (wakeup)
data
Rename
Retire
H
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  | WB | RT |  |  | 
i2: bnez r2, i7 |  | FE | DE | RN | RR | DI | IS | IS | IS | IS | IS | IS | EX | WB |  |  | 
i3: add r2, r5, #2 |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT | RT | RT |  |  | 
i4: add r7, r2, #3 |  |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT | RT |  |  | 
i4
i3
T
rob4, no misp.
rob4, no misp.
i2
i1
Don’t reset: rob5 != rob3
i5
i5

## Slide 84
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 1 | rob5
r3 | 0 | -
r4 | 1 | rob7
r5 | 0 | -
r6 | 0 | -
r7 | 1 | rob6
 | value
r0 | #10
r1 | #44
r2 | #0
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | #0 |  | r2 | 1 | 0 | 0 | i1
rob4 | - |  | - | 1 | 0 | 0 | i2
rob5 | #17 |  | r2 | 1 | 0 | 0 | i3
rob6 | #20 |  | r7 | 1 | 0 | 0 | i4
rob7 | - |  | r4 | 0 | 0 | 0 | i5
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | rob7 | 1 | #17 | 1 | #20
0 | rob4 | 1 | #0 | 1 | #0
0 | rob5 | 1 | #15 | 1 | #2
tag (wakeup)
data
Rename
Retire
H
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  | WB | RT |  |  | 
i2: bnez r2, i7 |  | FE | DE | RN | RR | DI | IS | IS | IS | IS | IS | IS | EX | WB | RT |  | 
i3: add r2, r5, #2 |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT | RT | RT | RT |  | 
i4: add r7, r2, #3 |  |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT | RT | RT |  | 
i4
i3
T
i2
i5
rob7,#17,#20
rob7

## Slide 85
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 0 | rob5
r3 | 0 | -
r4 | 1 | rob7
r5 | 0 | -
r6 | 0 | -
r7 | 1 | rob6
 | value
r0 | #10
r1 | #44
r2 | #17
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | #0 |  | r2 | 1 | 0 | 0 | i1
rob4 | - |  | - | 1 | 0 | 0 | i2
rob5 | #17 |  | r2 | 1 | 0 | 0 | i3
rob6 | #20 |  | r7 | 1 | 0 | 0 | i4
rob7 | #37 |  | r4 | 1 | 0 | 0 | i5
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | rob7 | 1 | #17 | 1 | #20
0 | rob4 | 1 | #0 | 1 | #0
0 | rob5 | 1 | #15 | 1 | #2
tag (wakeup)
data
Rename
Retire
H
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  | WB | RT |  |  | 
i2: bnez r2, i7 |  | FE | DE | RN | RR | DI | IS | IS | IS | IS | IS | IS | EX | WB | RT |  | 
i3: add r2, r5, #2 |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT | RT | RT | RT | RT | 
i4: add r7, r2, #3 |  |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT | RT | RT | RT | 
i4
i3
T
rob7,#37
rob7,#37
i5
Reset: rob5 == rob5

## Slide 86
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 0 | -
r3 | 0 | -
r4 | 1 | rob7
r5 | 0 | -
r6 | 0 | -
r7 | 0 | rob6
 | value
r0 | #10
r1 | #44
r2 | #17
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #20
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | #0 |  | r2 | 1 | 0 | 0 | i1
rob4 | - |  | - | 1 | 0 | 0 | i2
rob5 | #17 |  | r2 | 1 | 0 | 0 | i3
rob6 | #20 |  | r7 | 1 | 0 | 0 | i4
rob7 | #37 |  | r4 | 1 | 0 | 0 | i5
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | rob7 | 1 | #17 | 1 | #20
0 | rob4 | 1 | #0 | 1 | #0
0 | rob5 | 1 | #15 | 1 | #2
tag (wakeup)
data
Rename
Retire
H
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  | WB | RT |  |  | 
i2: bnez r2, i7 |  | FE | DE | RN | RR | DI | IS | IS | IS | IS | IS | IS | EX | WB | RT |  | 
i3: add r2, r5, #2 |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT | RT | RT | RT | RT | 
i4: add r7, r2, #3 |  |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT | RT | RT | RT | RT
i4
T
i5
Reset: rob6 == rob6

## Slide 87
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 0 | -
r3 | 0 | -
r4 | 0 | rob7
r5 | 0 | -
r6 | 0 | -
r7 | 0 | -
 | value
r0 | #10
r1 | #44
r2 | #17
r3 | #33
r4 | #37
r5 | #15
r6 | #-7
r7 | #20
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | #0 |  | r2 | 1 | 0 | 0 | i1
rob4 | - |  | - | 1 | 0 | 0 | i2
rob5 | #17 |  | r2 | 1 | 0 | 0 | i3
rob6 | #20 |  | r7 | 1 | 0 | 0 | i4
rob7 | #37 |  | r4 | 1 | 0 | 0 | i5
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | rob7 | 1 | #17 | 1 | #20
0 | rob4 | 1 | #0 | 1 | #0
0 | rob5 | 1 | #15 | 1 | #2
tag (wakeup)
data
Rename
Retire
H
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  | WB | RT |  |  | 
i2: bnez r2, i7 |  | FE | DE | RN | RR | DI | IS | IS | IS | IS | IS | IS | EX | WB | RT |  | 
i3: add r2, r5, #2 |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT | RT | RT | RT | RT | 
i4: add r7, r2, #3 |  |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT | RT | RT | RT | RT
T
i5
Reset: rob7 == rob7

## Slide 88
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 0 | -
r3 | 0 | -
r4 | 0 | -
r5 | 0 | -
r6 | 0 | -
r7 | 0 | -
 | value
r0 | #10
r1 | #44
r2 | #17
r3 | #33
r4 | #37
r5 | #15
r6 | #-7
r7 | #20
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | #0 |  | r2 | 1 | 0 | 0 | i1
rob4 | - |  | - | 1 | 0 | 0 | i2
rob5 | #17 |  | r2 | 1 | 0 | 0 | i3
rob6 | #20 |  | r7 | 1 | 0 | 0 | i4
rob7 | #37 |  | r4 | 1 | 0 | 0 | i5
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | rob7 | 1 | #17 | 1 | #20
0 | rob4 | 1 | #0 | 1 | #0
0 | rob5 | 1 | #15 | 1 | #2
tag (wakeup)
data
Rename
Retire
H
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  | WB | RT |  |  | 
i2: bnez r2, i7 |  | FE | DE | RN | RR | DI | IS | IS | IS | IS | IS | IS | EX | WB | RT |  | 
i3: add r2, r5, #2 |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT | RT | RT | RT | RT | 
i4: add r7, r2, #3 |  |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT | RT | RT | RT | RT
T

## Slide 89: Recovery Scenario
Previous scenario
  ROB did not impede OOO performance
    Fetch didn’t stall despite D$ miss (tolerated D$ miss), the same as without ROB.
    Thus, in-order retirement did not impede OOO, speculative execution.
  On the other hand, ROB was not ultimately called upon for recovery
    Hindsight is perfect
    Note: did leverage ROB for register renaming
Revise the scenario: mispredicted branch
  i1 (load instruction) gets the value #666 instead of #0

## Slide 90
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 1 | rob5
r3 | 0 | -
r4 | 1 | rob7
r5 | 0 | -
r6 | 0 | -
r7 | 1 | rob6
 | value
r0 | #10
r1 | #44
r2 | #11
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | #666 |  | r2 | 1 | 0 | 0 | i1
rob4 | - |  | - | 0 | 0 | 0 | i2
rob5 | #17 |  | r2 | 1 | 0 | 0 | i3
rob6 | #20 |  | r7 | 1 | 0 | 0 | i4
rob7 | - |  | r4 | 0 | 0 | 0 | i5
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | rob6 | 1 | #17 | 1 | #3
0 | rob4 | 1 | #666 | 1 | #0
0 | rob5 | 1 | #15 | 1 | #2
tag (wakeup)
data
Rename
Retire
H
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  | WB |  |  |  | 
i2: bnez r2, i7 |  | FE | DE | RN | RR | DI | IS | IS | IS | IS | IS | IS | EX |  |  |  | 
i3: add r2, r5, #2 |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT | RT |  |  |  | 
i4: add r7, r2, #3 |  |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT |  |  |  | 
i4
i3
rob7,#17,#20
i5
T
rob3,#666
rob3,#666
i1
i2
rob4,#666,#0
#666!=#0 is true, taken, misp.!

## Slide 91
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 1 | rob5
r3 | 0 | -
r4 | 1 | rob7
r5 | 0 | -
r6 | 0 | -
r7 | 1 | rob6
 | value
r0 | #10
r1 | #44
r2 | #666
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | #666 |  | r2 | 1 | 0 | 0 | i1
rob4 | - |  | - | 1 | 0 | 1 | i2
rob5 | #17 |  | r2 | 1 | 0 | 0 | i3
rob6 | #20 |  | r7 | 1 | 0 | 0 | i4
rob7 | - |  | r4 | 0 | 0 | 0 | i5
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
1 | rob7 | 1 | #17 | 1 | #20
0 | rob4 | 1 | #666 | 1 | #0
0 | rob5 | 1 | #15 | 1 | #2
tag (wakeup)
data
Rename
Retire
H
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  | WB | RT |  |  | 
i2: bnez r2, i7 |  | FE | DE | RN | RR | DI | IS | IS | IS | IS | IS | IS | EX | WB |  |  | 
i3: add r2, r5, #2 |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT | RT | RT |  |  | 
i4: add r7, r2, #3 |  |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT | RT |  |  | 
i4
i3
T
rob4, misp.
rob4, misp.
i2
i1
Don’t reset: rob5 != rob3
i5
i5

## Slide 92
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  | WB | RT |  |  | 
i2: bnez r2, i7 |  | FE | DE | RN | RR | DI | IS | IS | IS | IS | IS | IS | EX | WB | RT |  | 
i3: add r2, r5, #2 |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT | RT | RT | RT |  | 
i4: add r7, r2, #3 |  |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT | RT | RT |  | 
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 0 | -
r3 | 0 | -
r4 | 0 | -
r5 | 0 | -
r6 | 0 | -
r7 | 0 | -
 | value
r0 | #10
r1 | #44
r2 | #666
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | #666 |  | r2 | 1 | 0 | 0 | i1
rob4 | - |  | - | 1 | 0 | 1 | i2
rob5 | #17 |  | r2 | 1 | 0 | 0 | i3
rob6 | #20 |  | r7 | 1 | 0 | 0 | i4
rob7 | - |  | r4 | 0 | 0 | 0 | i5
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | rob7 | 1 | #17 | 1 | #20
0 | rob4 | 1 | #666 | 1 | #0
0 | rob5 | 1 | #15 | 1 | #2
tag (wakeup)
data
Rename
Retire
H
T
i2
Squash all pipeline stages. (i5) They contain only younger instructions when branch reaches ROB head.
Squash ROB by setting T=H.
Recover RMT by flash-clearing all valid bits.

## Slide 93
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
 | v | ROB tag
r0 | 0 | -
r1 | 0 | -
r2 | 0 | -
r3 | 0 | -
r4 | 0 | -
r5 | 0 | -
r6 | 0 | -
r7 | 0 | -
 | value
r0 | #10
r1 | #44
r2 | #666
r3 | #33
r4 | #7
r5 | #15
r6 | #-7
r7 | #345
 | value |  | dst | rdy | exc. | mis. | pc
rob0 |  |  |  |  |  |  | 
rob1 |  |  |  |  |  |  | 
rob2 |  |  |  |  |  |  | 
rob3 | #666 |  | r2 | 1 | 0 | 0 | i1
rob4 | - |  | - | 1 | 0 | 1 | i2
rob5 | #17 |  | r2 | 1 | 0 | 0 | i3
rob6 | #20 |  | r7 | 1 | 0 | 0 | i4
rob7 | - |  | r4 | 0 | 0 | 0 | i5
… |  |  |  |  |  |  | 
rob31 |  |  |  |  |  |  | 
Rename Map Table (RMT)
Issue Queue (IQ)
Architectural Register File (ARF)
Reorder Buffer (ROB)
v | dst tag | rs1 rdy | rs1 tag/value | rs2 rdy | rs2 tag/value
0 | rob7 | 1 | #17 | 1 | #20
0 | rob4 | 1 | #666 | 1 | #0
0 | rob5 | 1 | #15 | 1 | #2
tag (wakeup)
data
Rename
Retire
H
T
i7
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
i1: load r2, #0(r1) | FE | DE | RN | RR | DI | IS | EX@ | EXD$ | …miss… |  |  |  | WB | RT |  |  | 
i2: bnez r2, i7 |  | FE | DE | RN | RR | DI | IS | IS | IS | IS | IS | IS | EX | WB | RT |  | 
i3: add r2, r5, #2 |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT | RT | RT | RT |  | 
i4: add r7, r2, #3 |  |  |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | RT | RT | RT |  | 
i5: add r4, r2, r7 |  |  |  |  | (note: could have fetched more instr. here) |  |  |  | FE | DE | RN | RR | DI | IS | EX |  | 
i7: |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | FE | 

## Slide 94: From In-order to Out-of-Order
Rename
Decode
Fetch
Register Read
Dispatch
Issue
Decode
Fetch
Register Read / Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
Insert instructions in-order
Remove instructions out-of-order
Retire
Expanded Register File: ARF (committed state) + ROB (speculative state)
Provides for recovery and eliminates WAR/WAW
Commit instructions in-order from ROB to ARF