## Slide 1: ECE 463/563 Microprocessor Architecture
Additional ILP Topics
Prof. Eric Rotenberg

## Slide 2: Additional ILP topics
Interrupts
  Types
  Exception is akin to a mispredicted branch
  ROB supports exception recovery
Faster recovery of mispredicted branches
  Checkpointing and restoring the RMT
Handling memory dependencies
  Store Queue (SQ) and Load Queue (LQ)
Going from scalar to superscalar
  Examples of superscalar complexity

## Slide 3: Additional ILP topics
Interrupts
  Types
  Exception is akin to a mispredicted branch
  ROB supports exception recovery
Faster recovery of mispredicted branches
  Checkpointing and restoring the RMT
Handling memory dependencies
  Store Queue (SQ) and Load Queue (LQ)
Going from scalar to superscalar
  Examples of superscalar complexity

## Slide 4: Interrupts
Interrupt
  Event that requires temporarily stopping program execution to service the event
Synchronous vs. asynchronous interrupts
  Synchronous: Instruction in the program causes the interrupt
  Asynchronous: External request causes the interrupt

## Slide 5: Three types of interrupts
External interrupts
  Asynchronous
  Examples
    I/O device request
    Timer interrupt
    Power failure interrupt
Exceptions
  Synchronous
  Examples
    Invalid opcode
    Arithmetic overflow, divide-by-0, etc.
    Page fault
Operating system (O/S) calls
  Synchronous
  Initiated via an explicit instruction in ISA, e.g., “syscall” or “trap”

## Slide 6: Handling interrupts
Stop program execution
  Synchronous: Stop at the instruction causing the interrupt
  Asynchronous: Stop at an arbitrary instruction, as soon as convenient
Service the interrupt
  Transfer control to O/S interrupt handler
  Depending on the interrupt, the program may be:
    resumed immediately following the interrupt handler, OR
    context-switched out and resumed later
Resume program from where we left off

## Slide 7: Example: “Quick” Page Fault
1
2
3
4
5
6
7
8
15
9
10
11
12
13
14
8
O/S interrupt handler
load:
D-TLB miss, MMU page table walk: page fault
Restart from load: D-TLB miss, MMU page table walk: succeeds, fill D-TLB
Suspend Process-1 by saving its arch. registers to its process control block (PCB) in memory (stores)
Example: “Quick” page fault
  First-ever reference to this virtual page (no swap-in), and
  there’s already a free physical page in DRAM (no swap-out), therefore
  no swap file activity is required.
Update PTE in Page Table with virtual-to-physical mapping
Resume Process-1 by restoring its arch. registers from its PCB in memory (loads) and restarting from the load
dynamic instruction stream
Process-1

## Slide 8: Example: “Slow” Page Fault
1
2
3
4
5
6
7
8
15
9
10
11
12
13
14
8
O/S interrupt handler
load:
D-TLB miss, MMU page table walk: page fault
Suspend Process-1 by saving its arch. registers to its PCB in memory (stores)
Example: “Slow” page fault
  First-ever reference to this virtual page (no swap-in), and
  there isn’t a free physical page available in DRAM (need swap-out), therefore
  initiate one background DMA transfer to copy a victim physical page from DRAM to disk.
  DMA takes a few milliseconds in the background.
Context-switch to a different process to keep the processor busy in the meantime: resume previously suspended Process-2 by restoring its arch. registers from its PCB in memory (loads) and restarting from its previously interrupted PC
dynamic instruction stream
work on other program
Disk interrupts processor:
done with DMA transfer
O/S interrupt handler
Suspend Process-2 by saving its arch. registers to its PCB in memory (stores)
Zero-out bytes of freed physical page in DRAM (for security)
Update PTE in Page Table with virtual-to-physical mapping
Resume Process-1 by restoring its arch. registers from its PCB in memory (loads) and restarting from the load
Process-1
Process-2
Restart from load: D-TLB miss, MMU page table walk: succeeds, fill D-TLB

## Slide 9: Impact of exceptions from a microarchitecture standpoint
Offending instruction is akin to a mispredicted branch
  Fetch unit predicted the next PC as usual
  When the exception is detected later, we realize that the next PC after the offending instruction should be that of the exception handler
ROB supports recovery for this unexpected control-flow transfer
  Offending instruction posts exception flag and exception cause in its ROB entry
  Wait until ROB head (H) reaches the offending instruction
  Save PC of offending instruction and exception cause (both are available in its ROB entry) in ISA-defined system registers
  Squash the pipeline (ROB T=H, squash frontend and backend pipeline stages, flash-clear RMT valid bits)
  Set Fetch Unit’s PC to that of the generic exception handler (this PC is either pre-determined by the ISA or in an ISA-defined system register)

## Slide 10: Exception recovery via ROB
1
2
3
4
5
6
7
8
15
9
10
11
12
13
14
load:
page fault
reorder buffer
H
T
1
2
3
4
5
6
7
8
15
9
10
11
12
13
14
load:
page fault
reorder buffer
H
T
PC of 8
exc. cause
system regs.
1
2
3
4
5
6
7
reorder buffer
H
T
PC of 8
exc. cause
system regs.
a
h
b
c
d
e
f
g
first instr. in exception handler
1
2
3
4
5
6
7
reorder buffer
H
T
PC of 8
exc. cause
system regs.

## Slide 11: Additional ILP topics
Interrupts
  Types
  Exception is akin to a mispredicted branch
  ROB supports exception recovery
Faster recovery of mispredicted branches
  Checkpointing and restoring the RMT
Handling memory dependencies
  Store Queue (SQ) and Load Queue (LQ)
Going from scalar to superscalar
  Examples of superscalar complexity

## Slide 12: Branch misprediction recovery alternatives
Wait until mispredicted branch reaches head of ROB
  Simple recovery mechanism
    ROB: Tail = Head (after retiring the branch)
    Pipeline: squash all instructions in pipeline (all instructions are younger than the branch)
    RMT: flash-clear all valid bits
  Delaying recovery until retirement increases the misprediction penalty
Immediately initiate recovery, while branch is in middle of ROB
  Minimizes the misprediction penalty
  Complex recovery mechanism
    ROB: Tail = entry after branch’s ROB entry (still simple)
    Pipeline: Selectively squash only those instructions in the pipeline that are younger than the branch and not those that are older than the branch.
    RMT: Must restore RMT to what it was just after renaming the branch. One approach is to checkpoint the RMT after every branch. Restore RMT to the corresponding checkpoint when a mispredicted branch is detected. (Note that retirement unit updates not only RMT but also RMT-checkpoints.)

## Slide 13: RMT Checkpoint & Recovery (1)
dynamic instruction stream
ROB
Head
(Retire)
Tail
(Rename)
v
rob_tag
BRANCH
Head
(Retire)
rob0
rob1
rob2
rob3
rob4
rob5
r5
r5
r5
1
rob4
rob6
rob7
rob8
rob9
rob10
rob11
rob12
rob13
rob14
rob15
rob16

## Slide 14: Checkpoint & Recovery (2)
dynamic instruction stream
BRANCH
v
rob_tag
CHECKPOINT
Tail
(Rename)
v
rob_tag
Head
(Retire)
save
ROB
rob0
rob1
rob2
rob3
rob4
rob5
r5
r5
rob6
rob7
rob8
rob9
rob10
rob11
rob12
rob13
rob14
rob15
rob16
r5
1
rob4
r5
1
rob4

## Slide 15: Checkpoint & Recovery (3)
dynamic instruction stream
BRANCH
Tail
(Rename)
v
rob_tag
Head
(Retire)
wrong path
wrong
state!
v
rob_tag
CHECKPOINT
ROB
rob0
rob1
rob2
rob3
rob4
rob5
r5
r5
rob6
rob7
rob8
rob9
rob10
rob11
rob12
rob13
rob14
rob15
rob16
r5
1
rob4
r5
1
rob12
r5

## Slide 16: Checkpoint & Recovery (4)
dynamic instruction stream
BRANCH
Tail
(Rename)
v
rob_tag
Head
(Retire)
squashed
restore
v
rob_tag
CHECKPOINT
ROB
rob0
rob1
rob2
rob3
rob4
rob5
r5
r5
rob6
rob7
rob8
rob9
rob10
rob11
rob12
rob13
rob14
rob15
rob16
r5
1
rob4
r5
1
rob4

## Slide 17: Checkpoint & Recovery (5)
dynamic instruction stream
BRANCH
Tail
(Rename)
v
rob_tag
Head
(Retire)
correct path
correct
state
ROB
rob0
rob1
rob2
rob3
rob4
rob5
r5
r5
rob6
rob7
rob8
rob9
rob10
rob11
rob12
rob13
rob14
rob15
rob16
r5
r5
1
rob10

## Slide 18: What about exception recovery?
There’s nothing functionally wrong with initiating exception recovery immediately, while the offending instruction is in the middle of the ROB
  It is even ok to speculatively transfer control to the exception handler
  If there is an older mispredicted branch or an older exception, this offending instruction and its control-transfer to the handler will be squashed
The problem is that checkpoints are resource intensive and we can’t checkpoint the RMT at every instruction that could post an exception
There are alternate methods for repairing the RMT that leverage the ROB, for example:
  Flash-clear the RMT valid bits. This rolls it back to the ROB head, which is too far back.
  Temporarily stall the rename and retire stages.
  Serially restore RMT mappings by walking ROB entries from the ROB head to the offending instruction (ROB is used as a “redo log” to redo updates to the RMT).
  See ECE 721 for more on this!

## Slide 19: Using ROB to serially repair RMT (1)
dynamic instruction stream
BRANCH
Tail
(Rename)
v
rob_tag
Head
(Retire)
wrong path
wrong
state!
ROB
rob0
rob1
rob2
rob3
rob4
rob5
r5
r5
rob6
rob7
rob8
rob9
rob10
rob11
rob12
rob13
rob14
rob15
rob16
r5
1
rob12
r5

## Slide 20: Using ROB to serially repair RMT (2)
dynamic instruction stream
BRANCH
Tail
(Rename)
Head
(Retire)
squashed
ROB
rob0
rob1
rob2
rob3
rob4
rob5
r5
r5
rob6
rob7
rob8
rob9
rob10
rob11
rob12
rob13
rob14
rob15
rob16
v
rob_tag
r5
0
-
Flash-clear all valid bits …
rolls back too far. Start walking each ROB entry to re-enter mappings into RMT.

## Slide 21: Using ROB to serially repair RMT (3)
dynamic instruction stream
BRANCH
Tail
(Rename)
Head
(Retire)
squashed
ROB
rob0
rob1
rob2
rob3
rob4
rob5
r5
r5
rob6
rob7
rob8
rob9
rob10
rob11
rob12
rob13
rob14
rob15
rob16
v
rob_tag
r5
1
rob2
Still not there yet… keep walking ROB and re-enter mappings.

## Slide 22: Using ROB to serially repair RMT (4)
dynamic instruction stream
BRANCH
Tail
(Rename)
Head
(Retire)
squashed
ROB
rob0
rob1
rob2
rob3
rob4
rob5
r5
r5
rob6
rob7
rob8
rob9
rob10
rob11
rob12
rob13
rob14
rob15
rob16
v
rob_tag
r5
1
rob4
Still not there yet… keep walking ROB and re-enter mappings.

## Slide 23: Using ROB to serially repair RMT (5)
dynamic instruction stream
BRANCH
Tail
(Rename)
Head
(Retire)
squashed
ROB
rob0
rob1
rob2
rob3
rob4
rob5
r5
r5
rob6
rob7
rob8
rob9
rob10
rob11
rob12
rob13
rob14
rob15
rob16
v
rob_tag
r5
1
rob4
Done repairing the RMT. It again reflects having renamed all instructions up to and including the branch instruction. Repair strategy works for other offending instructions, such as exceptions and other kinds of mispredictions.

## Slide 24: Additional ILP topics
Interrupts
  Types
  Exception is akin to a mispredicted branch
  ROB supports exception recovery
Faster recovery of mispredicted branches
  Checkpointing and restoring the RMT
Handling memory dependencies
  Load/Store Queue (LSQ)
  Separate Store Queue (SQ) and Load Queue (LQ)
Going from scalar to superscalar
  Examples of superscalar complexity

## Slide 25: Load/Store Queue (LSQ)
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
Rename
Retire
LSQ
unified load/store queue (LSQ) | address | store value
store |  | 
store |  | 
load |  | 
store |  | 
load |  | 
load |  | 
head
tail
ROB
head
tail
1
in-order
Allocate a ROB entry, at ROB tail, for each instruction (including loads and stores).

## Slide 26: Load/Store Queue (LSQ)
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
Rename
Retire
LSQ
unified load/store queue (LSQ) | address | store value
store |  | 
store |  | 
load |  | 
store |  | 
load |  | 
load |  | 
head
tail
ROB
head
tail
2
in-order
Allocate a free IQ entry for each instruction (including loads and stores).
Allocate an LSQ entry, at the LSQ tail, for each load or store instruction.

## Slide 27: Load/Store Queue (LSQ)
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
Rename
Retire
LSQ
unified load/store queue (LSQ) | address | store value
store |  | 
store |  | 
load |  | 
store |  | 
load |  | 
load |  | 
head
tail
ROB
head
tail
3
OOO
After a load or store issues from the IQ (i.e., after register dependencies are resolved), its address is computed in the AGEN unit. Load: (1) Deposit address into its LSQ entry. (2) Search both the D$ and older stores in the LSQ (details to follow).
Store:
(1) Deposit address and value into its LSQ entry.
(2) Search younger loads for mispredicted loads (details to follow).

## Slide 28: Load/Store Queue (LSQ)
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
Rename
Retire
LSQ
unified load/store queue (LSQ) | address | store value
store |  | 
store |  | 
load |  | 
store |  | 
load |  | 
load |  | 
head
tail
ROB
head
tail
4
in-order
When the Retire stage retires a load or store from the ROB head, signal the LSQ to pop the same load or store from the LSQ head.
Load: If ROB misp. flag is set, squash (including mispredicted load) and restart fetching from the load (details to follow).
Store: Commit store to the D$ using its address and value
available in its LSQ entry (details to follow).
store

## Slide 29: Principle #1: Retire stores in-order and non-speculatively
LSQ holds all in-flight stores (dispatched but not yet retired) in their original program order
Retire a store from the LSQ to D$ only when the ROB signals that the store is at ROB head and is completed
  Stores to same address retire in-order: correctly handle WAW hazards through memory
  Each store retires non-speculatively: all prior instructions have retired so there are no prior unresolved mispredictions or exceptions

## Slide 30
unified load/store queue (LSQ) | address | store value
store |  | 
store |  | 
load |  | 
store |  | 
load |  | 
load |  | 
head
tail

## Slide 31
unified load/store queue (LSQ) | address | store value
store |  | 
store |  | 
load |  | 
store | A | 30
load |  | 
load |  | 
head
tail

## Slide 32
unified load/store queue (LSQ) | address | store value
store |  | 
store | A | 20
load |  | 
store | A | 30
load |  | 
load |  | 
head
tail

## Slide 33
unified load/store queue (LSQ) | address | store value
store | A | 10
store | A | 20
load |  | 
store | A | 30
load |  | 
load |  | 
head
tail
D$
retire
In-order retirement from ROB and LSQ:
Correct handling of WAW through memory.
Correct recovery to precise memory state (mispredictions, exceptions).

## Slide 34: Principle #2: A load searches both the LSQ and D$ to get the most recent value corresponding to its address

## Slide 35
unified load/store queue (LSQ) | address | store value
store | A | 10
store | A | 20
load |  | 
store | A | 30
load |  | 
load | A | 
head
tail
D$
Store-load forwarding examples
A: 10
B: 666
load gets “30” (not “20” from older matching store in LSQ or “10” from D$)

## Slide 36
unified load/store queue (LSQ) | address | store value
store | A | 10
store | A | 20
load |  | 
store | A | 30
load | B | 
load | A | 
head
tail
D$
A: 10
B: 666
load received “30”
load gets “666” from D$ (no LSQ hit)

## Slide 37: Principle #3: Need a load execution policy to handle unknown prior store addresses
Loads and stores issue from IQ OOO based on their source register readiness
A load’s address may be generated before prior stores’ addresses
This load sees that there are prior stores in the LSQ, but whether or not it conflicts with these prior stores is unknown
Two options:
  Stall the load similar to a cache miss (even if D$ has the block): “memory disambiguation stall”
  Speculatively execute the load based on a prediction that these prior stores do not conflict

## Slide 38
unified load/store queue (LSQ) | address | store value
store | A | 10
store | A | 20
load |  | 
store | (?) | 
load | B | 
load |  | 
head
tail
D$
A: 10
B: 666
load speculatively gets “666” from D$ (no LSQ hit)

## Slide 39
unified load/store queue (LSQ) | address | store value
store | A | 10
store | A | 20
load |  | 
store | A | 30
load | B | 
load |  | 
head
tail
D$
A: 10
B: 666
load speculatively got “666” from D$ (no LSQ hit at the time)
Older store, which executes late, searches LSQ for speculatively executed younger loads.
No conflict detected so do not post a misprediction. Speculative “load B” confirmed OK.

## Slide 40
unified load/store queue (LSQ) | address | store value
store | A | 10
store | A | 20
load |  | 
store | (?) | 
load |  | 
load | A | 
head
tail
D$
A: 10
B: 666
load speculatively gets 20

## Slide 41
unified load/store queue (LSQ) | address | store value
store | A | 10
store | A | 20
load |  | 
store | A | 30
load |  | 
load | A | 
head
tail
D$
A: 10
B: 666
load speculatively received “20”
Older store, which executes late, searches LSQ for speculatively executed younger loads.
Conflict detected (late) so post a misprediction in the mispredicted load’s ROB entry.
mispredicted load detected (got 20 instead of 30)

## Slide 42: Separate SQ and LQ
Typically, the LSQ is implemented physically with a separate Store Queue (SQ) and Load Queue (LQ)
  The effect is the same as having a unified LSQ
  More efficient hardware design (smaller CAMs / associative searches)
    Loads only need to search the SQ (not other loads) for store-load forwarding
    Stores only need to search the LQ (not other stores) for detecting mispredicted loads
  How it works
    A load knows where it logically exists among stores in the SQ, even though it doesn’t literally have a SQ entry. So it knows which stores are before it.
    A store knows where it logically exists among loads in the LQ, even though it doesn’t literally have a LQ entry. So it knows which loads are after it.

## Slide 43: Load/Store Execution Lane
AGEN unit for computing load and store addresses
Three structures
  L1 D$ (and L1 D-TLB)
  Store Queue (SQ): contains all active stores in program order
    Stores are speculative until they reach head of ROB
    SQ commits stores to D$ non-speculatively and in-order
    Loads search SQ for store values on which they depend
  Load Queue (LQ): contains all active loads in program order
    Loads may execute out-of-order with respect to prior stores
      Executed load gets wrong value if it depends on an older store that hasn’t executed yet
    Stores search LQ for mispredicted loads

## Slide 44: Store Instruction
Dispatch Stage (in-order)
  Store is allocated the SQ entry at tail of SQ (its SQ_index)
  Store also notes the current LQ tail, so it knows which loads are after it in program order (its LQ_index)
Execute Stage (out-of-order)
  AGEN: Generate store’s address
  Write SQ: Write store’s address and value into its SQ entry (at its SQ_index)
  Read LQ: Use store’s address and LQ_index to search LQ for mispredicted loads: loads after the store in program order (between its LQ_index and LQ_tail), with the same address as the store, which already executed.
Retire Stage (in-order)
  When a store reaches the head of the ROB, ROB signals SQ to commit its oldest store (SQ_head) to the D$

## Slide 45: Load Instruction
Dispatch Stage (in-order)
  Load is allocated the LQ entry at tail of LQ (its LQ_index)
  Load also notes the current SQ tail, so it knows which stores are before it in program order (its SQ_index)
Execute Stage (out-of-order)
  AGEN: Generate load’s address
  Write LQ: Write load’s address into its LQ entry (at its LQ_index)
  Read SQ and D$: Use load’s address and SQ_index to search SQ for best estimate (some stores’ addresses still unknown) of producer store: nearest store before the load in program order (between SQ_head and its SQ_index), with the same address as the load. If SQ hit, use store value, else use D$ value.
Retire Stage (in-order)
  When a load reaches the head of the ROB:
    Signal LQ to remove its oldest load (LQ_head)
    If load’s misprediction bit is set in ROB, initiate misprediction recovery. Fetch unit is redirected to PC of load so that the load re-executes, this time correctly since it is oldest instruction in pipeline (all prior stores have committed to D$).

## Slide 46: Speculative Load Handling: A Rich Design Space
A load is speculative if there are prior unknown store addresses (in general)
Four dimensions of speculative load handling
  Memory Dependence Predictor
  Store-load synchronization strategy
  Load misprediction recovery strategy
  Impact of store execution (split stores vs. no split stores)
ECE 721 covers store and load handling in depth.

## Slide 47: Additional ILP topics
Interrupts
  Types
  Exception is akin to a mispredicted branch
  ROB supports exception recovery
Faster recovery of mispredicted branches
  Checkpointing and restoring the RMT
Handling memory dependencies
  Store Queue (SQ) and Load Queue (LQ)
Going from scalar to superscalar
  Examples of superscalar complexity

## Slide 48: Superscalar processing
scalar = 1 instruction/cycle
superscalar: N instructions/cycle
  Increase width of each stage of the pipeline
FE | DE | RN | RR | DI | IS | EX | WB | RT |  |  | 
FE | DE | RN | RR | DI | IS | EX | WB | RT |  |  | 
 | FE | DE | RN | RR | DI | IS | EX | WB | RT |  | 
 | FE | DE | RN | RR | DI | IS | EX | WB | RT |  | 
 |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | 
 |  | FE | DE | RN | RR | DI | IS | EX | WB | RT | 

## Slide 49: Superscalar Complexity
Rename
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
D$
agen
Simple ALU
Complex ALU
Mem
Retire
Achieving peak fetch width requires interleaved I$ plus fetch bundle formation logic.
Predict multiple branches per cycle.
Predicted-taken branches cause lower-than-peak fetch width.
I$ / branch predictor performance critical for superscalar: larger I$/predictor is slower.
Highly-ported register file (ARF+ROB). N-way superscalar: 2N read ports and N write ports.
Exposing more instruction-level parallelism requires larger IQ.
Issue logic more complex. N-way superscalar: (1) N wakeup ports, (2) select and issue up to N ready instructions (N arbiters, N read ports).
Bypass network is very complex. Each execution lane forwards its value to every other execution lane. N-way superscalar: (1) N bypasses, (2) bypasses are long wires (must span all execution lanes), (3) each lane has an {N+1}:1 MUX at bypass sinks to select a forwarded value from any lane or the instruction’s value from the IQ.
Highly-ported RMT. N-way superscalar: 2N read ports and N write ports.
Must handle dependencies within rename bundle: cross-check logic + RMT bypass muxes.
N-way superscalar: (1) must locate up to N free IQ entries, (2) N write ports into IQ.

## Slide 50: Navigating the IPC/frequency Trade-off
Naïvely increasing superscalar complexity can increase cycle time, hence, decrease frequency
How to navigate the IPC/frequency trade-off
  Microarchitect must balance IPC and frequency to achieve best overall performance
  Heroic physical design so that you can “have your cake (high IPC) and eat it too (high frequency)”
    Surgical pipelining of critical paths
    Custom cells vs. standard cells
    Expend more power for speed where profitable

## Slide 51: Case study of superscalar complexity: fetch multiple instructions in parallel
Suppose I$ block size = 16 bytes = four 4-byte instr.
Suppose we want a superscalar processor with a fetch width of four instructions
Conventional I$ can supply 1 block at most
  Good: get 4 instr. if fetch bundle is aligned at a block boundary.
  Bad: get fewer than 4 instr. if it is not aligned.
A taken branch’s target can land the fetch PC in the middle of a block, i.e., the next fetch bundle starts in the middle of a block

## Slide 52: I$ misalignment
Fetch 1 aligned cache block / cycle
Unaligned PC: Fetch useless instructions before 1st instr. and not enough instructions after

## Slide 53: Dual-Ported I$
Read two blocks to get full bandwidth
Two read ports are expensive

## Slide 54: Inexpensive dual-porting: interleaving
Realization
  Don’t need to read out any two blocks
  Just need to read out two consecutive blocks
  Split cache into two banks: one bank holds blocks with even block addresses, other holds blocks with odd block addresses
  This is called 2-way interleaving or banking
  Guarantees full fetch width each cycle despite misaligned PC (assuming no predicted-taken branch terminates the fetch bundle early)

## Slide 55: Interleaved I$
Divide cache into two banks
  First bank has even blocks
  Second bank has odd blocks
  Called an interleaved cache or banked cache