## Slide 1: ECE 463/563 Microprocessor Architecture
Caches: 3C’s model of misses
Prof. Eric Rotenberg

## Slide 2: Categories of misses (3C’s model)
Compulsory misses
  The first reference to a memory block
Capacity and Conflict misses
  Scenario:
    A memory block is in the cache, then replaced, then re-referenced
    The re-reference is a miss (either capacity miss or conflict miss)
  Difference between capacity miss and conflict miss
    Capacity miss:
      A miss that occurs due to the limited capacity of the cache
      A capacity miss is attributed to limited capacity, not constraints of the cache’s mapping function
    Conflict miss:
      A miss that occurs due to limited capacity within a set
      A conflict miss is attributed to constraints of the cache’s mapping function. For example, suppose only four memory blocks are ever referenced by a program, the cache is direct-mapped and has a capacity of 256 memory blocks, but all four memory blocks referenced by the program map to the same set. Clearly there is sufficient capacity for the four blocks, but the inflexible mapping function prevents caching all of them at the same time.
    Note:
      A fully-associative cache only suffers compulsory misses and capacity misses. It doesn’t suffer conflict misses. Any non-compulsory miss is attributed to limited capacity, not to the mapping function, because a block can be put anywhere in the cache.
      Direct-mapped and set-associative caches suffer from all three types of misses.
The 3Cs:
Compulsory miss
Capacity miss
Conflict miss

## Slide 3: How to classify a miss?
Suppose we are simulating a “cache under observation” and a given reference misses in the cache. We want to classify the miss as compulsory, capacity, or conflict.
If first reference to a memory block
  Compulsory miss
  This also means that the number of compulsory misses is the number of unique memory blocks ever referenced.
Else
  The miss is either a capacity miss or a conflict miss. How to figure out the type of miss?
  In addition to simulating the cache under observation, ALSO simulate a fully-associative cache that has the same total capacity (same number of blocks) as the cache under observation.
    If fully-associative test cache also misses, then classify the miss as a capacity miss
    If fully-associative test cache hits, then classify the miss as a conflict miss

## Slide 4: Example
Direct-mapped cache
Capacity is 2 memory blocks
The processor references three different memory blocks (A,B,C) in the following sequence
All three memory blocks map to the same set
C C B C B C A C B

## Slide 5: Example (cont.)
cache under observation:
direct-mapped, two blocks
test cache:
fully-assoc., two blocks
Compulsory miss
First time C is ever referenced: The miss in “cache under observation” is a compulsory miss.
miss
(miss)
C C B C B C A C B
BEFORE
cache under observation:
direct-mapped, two blocks
test cache:
fully-assoc., two blocks
ANALYSIS
C
AFTER
C | 

## Slide 6: Example (cont.)
cache under observation:
direct-mapped, two blocks
test cache:
fully-assoc., two blocks
hit
(hit)
C C B C B C A C B
BEFORE
cache under observation:
direct-mapped, two blocks
test cache:
fully-assoc., two blocks
ANALYSIS
C
C
AFTER
C | 
C | 

## Slide 7: Example (cont.)
cache under observation:
direct-mapped, two blocks
test cache:
fully-assoc., two blocks
C C B C B C A C B
BEFORE
cache under observation:
direct-mapped, two blocks
test cache:
fully-assoc., two blocks
ANALYSIS
C
B
AFTER
Compulsory miss
First time B is ever referenced: The miss in “cache under observation” is a compulsory miss.
miss
(miss)
C | 
C (lru) | B

## Slide 8: Example (cont.)
cache under observation:
direct-mapped, two blocks
test cache:
fully-assoc., two blocks
C C B C B C A C B
BEFORE
cache under observation:
direct-mapped, two blocks
test cache:
fully-assoc., two blocks
ANALYSIS
B
C
AFTER
Conflict miss
C has been referenced before, so the miss in “cache under observation” is not a compulsory miss. The miss in “cache under observation” is a conflict miss: the test cache hit, meaning there is sufficient capacity in both caches for the two most recently referenced blocks (C,B) prior to this reference (C).
miss
(hit)
C (lru) | B
C | B (lru)

## Slide 9: Example (cont.)
cache under observation:
direct-mapped, two blocks
test cache:
fully-assoc., two blocks
C C B C B C A C B
BEFORE
cache under observation:
direct-mapped, two blocks
test cache:
fully-assoc., two blocks
ANALYSIS
C
B
AFTER
Conflict miss
B has been referenced before, so the miss in “cache under observation” is not a compulsory miss. The miss in “cache under observation” is a conflict miss: the test cache hit, meaning there is sufficient capacity in both caches for the two most recently referenced blocks (B,C) prior to this reference (B).
miss
(hit)
C | B (lru)
C (lru) | B

## Slide 10: Example (cont.)
cache under observation:
direct-mapped, two blocks
test cache:
fully-assoc., two blocks
C C B C B C A C B
BEFORE
cache under observation:
direct-mapped, two blocks
test cache:
fully-assoc., two blocks
ANALYSIS
B
C
AFTER
Conflict miss
C has been referenced before, so the miss in “cache under observation” is not a compulsory miss. The miss in “cache under observation” is a conflict miss: the test cache hit, meaning there is sufficient capacity in both caches for the two most recently referenced blocks (C,B) prior to this reference (C).
miss
(hit)
C (lru) | B
C | B (lru)

## Slide 11: Example (cont.)
cache under observation:
direct-mapped, two blocks
test cache:
fully-assoc., two blocks
C C B C B C A C B
BEFORE
cache under observation:
direct-mapped, two blocks
test cache:
fully-assoc., two blocks
C
A
AFTER
ANALYSIS
Compulsory miss
First time A is ever referenced: The miss in “cache under observation” is a compulsory miss.
miss
(miss)
C | B (lru)
C (lru) | A

## Slide 12: Example (cont.)
cache under observation:
direct-mapped, two blocks
test cache:
fully-assoc., two blocks
C C B C B C A C B
BEFORE
cache under observation:
direct-mapped, two blocks
test cache:
fully-assoc., two blocks
A
C
AFTER
ANALYSIS
Conflict miss
C has been referenced before, so the miss in “cache under observation” is not a compulsory miss. The miss in “cache under observation” is a conflict miss: the test cache hit, meaning there is sufficient capacity in both caches for the two most recently referenced blocks (C,A) prior to this reference (C).
miss
(hit)
C (lru) | A
C | A (lru)

## Slide 13: Example (cont.)
cache under observation:
direct-mapped, two blocks
test cache:
fully-assoc., two blocks
C C B C B C A C B
BEFORE
cache under observation:
direct-mapped, two blocks
test cache:
fully-assoc., two blocks
C
B
AFTER
ANALYSIS
Capacity miss
B has been referenced before, so the miss in “cache under observation” is not a compulsory miss. The miss in “cache under observation” is a capacity miss: the test cache also missed, meaning there is NOT sufficient capacity in both caches for the three most recently referenced blocks (B,A,C) prior to this reference (B).
miss
(miss)
C | A (lru)
C (lru) | B

## Slide 14: Backup Slides
Same example on the next slide, simulated more efficiently on one slide

## Slide 15: Example (cont.)
cache under observation:
direct-mapped, two blocks
test cache:
fully-assoc., two blocks
reference
hit/miss, miss type
C
C
C
C
B
C
C
C
B
C (lru)
B
B
C
C
B (lru)
C
B
C (lru)
B
A
C
C
B (lru)
C
A
C (lru)
A
B
C
C
A (lru)
Compulsory miss
Compulsory miss
Compulsory miss
Hit
Conflict miss
Conflict miss
Conflict miss
Conflict miss
Capacity miss