## Slide 1: ECE 463/563 Microprocessor Architecture
Caches: AAT; influence of cache size, assoc., and block size; influence of L2 cache
Prof. Eric Rotenberg

## Slide 2: Three factors of cache performance
hit time (HT):
  The cache access time (in units of seconds), i.e., time it takes to search the cache (whether it hits or misses)
  Depends on cache configuration, circuit level implementation, and technology
miss rate (MR):
  The fraction of memory references that miss in the cache:
    miss rate = number of misses / number of references
  Depends on cache configuration and the running program’s memory reference stream
miss penalty (MP):
  The time it takes to bring a memory block into the cache
  With one level of cache and a simple memory system, miss penalty is often approximated with a fixed value
  More generally, different misses perceive different miss penalties due to complex memory hierarchy: multiple levels of cache and a complex memory system. In this case, miss penalty is the average miss penalty.

## Slide 3: Average access time (AAT)
Memory stall time:
Memory stall time = Number of misses x Miss penalty
Total time spent on memory references, including both hits and misses:
Total access time = (Number of references) x (Hit time) + (Number of misses) x (Miss penalty)
Average access time (AAT) for a single memory reference:
AAT = Total access time / Number of references
AAT = (Hit time) + (Number of misses / Number of references) x (Miss penalty)
AAT = (Hit time) + (Miss rate) x (Miss penalty)
AAT = HT + MR x MP

## Slide 4: Measuring cache performance
Run a program and collect a trace of memory references
Simulate just the control part (i.e., metadata) of cache under consideration (metadata: valid bits, dirty bits, tags, LRU or other replacement counters)
Measure miss rate
  Can use to estimate Average Access Time (AAT)
Example below:
parameter | description | where gotten from | example value
HTL1 | hit time of L1 | circuit design analysis | 1 ns
MRL1 | miss rate of L1 | computer architecture simulator (e.g., Proj. 1) | 0.01
MPL1 | miss penalty of L1 | system level analysis of time to get a block from main memory | 100 ns

## Slide 5: Influence on AAT of:
L1 cache’s size
L1 cache’s associativity
L1 cache’s block size
Addition of L2 cache
When you play with the factors above, one or more of HTL1, MRL1, and/or MPL1 will be affected.

## Slide 6: Increase L1 cache’s size keep assoc. fixed and block size fixed
Decrease miss rate
Increase hit time
miss rate
“diminishing returns”
log2(cache size)
Small decrease in miss rate in this region may not justify (1) big increase in hit time, and (2) taking chip area away from other units.
Asymptotically approaches just the compulsory miss rate. At some point, cache size becomes large enough to eliminate capacity and conflict misses.
compulsory miss rate

## Slide 7: Increase L1 cache’s associativity keep size fixed and block size fixed
In general, for the same cache size and block size, increasing associativity tends to decrease miss rate
  Decrease conflict misses
  Asymptotically approaches just the compulsory + capacity miss rate
May increase hit time, for the same cache size. Energy per access must also be looked at.
diminishing returns
miss rate
log2(associativity)
4-way or 8-way set-associative is almost equivalent to fully-associative in many cases
compulsory+capacity miss rate
direct- mapped
fully- assoc.

## Slide 8: Increase L1 cache’s block size keep size fixed and assoc. fixed
Miss rate may decrease, up to a point, due to exploiting more spatial locality
  May reduce compulsory misses. Larger blocks may result in fewer unique blocks as compared to smaller blocks, resulting in fewer compulsory misses. This is definitely true if the larger blocks tend to encompass multiple of the smaller blocks that we originally had.
Miss rate may increase after a point, due to cache pollution
  For a fixed cache size, a side-effect of larger blocks is having fewer total blocks in the cache. It’s a trade-off between hits on consecutive bytes (favors fewer, large blocks) and hits on non-consecutive bytes (favors more, small blocks). At some point, you exhaust all the spatial locality and increasing block size further only takes cache space away from useful bytes in other blocks.
log2(block size)
miss rate
“cache pollution”

## Slide 9
Main Memory (shown: bytes frequently referenced by CPU)
Example:
Cache has 256B capacity.
Eight 32B blocks
Four 64B blocks
8 compulsory misses
4 compulsory misses
Sixteen 16B blocks
16 compulsory misses
16B
32B
64B
Two 128B blocks
4 compulsory misses
128B
cache pollution
Many capacity misses: can’t fit four 128B blocks.
Best block size for this reference pattern.

## Slide 10: Motivation for adding an L2 cache
Trade-off when you increase L1 cache size
  Decrease L1 miss rate
  Increase L1 hit time
At the crossover point where increasing L1 cache size is harmful to AAT:
  Stop increasing L1 cache size.
  Instead, turn to reducing the average miss penalty of L1 by “catching” some L1 capacity misses (and conflict misses) as hits in a larger cache between L1 cache and main memory.
Acronyms:
HT: hit time
MR: miss rate
MP: miss penalty
AAT = HTL1 + MRL1* MPL1
AAT
Big decrease in MRL1 dominates increase in HTL1.
Increase in HTL1 dominates smaller decrease in MRL1.
L1 cache size

## Slide 11: Add L2 cache
Adding an L2 cache reduces the L1 cache’s miss penalty
L1’s miss penalty without L2 cache
L1’s miss penalty with L2 cache
Acronyms:
HT: hit time
MR: miss rate
MP: miss penalty
MPL1 (w/ L2 cache) = AATL2 = HTL2 + MRL2 * MPL2
MPL2 = main_memory_access_time
MPL1 (w/out L2 cache) = main_memory_access_time
AAT = HTL1 + MRL1 * MPL1

## Slide 12: Add L2 cache (cont.): Example
L1 cache
L2 cache
main memory
12 ns
100 ns
Example | HT | MR | MP
L1 | 1 ns | 0.01 | it depends
L2 | 12 ns | 0.1 | 100 ns
L1 cache
main memory
100 ns
 | L1 cache only | L1 and L2 caches
MPL1 | 100 ns | 22 ns (12 ns + 0.1*100 ns)
AAT | 2 ns (1 ns + 0.01*100 ns) | 1.22 ns (1 ns + 0.01*22 ns)
1,000,000 refs from CPU to L1
10,000 refs from L1 to L2
1,000 refs from L1 to L2

## Slide 13: Old Slides for Backup

## Slide 14
Main Memory (shown: bytes frequently referenced by CPU)
Example:
Cache has 256B capacity.
Eight 32B blocks
Four 64B blocks
8 compulsory misses
4 compulsory misses

## Slide 15
Main Memory (shown: bytes frequently referenced by CPU)
Example:
Cache has 256B capacity.
Eight 32B blocks
Four 64B blocks
exploit more spatial locality
cache pollution