## Slide 1: ECE 463/563 Microprocessor Architecture
Prof. Rotenberg
Simulation Example: L1 + L2 cache, both with WBWA write policy.
Manually simulate the address trace on the following memory hierarchy. Initially, the cache(s) are empty (no valid blocks in cache(s)). Evictions are always performed before bringing in blocks (important detail if simulating multiple levels of cache).

## Slide 2
 | L1 cache |  |  | L2 cache |  | 
address (hex) | tag (hex) | index ¦¦ block offset (binary) | index (hex) | tag (hex) | index ¦¦ block offset (binary) | index (hex)
w 10001AC4 | 10001A | 11000100 | C | 10001 | 101011000100 | AC
r 10002AC2 | 10002A | 11000010 | C | 10002 | 101011000010 | AC
r 10003AC6 | 10003A | 11000110 | C | 10003 | 101011000110 | AC
w 10003AC7 | 10003A | 11000111 | C | 10003 | 101011000111 | AC
cache level | size | associativity | block size | replacement policy | write policy
L1 | 256 B | 1 (direct-mapped) | 16 B | not applicable | WBWA
L2 | 8 KB | 2 | 16 B | LRU | WBWA
L1 # sets =
L1 # index bits = log2(L1 # sets) = log2(16) = 4
L1 # block offset bits = log2(L1_BLOCKSIZE) = log2(16) = 4
L1 # tag bits = 32-4-4 = 24 (top 6 nibbles of address)
L2 # sets =
L2 # index bits = log2(L2 # sets) = log2(256) = 8
L2 # block offset bits = log2(L2_BLOCKSIZE) = log2(16) = 4
L1 # tag bits = 32-8-4 = 20 (top 5 nibbles of address)

## Slide 3
 | L2 cache contents |  |  |  |  |  |  | 
set # | V | D | tag | lru | V | D | tag | lru
AC | 0 | - | - | 0 | 0 | - | - | 1
 | L1 cache contents |  | 
set # | V | D | tag
C | 0 | - | -
CPU issues write request to L1: w 10001AC4
L1 write request (tag=10001A, index=C)
L1 write miss
L1 issues read request to L2: r 10001AC
L2 read request (tag=10001, index=AC)
L2 read miss
L2 issues read request to MEM: r 10001AC
MEM read request (block 10001AC)
L2 installs the block (tag=10001, index=AC, clean)
L2 updates LRU info of set AC
L2 returns the block to L1
L1 installs the block (tag=10001A, index=C, clean)
L1 performs the CPU’s write and sets dirty bit
 | L2 cache contents |  |  |  |  |  |  | 
set # | V | D | tag | lru | V | D | tag | lru
AC | 0 | - | - | 1 | 1 | 0 | 10001 | 0
 | L1 cache contents |  | 
set # | V | D | tag
C | 1 | 1 | 10001A
❶
❷
L1 reads: 0
L1 read misses: 0
L1 writes: 1
L1 write misses: 1
L1 writebacks to L2: 0
L2 reads: 1
L2 read misses: 1
L2 writes: 0
L2 write misses: 0
L2 writebacks to MEM: 0
Total MEM traffic: 1
L1 copy now dirty (differs) wrt L2 copy
L2 copy clean (same) wrt MEM copy

## Slide 4
 | L2 cache contents |  |  |  |  |  |  | 
set # | V | D | tag | lru | V | D | tag | lru
AC | 0 | - | - | 1 | 1 | 0 | 10001 | 0
 | L1 cache contents |  | 
set # | V | D | tag
C | 1 | 1 | 10001A
CPU issues read request to L1: r 10002AC2
L1 read request (tag=10002A, index=C)
L1 read miss, dirty victim block 10001AC
L1 issues write request to L2: w 10001AC
L2 write request (tag=10001, index=AC)
L2 write hit
L2 updates LRU info of set AC
L2 performs L1’s write and sets dirty bit
L1 issues read request to L2: r 10002AC
L2 read request (tag=10002, index=AC)
L2 read miss
L2 issues read request to MEM: r 10002AC
MEM read request (block 10002AC)
L2 installs the block (tag=10002, index=AC, clean)
L2 updates LRU info of set AC
L2 returns the block to L1
L1 installs the block (tag=10002A, index=C, clean)
L1 returns the requested byte(s) to CPU
 | L2 cache contents |  |  |  |  |  |  | 
set # | V | D | tag | lru | V | D | tag | lru
AC | 1 | 0 | 10002 | 0 | 1 | 1 | 10001 | 1
 | L1 cache contents |  | 
set # | V | D | tag
C | 1 | 0 | 10002A
❷
❹
 | L2 cache contents |  |  |  |  |  |  | 
set # | V | D | tag | lru | V | D | tag | lru
AC | 0 | - | - | 1 | 1 | 1 | 10001 | 0
 | L1 cache contents |  | 
set # | V | D | tag
C | 1 | 0 | 10001A
❸
L1 reads: 1
L1 read misses: 1
L1 writes: 1
L1 write misses: 1
L1 writebacks to L2: 1
L2 reads: 2
L2 read misses: 2
L2 writes: 1
L2 write misses: 0
L2 writebacks to MEM: 0
Total MEM traffic: 2
❸
L1 copy now clean (same) wrt L2 copy
L2 copy now dirty (differs) wrt MEM copy

## Slide 5
CPU issues read request to L1: r 10003AC6
L1 read request (tag=10003A, index=C)
L1 read miss, clean victim block 10002AC
L1 issues read request to L2: r 10003AC
L2 read request (tag=10003, index=AC)
L2 read miss, dirty victim block 10001AC
L2 issues write request to MEM: w 10001AC
MEM write request (block 10001AC)
L2 issues read request to MEM: r 10003AC
MEM read request (block 10003AC)
L2 installs the block (tag=10003, index=AC, clean)
L2 updates LRU info of set AC
L2 returns the block to L1
L1 installs the block (tag=10003A, index=C, clean)
L1 returns the requested byte(s) to CPU
 | L2 cache contents |  |  |  |  |  |  | 
set # | V | D | tag | lru | V | D | tag | lru
AC | 1 | 0 | 10002 | 0 | 1 | 1 | 10001 | 1
 | L1 cache contents |  | 
set # | V | D | tag
C | 1 | 0 | 10002A
❹
 | L2 cache contents |  |  |  |  |  |  | 
set # | V | D | tag | lru | V | D | tag | lru
AC | 1 | 0 | 10002 | 0 | 1 | 0 | 10001 | 1
 | L1 cache contents |  | 
set # | V | D | tag
C | 1 | 0 | 10002A
❺
 | L2 cache contents |  |  |  |  |  |  | 
set # | V | D | tag | lru | V | D | tag | lru
AC | 1 | 0 | 10002 | 1 | 1 | 0 | 10003 | 0
 | L1 cache contents |  | 
set # | V | D | tag
C | 1 | 0 | 10003A
❻
L1 reads: 2
L1 read misses: 2
L1 writes: 1
L1 write misses: 1
L1 writebacks to L2: 1
L2 reads: 3
L2 read misses: 3
L2 writes: 1
L2 write misses: 0
L2 writebacks to MEM: 1
Total MEM traffic: 4
L2 copy now clean (same) wrt MEM copy
❺

## Slide 6
CPU issues write request to L1: w 10003AC7
L1 write request (tag=10003A, index=C)
L1 write hit
L1 performs the CPU’s write and sets dirty bit
 | L2 cache contents |  |  |  |  |  |  | 
set # | V | D | tag | lru | V | D | tag | lru
AC | 1 | 0 | 10002 | 1 | 1 | 0 | 10003 | 0
 | L1 cache contents |  | 
set # | V | D | tag
C | 1 | 0 | 10003A
❻
 | L2 cache contents |  |  |  |  |  |  | 
set # | V | D | tag | lru | V | D | tag | lru
AC | 1 | 0 | 10002 | 1 | 1 | 0 | 10003 | 0
 | L1 cache contents |  | 
set # | V | D | tag
C | 1 | 1 | 10003A
❼
L1 reads: 2
L1 read misses: 2
L1 writes: 2
L1 write misses: 1
L1 writebacks to L2: 1
L2 reads: 3
L2 read misses: 3
L2 writes: 1
L2 write misses: 0
L2 writebacks to MEM: 1
Total MEM traffic: 4
L1 copy now dirty (differs) wrt L2 copy
L2 copy still clean (same) wrt MEM copy