## Slide 1: ECE 463/563 Microprocessor Architecture
Memory Hierarchies, Cache Memories H&P: Appendix B and Chapter 2
Prof. Eric Rotenberg

## Slide 2: Processor-memory performance gap
CPU
60%/yr.
(2X/1.5yr)
DRAM
9%/yr.
(2X/10 yrs)
1
10
100
1000
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
DRAM
CPU
1982
processor-memory
performance gap (grew 50% / year)
Performance
Time

## Slide 3: Why main memory is slow
Implementation technology optimized for density (cost), not speed
  DRAM 1T-1C cell
    Dense
    Slower to access than other technologies (e.g., SRAM 6T cell)
  Many bits per unit area
    Cost per bit is low
    More storage for same cost as faster technologies
Main memory is a very large RAM
  Accessing a larger RAM is inherently slower than accessing a smaller RAM
    Regardless of the implementation technology
  Larger address decoders, longer routing to banks, longer wordlines/bitlines within banks, etc.
Going off chip is slow
  On-chip memory controller  I/O pins  memory bus  DRAM chip
  High latency
  Low bandwidth (limited number of I/O pins)

## Slide 4: Quote from 1946
“Ideally one would desire an indefinitely large memory capacity such that any particular … word would be immediately available … We are … forced to recognize the possibility of constructing a hierarchy of memories, each of which has greater capacity than the preceding but which is less quickly accessible.”
A. W. Burks, H. H. Goldstine, and J. von Neumann
Preliminary Discussion of the Logical Design of an Electronic Computing Instrument (1946)

## Slide 5: Locality of Reference
Temporal locality:
  Recently accessed items are likely to be re-accessed soon
  Implies: Keep recently accessed items close by (in a cache)
Spatial locality:
  Items with addresses near one another are likely to be accessed close together in time
  Sequential locality (special case): next item accessed is likely to be at the next sequential address in memory
  Implies: Fetch the “nearest neighbors” of an item when fetching the item (fetch a large memory block)

## Slide 6: How caches work (very high level)
A cached memory block is “tagged” with its address in main memory (so that it can be searched for within the cache)
As a black box:
Cache
searches for
memory block X
CPU asks for a word that is part of memory block X
(X is the address of the referenced memory block)
If not there, cache asks
main memory for memory block X
(called a cache miss)
CPU gets requested word
(it never talks to main memory)

## Slide 7: Simple Memory Hierarchy
registers
data
cache
instruction
cache
Level 1 or “L1” caches
unified data+inst.
L2 cache
CPU
main memory
(DRAM)
memory bus
disk
OS page fault handler
“swap file” on disk gives appearance of a larger main memory
load
store
cache miss
cache miss
page fault
(not relevant to main memory discussion) user files in file system.

## Slide 8: Example Hierarchy: Intel Skylake
Source:
https://en.wikichip.org/wiki/intel/microarchitectures/skylake_(server)
Core 0
L1 D$:
32KB
L1 I$:
32KB
L2 $:
1MB
Core 1
L1 D$:
32KB
L1 I$:
32KB
L2 $:
1MB
Core n
L1 D$:
32KB
L1 I$:
32KB
L2 $:
1MB
…
Shared L3 $: 1.375 x n MB
Physically, each core has a “slice” of the L3 cache; but each core can access any slice.
L3 $ slice:
1.375 MB
L3 $ slice:
1.375 MB
L3 $ slice:
1.375 MB
Interconnection Network
L1 D$: 4 cycles
L2: 14 cycles
L3: 50-70 cycles