## Slide 1: ECE 463/521 Fall `20
Basic Cache Operation
Prof. Eric Rotenberg

## Slide 2
byte #0 | 00…00000000 | 
byte #1 | 00…00000001 | 
byte #2 | 00…00000010 | 
… | 00…00000011 | 
 | 00…00000100 | 
 | 00…00000101 | 
 | 00…00000110 | 
 | 00…00000111 | 
 | 00…00001000 | 
 | 00…00001001 | 
 | 00…00001010 | 
 | 00…00001011 | 
 | 00…00001100 | 
 | … | 
 | … | 
byte #(232-1) | 11…11111111 | 
32-bit address
232 bytes
1 byte of data
MAIN
MEMORY

## Slide 3
mem. block #0 | 00…00000xxx |  |  |  |  |  |  |  | 
mem. block #1 | 00…00001xxx |  |  |  |  |  |  |  | 
mem. block #2 | 00…00010xxx |  |  |  |  |  |  |  | 
… | 00…00011xxx |  |  |  |  |  |  |  | 
 | 00…00100xxx |  |  |  |  |  |  |  | 
 | 00…00101xxx |  |  |  |  |  |  |  | 
 | 00…00110xxx |  |  |  |  |  |  |  | 
 | 00…00111xxx |  |  |  |  |  |  |  | 
 | 00…01000xxx |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | 11…11111xxx |  |  |  |  |  |  |  | 
32-bit address
232 bytes
1 block = 8 bytes
(229 memory blocks)
000
001
010
011
100
101
110
111
block
offset
block
address
Block offset
  Low-order bits of address that specify a byte within the block
  Since cache is managed at granularity of blocks, the block offset bits are irrelevant for determining hit or miss
MAIN
MEMORY

## Slide 4
mem. block #0 | 00…00000xxx |  |  |  |  |  |  |  | 
mem. block #1 | 00…00001xxx |  |  |  |  |  |  |  | 
mem. block #2 | 00…00010xxx |  |  |  |  |  |  |  | 
… | 00…00011xxx |  |  |  |  |  |  |  | 
 | 00…00100xxx |  |  |  |  |  |  |  | 
 | 00…00101xxx |  |  |  |  |  |  |  | 
 | 00…00110xxx |  |  |  |  |  |  |  | 
 | 00…00111xxx |  |  |  |  |  |  |  | 
 | 00…01000xxx |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | 11…11111xxx |  |  |  |  |  |  |  | 
32-bit address
MAIN
MEMORY
1 block = 8 bytes
000
001
010
011
100
101
110
111
block
offset
block
address
CACHE
cache set #0 |  |  |  |  |  |  |  |  | 
cache set #1 |  |  |  |  |  |  |  |  | 
cache set #2 |  |  |  |  |  |  |  |  | 
cache set #3 |  |  |  |  |  |  |  |  | 
Example:
SIZE = 32 bytes
BLOCKSIZE = 8 bytes
1 block per cache set

## Slide 5
mem. block #0 | 00…00000xxx |  |  |  |  |  |  |  | 
mem. block #1 | 00…00001xxx |  |  |  |  |  |  |  | 
mem. block #2 | 00…00010xxx |  |  |  |  |  |  |  | 
… | 00…00011xxx |  |  |  |  |  |  |  | 
 | 00…00100xxx |  |  |  |  |  |  |  | 
 | 00…00101xxx |  |  |  |  |  |  |  | 
 | 00…00110xxx |  |  |  |  |  |  |  | 
 | 00…00111xxx |  |  |  |  |  |  |  | 
 | 00…01000xxx |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | 11…11111xxx |  |  |  |  |  |  |  | 
32-bit address
MAIN
MEMORY
1 block = 8 bytes
000
001
010
011
100
101
110
111
block
offset
block address
CACHE
cache set #0 |  |  |  |  |  |  |  |  | 
cache set #1 |  |  |  |  |  |  |  |  | 
cache set #2 |  |  |  |  |  |  |  |  | 
cache set #3 |  |  |  |  |  |  |  |  | 
index
Index
  Low-order bits of block address indicate which cache set the block will be placed in and where it will be searched for later

## Slide 6
mem. block #0 | 00…00000xxx |  |  |  |  |  |  |  | 
mem. block #1 | 00…00001xxx |  |  |  |  |  |  |  | 
mem. block #2 | 00…00010xxx |  |  |  |  |  |  |  | 
… | 00…00011xxx |  |  |  |  |  |  |  | 
 | 00…00100xxx |  |  |  |  |  |  |  | 
 | 00…00101xxx |  |  |  |  |  |  |  | 
 | 00…00110xxx |  |  |  |  |  |  |  | 
 | 00…00111xxx |  |  |  |  |  |  |  | 
 | 00…01000xxx |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  |  | 
 | 11…11111xxx |  |  |  |  |  |  |  | 
32-bit address
MAIN
MEMORY
1 block = 8 bytes
000
001
010
011
100
101
110
111
block
offset
block
address
CACHE
cache set #0 |  |  |  |  |  |  |  |  | 
cache set #1 |  |  |  |  |  |  |  |  | 
cache set #2 |  |  |  |  |  |  |  |  | 
cache set #3 |  |  |  |  |  |  |  |  | 
tag
index
tag
data
Tag
  Many memory blocks have the same index, i.e., they map to the same cache set
  High-order bits of block address differentiate memory blocks that map to the same cache set
  Record the tag alongside the cached memory block, to identify which memory block is cached in the set
v

## Slide 7: A direct-mapped cache
31
3
2
0
tag
block
offset
index
6
5
hit/miss
row
dec
=?
tag (26 bits)
blocks (8 bytes)
word select (mux)
MAR
MDR
TAG STORE
DATA STORE
LATCH
LATCH
set (holds 1 block)
(26)
(3)
(3)

## Slide 8: A (2-way) set-associative cache
31
3
2
0
tag
block
offset
index
5
4
tag (27 bits)
blocks (8 bytes)
word select (mux)
MAR
MDR
block select (mux)
Notes: this cache is the same size as
the (previous) direct-mapped cache, but
the index field is 1 bit shorter (2 bits total)
A direct-mapped cache is really a 1-way set-associative cache
row
dec
=?
=?
set (holds 2 blocks)
(27)
(2)
(3)

## Slide 9: A fully-associative cache (also called a content addressable memory or CAM)
31
3
2
0
tag
block
offset
tag (29 bits)
word select (mux)
MAR
MDR
=?
tag
=?
tag
=?
tag
=?
tag
=?
tag
=?
tag
=?
tag
=?
tag
Notes: Same size as previous
caches, but no row decoder and
no index at all! Comparators (one
per block) take the place of the row
decoder
(3)
(29)

## Slide 10: Summary: decoding the address
Cache is normally specified as follows:
  {SIZE, ASSOC, BLOCKSIZE}
    SIZE: total bytes of data storage
      Does NOT include “metadata”, aka control bits: valid bit, dirty bit, tag, replacement counters, coherence bits, etc.
    ASSOC: associativity (# of blocks in a set)
    BLOCKSIZE: size of cache block in bytes
  Question: how do we decode the address?
  REMEMBER the following equation (derivation next slide)
  Then compute size of each address field
tag
index
block offset
?
?
?
tag
index
block offset

## Slide 11: Derivation: # sets
 | way 0 | way 1 | way 2 | … | way (ASSOC-1)
set 0 | block | block | block | ... | block
set 1 | block | block | block |  | block
set 2 | block | block | block |  | block
… |  |  |  |  | 
set (#sets-1) | block | block | block |  | block
total bytes of data storage = (# sets) x (# blocks/set) x (# bytes/block)
total bytes of data storage = (# sets) x (# ways) x (# bytes/block)
SIZE = (# sets) x (ASSOC) x (BLOCKSIZE)

## Slide 12: Cache types revisited
Every cache can be classed as a particular “N-way set-associative cache”
Direct-mapped and fully-associative caches are just extremes
Direct-mapped
  Any cache with only 1 way is a direct-mapped cache.
  A direct-mapped cache is the same as a 1-way set-associative cache.
Fully-associative
  Any cache with only 1 set is a fully-associative cache.
  A fully-associative cache is the same as an N-way set-associative cache with only 1 set containing N blocks.

## Slide 13: Generic picture of N-way set-associative cache
 | way 0 | way 1 | way 2 | … | way (N-1)
set 0 | block | block | block | ... | block
set 1 | block | block | block |  | block
set 2 | block | block | block |  | block
… |  |  |  |  | 
set (#sets-1) | block | block | block |  | block
Index a set using the index bits of the block address.
Associatively search for the block among N ways of the set.
Direct-mapped cache is one extreme where there is only 1 way. Once a set is indexed using the index bits from the block address, there is no need to search among multiple blocks within the set because there is only 1 block in the set.
X

## Slide 14: Generic picture of N-way set-associative cache
 | way 0 | way 1 | way 2 | … | way (N-1)
set 0 | block | block | block | ... | block
set 1 | block | block | block |  | block
set 2 | block | block | block |  | block
… |  |  |  |  | 
set (#sets-1) | block | block | block |  | block
Index a set using the index bits of the block address.
Associatively search for the block among N ways of the set.
Fully-associative cache is one extreme where there is only 1 set. There are no index bits within the block address because there is only 1 set: log2(1 set) = 0 index bits. Must associatively search the entire set, i.e., must associatively search the entire cache, for the block.
X