## Slide 1: ECE 463/563 Microprocessor Architecture
Basic Cache Operation, cont.: replacement policies, write policies
Prof. Eric Rotenberg

## Slide 2: Generic Cache
The same equations hold for any cache type
Equation for # of blocks in the cache:
Equation for # of sets in the cache:
Fully-associative: ASSOC = # blocks

## Slide 3: Generic Cache (cont.)
Cache Type | Viewed as generic “N-way Set-Associative Cache”, where N is equal to…
“direct-mapped” | N = 1
“set-associative” | 1 < N < # blocks
“fully-associative” | N = # blocks
 | direct-mapped | 2-way set-associative | fully-associative
BLOCKSIZE | 16 B | 16 B | 16 B
SIZE | 128 B | 128 B | 128 B
ASSOC (N) | 1 | 2 | 8
# blocks | 8 | 8 | 8
# sets | 8 | 4 | 1
way 0
set 0
set 1
set 2
set 3
set 4
set 5
set 6
set 7
way 0
set 0
set 1
set 2
set 3
way 1
way 0
set 0
way 1
way 2
way 3
way 4
way 5
way 6
way 7

## Slide 4: Generic Cache (cont.)
What this means for your Project 1 simulator
  You don’t have to treat the three cache types differently in your simulator
  Support a generic N-way set-associative cache
  Don’t have to specifically worry about the two extremes (direct-mapped / fully-associative)
Also, question: “How do I specify ‘fully-associative’ in the simulator command-line arguments?”
  You don’t specify this explicitly
  Instead, just specify ASSOC to be equal to SIZE/BLOCKSIZE (the number of blocks)

## Slide 5: Replacement Policy
Which block in a set should be replaced when a new block has to be allocated?
  LRU (Least-Recently-Used) is common (or cheaper variants such as pseudo-LRU)
  Others: FIFO, Random, more advanced policies

## Slide 6: LRU Implementation
Small counter per block in set
  # bits in each counter = log2(ASSOC)
  Each block’s counter indicates recency of access w.r.t. other blocks’ counters
  For example: If a set has four blocks, each block gets a 2-bit counter. The block with “0” (b’00) counter was most-recently referenced, the block with “1” (b’01) was second-most-recently referenced, … and the block with “3” (b’11) was least-recently referenced overall.
If access hits in cache:
  Increment the counters of other blocks whose counters are less than the referenced block’s counter (i.e., shift these formerly “more-recent” blocks to now be “less-recent” than the referenced block)
  Set the referenced block’s counter to “0” (now the most-recently-used)
If access misses in cache:
  Replace the LRU block (the block with counter “3”) and set the newly allocated block’s counter to “0” (now the most-recently-used block)
  Increment the counters of all other blocks

## Slide 7: LRU Example
Blocks A, B, C, D, and E all map to the same set
Trace: A B C D D D B D E
(LRU counters are shown in parentheses)
(0)
(2)
(1)
(3)
(1)
(3)
(2)
A (0)
(2)
B (0)
(3)
A (1)
(3)
B (1)
C (0)
A (2)
D (0)
B (2)
C (1)
A (3)
D (0)
B (2)
C (1)
A (3)
D (0)
B (2)
C (1)
A (3)
D (1)
B (0)
C (2)
A (3)
D (0)
B (1)
C (2)
A (3)
D (1)
B (2)
C (3)
E (0)

## Slide 8: Handling Writes
Two questions
  The write update question: Suppose there is a write request to a memory block that is cached in a given cache C. Is just C’s copy of the block updated with new data, or is the next level of the memory hierarchy updated at the same time?
  The write allocate question: Suppose there is a write request to a memory block that is not cached in a given cache C. Do we bring the missing block into C (i.e., do we “allocate” the block)?

## Slide 9: The Write Update Question (1)
Write-through (WT) policy
cache
next level in memory hierarchy

## Slide 10: The Write Update Question (2)
Write-back (WB) policy
cache
next level in memory hierarchy

## Slide 11: The Write Update Question (3)
Write-back (WB) policy
  What happens when a block previously written to needs to be replaced?
  Need to have a “dirty bit” (D) with each block in the cache: set it when block is written to
  When a dirty block is replaced, need to write entire block back to next level of memory (“writeback”)

## Slide 12: The Write Update Question (4)
Write-back (WB) policy
cache
next level in memory hierarchy
D
replacement of a dirty block causes writeback

## Slide 13: The Write Allocation Question (1)
Write-Allocate (WA)
  Bring the block into the cache if the write misses (handled just like a read miss)
  Typically, used with write-back policy: WBWA
Write-No-Allocate (NA)
  Do not bring the block into the cache if the write misses
  Typically, used with write-through policy: WTNA

## Slide 14: The Write Allocation Question (2)
WTNA (scenario: the write misses)
cache
next level in memory hierarchy
write miss

## Slide 15: The Write Allocation Question (3)
WBWA (scenario: the write misses)
cache
next level in memory hierarchy
write miss
D

## Slide 16: Memory Hierarchies, and Key Meaning of Dirty Bit
Memory hierarchies can cause there to be multiple copies of the same block among different levels.
A block is “dirty” within a given cache, if the copy of the block in that cache differs from the nearest copy in a level below it.
A block is “clean” within a given cache, if the copy of the block in that cache is the same as the nearest copy in a level below it.

## Slide 17: Memory Hierarchies, and Write Policies
“Write policy” is a policy associated with a given cache (how that cache handles write requests to it), not with the memory hierarchy as a whole.
That is, different caches at different levels of the memory hierarchy may be designed with different write policies.
That is, for example, you can have a mix of WBWA and WTNA caches in the same memory hierarchy.
When a given cache receives a write request, how that write is handled by that cache depends on that cache’s local write policy.

## Slide 18
 | Mem. Hier. #1 |  |  |  |  | Mem. Hier. #2 |  |  |  |  | Mem. Hier. #3 |  |  | 
 | L1 cache (WBWA) |  |  |  |  | L1 cache (WTNA) |  |  |  |  | L1 cache (WTNA) |  |  | 
 | L2 cache (WTNA) |  |  |  |  | L2 cache (WTNA) |  |  |  |  | L2 cache (WBWA) |  |  | 
X: | 0 | 0 | 99 | 0 | X: | 0 | 0 | 99 | 0 | X: | 0 | 0 | 99 | 0
 | Main Memory |  |  |  |  | Main Memory |  |  |  |  | Main Memory |  |  | 
X: | 0 | 0 | 99 | 0 | X: | 0 | 0 | 99 | 0 | X: | 0 | 0 | 99 | 0
Consider three different memory hierarchies. They all have L1 cache, L2 cache, and main memory. They differ in their L1 write policy or L2 write policy or both, as shown.
The block size is only 4 bytes. In the figure below, each byte of a block is shown as a small rectangle with a value inside. For example, the third byte of block X has the value 99 and all other bytes have the value 0.
INITIAL STATE: Suppose block X was brought into both the L1 and L2 caches but subsequent activity caused block X to be evicted from the L1 cache. Therefore, initially, block X is not in the L1 cache and block X is in the L2 cache.
Suppose the processor issues a write request to the third byte of block X, changing its value from 99 to 55. For each memory hierarchy:
Show where copies of block X exist, after the write is performed.
Show the values of all bytes within block X wherever block X exists, after the write is performed.

## Slide 19
 | Mem. Hier. #1 |  |  |  |  | Mem. Hier. #2 |  |  |  |  | Mem. Hier. #3 |  |  | 
 | L1 cache (WBWA) |  |  |  |  | L1 cache (WTNA) |  |  |  |  | L1 cache (WTNA) |  |  | 
 | L2 cache (WTNA) |  |  |  |  | L2 cache (WTNA) |  |  |  |  | L2 cache (WBWA) |  |  | 
X: | 0 | 0 | 99 | 0 | X: | 0 | 0 | 99 | 0 | X: | 0 | 0 | 99 | 0
 | Main Memory |  |  |  |  | Main Memory |  |  |  |  | Main Memory |  |  | 
X: | 0 | 0 | 99 | 0 | X: | 0 | 0 | 99 | 0 | X: | 0 | 0 | 99 | 0
0
0
55
0
X:
55
55
55

## Slide 20
 | Mem. Hier. #1 |  |  |  |  | Mem. Hier. #2 |  |  |  |  | Mem. Hier. #3 |  |  | 
 | L1 cache (WBWA) |  |  |  |  | L1 cache (WTNA) |  |  |  |  | L1 cache (WTNA) |  |  | 
 | L2 cache (WTNA) |  |  |  |  | L2 cache (WTNA) |  |  |  |  | L2 cache (WBWA) |  |  | 
X: | 0 | 0 | 99 | 0 | X: | 0 | 0 | 99 | 0 | X: | 0 | 0 | 99 | 0
 | Main Memory |  |  |  |  | Main Memory |  |  |  |  | Main Memory |  |  | 
X: | 0 | 0 | 99 | 0 | X: | 0 | 0 | 99 | 0 | X: | 0 | 0 | 99 | 0
0
0
55
0
X:
55
55
55
dirty
clean
clean
dirty