## Slide 1: ECE 463/563 Microprocessor Architecture
Reducing misses: prefetching, loop transformations
Prof. Eric Rotenberg

## Slide 2: Optimizations for Reducing Misses
Prefetching: Hardware, Software
Transform program to increase locality

## Slide 3: Prefetching
Idea: Fetch a block into the cache before the CPU makes a request to that block.
Prefetching can be implemented in hardware, software (e.g., compiler), or both.
Terms: “demand misses” vs. “prefetch misses”
  “Demand miss”: This is a miss triggered by a CPU request. The CPU is demanding a block, right now, and that block is not in the cache.
  “Prefetch miss”: This is a miss triggered by a request made by the prefetcher, which is kind of the point of prefetching: initiate a miss early, before it becomes a demand miss (so that the CPU sees a hit).

## Slide 4: Convert Demand Miss into Prefetch Miss
CPU
$
CPU request (block X)
TIME
demand miss
prefetcher
$
prefetch request (block X)
prefetch miss
CPU
$
CPU request (block X)
hit
time to fetch block (miss penalty)
without prefetching
with prefetching
CPU stalls
CPU doesn’t stall

## Slide 5: Key Aspects of a Hardware Prefetcher
Prefetch trigger: What triggers the hardware prefetcher to initiate a prefetch request?
  Often, a hardware prefetcher initiates a prefetch request for one or more blocks, when a CPU request causes a demand miss. I.e., concurrently with resolving the demand miss to, say, block A, initiate prefetch misses to other blocks X, Y, …, in anticipation of these other blocks being needed in the near future.
  Note, if a prefetch request doesn’t actually miss in the cache (i.e., it hits), then that block isn’t prefetched (obviously).

## Slide 6: Key Aspects of a Hardware Prefetcher (cont.)
Prefetch degree: How many blocks does the hardware prefetcher prefetch, when it is triggered?
  “Prefetch degree” is the number of blocks prefetched, for each trigger event.
  The most conservative prefetcher has a prefetch degree of 1.
  Aggressive prefetchers have prefetch degrees > 1.

## Slide 7: Key Aspects of a Hardware Prefetcher (cont.)
Prediction algorithm: Which block(s) does the hardware prefetcher prefetch?
  This is the secret sauce: predicting which blocks will be referenced in the future that are not currently in the cache.
  Some reference patterns are easy to predict
    Sequential locality of instructions and arrays
    Fixed-strided accesses to arrays
  Other reference patterns are hard to predict
    Linked data structures (lists, trees, graphs, etc.)
    Indirect memory accesses, e.g., a[b[i]]
    Control flow (branches) can cause gaps in sequential or fixed-strided accesses

## Slide 8: Key Aspects of a Hardware Prefetcher (cont.)
Prefetch distance: How far ahead in the anticipated miss stream must we prefetch in order to be timely?
  Timeliness is perhaps less of a concern in an in-order processor
    Suppose the prefetch trigger is a demand miss. CPU demand-misses on block A, and stalls for a long time anyway. While it is stalled, exploit “memory level parallelism” to do one or more prefetch misses in parallel with the demand miss.
  Timeliness of prefetches is a big concern in OOO processors
    An OOO processor can keep fetching and executing instructions when there is a demand miss. So now the prefetcher must be concerned about timeliness: it must be sufficiently far ahead in the reference stream w.r.t. where the CPU is in the reference stream, to provide a tangible advantage.

## Slide 9: Key Aspects of a Hardware Prefetcher (cont.)
Where to put prefetched blocks?
  Prefetch directly into the cache
    Pro: no extra hardware for prefetch buffers
    Con: potential for cache pollution (useless prefetched blocks displacing useful blocks)
    Idea: exploit set-associative caches; prefetched block replaces LRU block in the set, and keep the prefetched block as the LRU since it hasn’t been referenced by the CPU yet.
  Prefetch into a prefetch buffer, and only bring it into the cache when a CPU request hits in the prefetch buffer
    Pro: avoids cache pollution
    Con: added cost of prefetch buffer(s)
    e.g., “stream buffers” for sequential or fixed-strided reference streams

## Slide 10: Key Aspects of a Hardware Prefetcher (cont.)
Where to put hardware prefetchers and how to coordinate multiple prefetchers?
  Prefetchers can be placed at L1, L2, and/or L3
    Just at L1? Just at L2? Just at L3?
    If at multiple levels, should they coordinate?
  Multi-core
    There’s a private L1/L2 prefetcher per core
    If there is a shared L3 prefetcher, does its prediction algorithm get confused by interleaved reference streams from many cores (and from their private L1/L2 prefetchers)?

## Slide 11: Simple Hardware Prefetchers
 | trigger | degree | prediction algorithm | distance | put where?
next-line prefetcher | demand miss A | 1 | prefetch: A+1 | 1 | cache
N next-line prefetcher | demand miss A | N | prefetch: A+1, A+2, …, A+N | 1 | cache
N next-line prefetcher with distance d | demand miss A | N | prefetch: A+1+d, A+2+d, …, A+N+d | d | cache
N-entry stream buffer | Two different triggers: ‘A’ misses in L1 and stream buffer: fill the stream buffer (a FIFO) with N sequential blocks A+1 to A+N. ‘A+1’ misses in L1 and hits at head of stream buffer: pop A+1 from head of stream buffer and move to L1, prefetch A+N+1 at tail of stream buffer to continue the stream. | N to fill stream buffer on a stream buffer miss. 1 to continue stream thereafter on stream buffer hit. | See “trigger” description. | N, because prefetches at the tail of stream buffer keep the prefetcher ahead of the CPU by size of the stream buffer | stream buffer

## Slide 12: Stream Buffer
CPU
$
CPU request (block A)
miss
miss
Stream Buffer
1
CPU
$
A+1
A+2
A+3
A+4
…
A+N
Stream Buffer
2
A
Fetch A to $.
Prefetch A+1…A+N to Stream Buffer.

## Slide 13: Stream Buffer (cont.)
CPU
$
CPU request (block A+1)
A+1
A+2
A+3
A+4
…
A+N
miss
hit
Stream Buffer
3
CPU
$
A+2
A+3
A+4
…
A+N
A+N+1
Stream Buffer
4
A
Pop A+1 from Stream Buffer head to $.
Prefetch A+N+1 to Stream Buffer tail.
A
A+1
Once locked onto a stream, Stream Buffer is always N references ahead of CPU, in the reference stream.

## Slide 14: Stride Prefetcher
A stride prefetcher learns, for each static load (each load PC) in the program, whether or not the load exhibits a strided access pattern and what its stride is.
Example: (block size = 4 elements of a[], b[]) for (i = 1; i < MAX; i += 8) a[i] = b[i];
block X | b[0] | b[1] | b[2] | b[3]
X+1 | b[4] | b[5] | b[6] | b[7]
X+2 | b[8] | b[9] | b[10] | b[11]
X+3 | b[12] | b[13] | b[14] | b[15]
The stride prefetcher is comprised of a PC-indexed prediction table, which is trained by observing
addresses generated by loads. For each load, its entry in the table indicates if it has a fixed stride and what that stride is (as gauged by previous instances of the load). Other aspects such as trigger, degree, distance, and “put where?” are up to the microarchitect. For example, Stride Prefetcher can work in conjunction with a Stream Buffer.
The static load of “b[i]” exhibits a stride of +2 at the block level (X, X+2, X+4, …).

## Slide 15: Software prefetching
Need a “prefetch” instruction
  Sole purpose is to calculate an address and access the cache with the address. If it hits, nothing happens. If it misses, the processor does not stall; the only thing that happens is that the cache will fetch the memory block.
  Like a load instruction, except:
    It does not delay processor on a miss
    It does not change the processor’s architectural state in any way:
      Doesn’t have a destination register
      Doesn’t cause exceptions (we’ll learn about exceptions later)
In other words, the sole purpose of a “prefetch” instruction is to tell the cache to fetch the specified block if it doesn’t already have that block

## Slide 16: Software prefetching (cont.)
Compiler predicts which accesses are likely to cause misses
Compiler inserts prefetch instructions well enough ahead to prevent these accesses from missing
  The misses still occur, but they occur in advance
  The prefetches miss, but the accesses that are targeted by the prefetches do not (if everything works as planned)
for (i = 0; i < 100; i++)
x[i] = c * x[i];
for (i = 0; i < 100; i++) {
prefetch(x[i+k]);
x[i] = c * x[i];
}
Where k depends on (1) the miss penalty
and (2) the time it takes to execute an
iteration assuming hits

## Slide 17: Software prefetching (cont.)
for (i = 0; i < 100; i++) {
prefetch(x[i+k]);
x[i] = c * x[i];
}
Where k depends on (1) the miss penalty
and (2) the time it takes to execute an
iteration assuming hits.
. . .
execution time for one iteration
of inner loop,
assuming cache hits
. . .
CPU is currently in iteration i
prefetch
x[i+10]
miss penalty: time to service a miss
i
i+10
In the example below, k = (100 ns)/(10 ns) = 10.
Example: 100 ns
Example: 10 ns

## Slide 18: Potential issues with prefetching
Cache pollution
  Inaccurate prefetches bring in useless blocks, displacing useful ones
  Must be careful not to increase miss rate
  Solution: prefetch block into a prefetch buffer, transfer block to main cache only when the block is actually referenced by the program
Bandwidth hog
  Inaccurate prefetches waste bandwidth throughout the memory hierarchy
  Must be careful that prefetch misses (prefetch traffic) do not delay demand misses (legitimate traffic)
  Solutions:
    Be selective: balance removing as many misses as possible with minimizing useless prefetches
    Request queues throughout memory hierarchy should prioritize demand misses over prefetch misses
    Software, ISA, and hardware support for enabling/disabling (“chicken switch”) and configuring hardware prefetchers

## Slide 19: Transform program to increase locality
Increase spatial locality
  Explicitly place items close to each other, that are accessed close in time
Increase temporal locality
  Transform computation to increase the number of times items are reused before being replaced in the cache
  Examples:
    Loop interchange
    Loop fusion
    Loop tiling (also called loop blocking)
We’ll only cover this one since it is quite relevant
Feel free to explore these on your own

## Slide 20: Tiling
Idea: access “regions” of arrays instead of whole array
cache
Each iteration of k scans entire x[ ][ ]:
1
2
3
4
for (k = 0; k < N; k++)
for (i = 0; i < N; i++)
for (j = 0; j < N; j++)
… reference x[i][j] …
for (ii = 0; ii < N; ii += T)
for (jj = 0; jj < N; jj += T)
for (k = 0; k < N; k++)
for (i = ii; i < min(ii+T, N); i++)
for (j = jj; j < min(jj+T,N); j++)
… reference x[i][j] …
i
j
j
i
T
Tiling
factor “T”
selected so
that a tile
of x[i][j] fits
in the cache
problem: all of x[i][j] can’t fit in the cache
T
Memory layout of x[ ][ ] shown in 2D
k =
0
ii =
0
jj =
0
i =
0…T
j =
0…T

## Slide 21: Tiling (cont.)
cache
Each iteration of k scans entire x[ ][ ]:
1
2
3
4
for (k = 0; k < N; k++)
for (i = 0; i < N; i++)
for (j = 0; j < N; j++)
… reference x[i][j] …
for (ii = 0; ii < N; ii += T)
for (jj = 0; jj < N; jj += T)
for (k = 0; k < N; k++)
for (i = ii; i < min(ii+T, N); i++)
for (j = jj; j < min(jj+T,N); j++)
… reference x[i][j] …
i
j
j
i
T
problem: all of x[i][j] can’t fit in the cache
T
Memory layout of x[ ][ ] shown in 2D
k =
1
ii =
0
jj =
0
i =
0…T
j =
0…T
Tiling
factor “T”
selected so
that a tile
of x[i][j] fits
in the cache

## Slide 22: Tiling (cont.)
cache
Each iteration of k scans entire x[ ][ ]:
1
2
3
4
for (k = 0; k < N; k++)
for (i = 0; i < N; i++)
for (j = 0; j < N; j++)
… reference x[i][j] …
for (ii = 0; ii < N; ii += T)
for (jj = 0; jj < N; jj += T)
for (k = 0; k < N; k++)
for (i = ii; i < min(ii+T, N); i++)
for (j = jj; j < min(jj+T,N); j++)
… reference x[i][j] …
i
j
j
i
T
problem: all of x[i][j] can’t fit in the cache
T
Memory layout of x[ ][ ] shown in 2D
k =
0
ii =
0
jj =
T
i =
0…T
j =
T…2T
Tiling
factor “T”
selected so
that a tile
of x[i][j] fits
in the cache