## Slide 1: ECE 463/563 Fall `20
Victim Caches
Prof. Eric Rotenberg

## Slide 2: The problem of conflicts at a set
Suppose we have an L1 cache that is direct-mapped and HUGE (tons of sets)
Suppose blocks A and B map to the same set of the L1 cache
Suppose this is what the CPU trace of requests looks like: A B A B A B A B ….
A and B cannot co-exist in this cache and they repeatedly replace each other leading to a 100% miss rate (all requests miss) even though there are only two requested blocks and the L1 cache can conceivably hold a huge number of blocks. A and B are just unlucky.

## Slide 3: What if?
What if we could still have a direct-mapped cache, but just add a little bit of set-associativity at the hotly-contested set? This is essentially the idea behind a victim cache: a flexibly-allocated set-associativity boost to hotly contested sets.
 | way 0
set 0 | 
set 1 | 
… | 
set “unlucky” | A
… | 
… | 
set HUGE-1 | 
After first request A
After second request B
 | way 0
set 0 | 
set 1 | 
… | 
set “unlucky” | B
… | 
… | 
set HUGE-1 | 
A
 | way 0
set 0 | 
set 1 | 
… | 
set “unlucky” | A
… | 
… | 
set HUGE-1 | 
B
After third request A
“swap”

## Slide 4: Victim cache
A victim cache is a small fully-associative cache (e.g., 2-16 cache blocks) that sits alongside the main cache that the victim cache is enhancing.
Throughout this discussion, we’ll talk about a victim cache for the L1 cache. Note, however, that any cache level can be enhanced with its own victim cache.
The L1 cache’s victim cache is NOT just another L2 cache because:
  It is tiny, much smaller than even the L1 cache that it is enhancing.
  The victim cache is an augmentation of the L1 cache – at the same level of the memory hierarchy as the L1 cache – and NOT at a different level in the memory hierarchy.
  It is managed very differently from a conventional cache. In particular, the only way it gets blocks is by taking blocks discarded from the L1 cache as opposed to requesting blocks from the next level. Moreover, the victim cache never contains blocks that are currently in the L1 cache, i.e., the L1 cache and its victim cache are mutually exclusive.

## Slide 5: Victim cache operation
When the L1 cache evicts (replaces) a block, the victim cache will take the evicted (replaced) block. The evicted block is called the “victim block”.
  This is true whether the victim block is clean or dirty. Moreover, the block’s dirty bit transfers with the block when it gets evicted from the L1 cache to the victim cache, because its dirty/clean status is unchanged with respect to the L2 cache below.
When a CPU request to the L1 cache misses, the L1 cache searches its victim cache for recently evicted blocks.
  Victim cache miss: the L1 cache requests the block from the L2 cache, and the newly-evicted block from the L1 cache goes into the victim cache (replacing the LRU block in the victim cache).
  Victim cache hit: the L1 cache and victim cache “swap” blocks. The victim cache sends the requested block to the L1 and the L1 sends its newly-evicted block to the victim cache at the location just vacated by the requested block.

## Slide 6: Victim cache example
2-entry victim cache
  Initially holds blocks X, Y. Note: The only way X and Y could have gotten into the victim cache is they were previously evicted from the L1 cache; and the only way that they can still be there is they have not been subsequently requested by the CPU.
  Y is the LRU block in the victim cache (X was evicted from L1 to victim cache more recently than Y was).
L1 cache is direct-mapped
  Blocks A and B map to the same set in L1 cache
  Trace: A B A B A B…

## Slide 7
X
Y (LRU)
W
L1 cache
victim cache
X (LRU)
W
A
L1 cache
victim cache
BEFORE
AFTER
CPU request: A
“A” misses in L1. L1 searches VC for “A” and it misses. L1 gets “A” from L2 and replaces “W”, VC takes the victim “W”, “W” replaces VC’s LRU block “Y”, and “X” becomes VC’s LRU block.

## Slide 8
X (LRU)
W
A
L1 cache
victim cache
A
W (LRU)
B
L1 cache
victim cache
BEFORE
AFTER
CPU request: B
“B” misses in L1. L1 searches VC for “B” and it misses. L1 gets “B” from L2 and replaces “A”, VC takes the victim “A”, “A” replaces VC’s LRU block “X”, and “W” becomes VC’s LRU block.

## Slide 9
A
W (LRU)
B
L1 cache
victim cache
B
W (LRU)
A
L1 cache
victim cache
BEFORE
AFTER
CPU request: A
“A” misses in L1. L1 searches VC for “A” and it hits. L1 and VC swap blocks: requested block “A” goes from VC to L1, newly-evicted block “B” goes from L1 to VC, notice “B” goes into VC where “A” just vacated, not the VC’s LRU block “W”.

## Slide 10
B
W (LRU)
A
L1 cache
victim cache
A
W (LRU)
B
L1 cache
victim cache
BEFORE
AFTER
CPU request: B
“B” misses in L1. L1 searches VC for “B” and it hits. L1 and VC swap blocks: requested block “B” goes from VC to L1, newly-evicted block “A” goes from L1 to VC, notice “A” goes into VC where “B” just vacated, not the VC’s LRU block “W”.

## Slide 11: Victim Cache – why?
Direct-mapped caches suffer badly from repeated conflicts
  Victim cache provides illusion of set-associativity
  A poor-man’s version of set-associativity