## Slide 1: ECE 463/563 Microprocessor Architecture
Virtual Memory
Prof. Eric Rotenberg

## Slide 2: Virtual Memory
“Virtual memory” is a collaboration between the operating system (O/S) and hardware, facilitated by a specification of virtual memory in the instruction set architecture (ISA)
I strongly recommend you take a solid operating systems course sometime in your career to learn more about the O/S side of virtual memory implementation
  Processes (programs that are being run)
  Page tables
  Memory management

## Slide 3: Virtual Memory
ISA abstraction: every program has its own virtual memory
  Large virtual address space
  Divided into virtual pages (e.g., 4KB)
When a program runs, it needs physical memory
  Physical memory is actual storage:
    DRAM: main memory
    “Swap File” in Hard Disk: overflow storage for main memory
  Operating System (O/S) manages physical memory as a shared resource among many concurrent processes. O/S maps virtual pages to physical pages.
  A process incurs a “page fault” when it references a virtual page that is not mapped to a physical page in DRAM. Either:
    First-ever reference to the virtual page, or
    the virtual page was referenced before and at one time was mapped to a physical page in DRAM, but its physical page currently resides in the swap file and needs to be brought back into the DRAM.
  Page faults are resolved by the O/S page fault handler
A program that is being run is called a “process”.

## Slide 4: Virtual Memory (cont.)
…
…
Physical Memory
Virtual Memory for Process #1
…
Virtual Memory for Process #2
1 physical page
Virtual Page Number
(VPN)
3
4
8
Physical Page Number (PPN)
1 virtual page
DRAM: Main Memory
0
1
2
5
6
7
3
4
8
0
1
2
5
6
7
Virtual Page Number
(VPN)
3
4
N
0
1
2
5
Hard Disk: Overflow Storage for Main Memory
swap file
other files

## Slide 5: Virtual Memory (cont.)
…
…
Physical Memory
Virtual Memory for Process #1
…
Virtual Memory for Process #2
1 physical page
Virtual Page Number
(VPN)
3
4
8
Physical Page Number (PPN)
1 virtual page
DRAM: Main Memory
0
1
2
5
6
7
3
4
8
0
1
2
5
6
7
Virtual Page Number
(VPN)
3
4
N
0
1
2
5
Hard Disk: Overflow Storage for Main Memory
swap file
other files
??
page fault

## Slide 6: Virtual Memory (cont.)
…
…
Physical Memory
Virtual Memory for Process #1
…
Virtual Memory for Process #2
1 physical page
Virtual Page Number
(VPN)
3
4
8
Physical Page Number (PPN)
1 virtual page
DRAM: Main Memory
0
1
2
5
6
7
3
4
8
0
1
2
5
6
7
Virtual Page Number
(VPN)
3
4
N
0
1
2
5
Hard Disk: Overflow Storage for Main Memory
swap file
other files
??
page fault

## Slide 7: Virtual Memory Benefit #1
Automatically allows multiple processes, which use the same virtual addresses, to share a machine without conflicting
  Without virtual memory (no virtual addresses), either only one process could run at a time or everyone would need to coordinate which physical addresses they could use!

## Slide 8: Virtual Memory (cont.)
…
…
Physical Memory
Virtual Memory for Process #1
…
Virtual Memory for Process #2
DRAM: Main Memory
VPN:
3
4
8
0
1
2
5
6
7
PPN:
3
4
N
0
1
2
5
3
4
8
0
1
2
5
6
7
VPN:
Hard Disk: Overflow Storage for Main Memory
swap file
other files

## Slide 9: Virtual Memory (cont.)
Hard Disk: Overflow Storage for Main Memory
swap file
…
…
…
11
12
10
??
Physical Memory
Virtual Memory for Process #1
Virtual Memory for Process #2
VPN:
VPN:
DRAM: Main Memory
PPN:
3
4
8
0
1
2
5
6
7
9
3
4
8
1
2
5
6
7
0
3
4
N
0
1
2
5
other files
page fault

## Slide 10: Virtual Memory Benefit #2
Many processes with large memory footprints can all run even if main memory is exhausted
  Swap file provides an extension to main memory

## Slide 11: Virtual Memory Benefit #3
Access control
  Pages can be annotated with attributes such as read-only vs. read-write, executable vs. non-executable, etc.

## Slide 12: O/S Page Tables
O/S maintains a page table (PT) per process
  PT is software data structure used to translate the process’ virtual addresses to physical addresses
  PT is searched using the virtual address
  There is one PT entry for each virtual page used by the process. Contents of PT entry (for example):
    Whether or not the virtual page has been mapped to a physical page yet
    Whether corresponding physical page is in main memory (DRAM) or in swap space (hard disk)
    If in main memory: PT entry provides physical page number
    If in swap space: PT entry provides location on disk
    PT entry typically has other information too (recency of access, access control bits, etc.)

## Slide 13: Virtual-to-Physical Address Translation
A running program (process)
virtual address
Search the process’ Page Table
physical address
translate virtual address to physical address
Access L1 I/D caches (entry point to memory hierarchy)
* pid = process id, which is held in a special-purpose system register in the CPU
(and pid*)

## Slide 14: Overhead of Virtual Memory
Program counter is a virtual address
  Each instruction fetch requires address translation
Loads and stores generate virtual addresses
  Each load and store requires address translation
So, for each instruction fetch, load, and store, we must search the page table?
  Being literal about this would have unacceptable performance
  Terminology: searching the page table is sometimes called “walking the page table” because it involves multiple accesses to a hierarchical page table (multilevel page table) (note: there are other page table organizations)
  Different ISAs define either hardware page table walks or software page table walks
    Hardware: The hardware’s MMU (memory management unit) does the page table walk
    Software: An O/S software handler does the page table walk

## Slide 15: Virtual-to-Physical Address Translation
A running program (process)
virtual address
physical address
translate virtual address to physical address
Access L1 I/D caches (entry point to memory hierarchy)
Hardware Page Table Walker
10s-100s of cycles
OR
A running program (process)
virtual address
physical address
Access L1 I/D caches (entry point to memory hierarchy)
Software Page Table Walker
10s-100s of cycles
(and pid)
(and pid)

## Slide 16: Translation Lookaside Buffer (TLB)
The TLB is a small cache of recently used address translations

## Slide 17: Virtual-to-Physical Address Translation, with TLB (shown: hardware page table walker)
A running program (process)
virtual address
Hardware Page Table Walker
physical address
translate virtual address to physical address
Access L1 I/D caches (entry point to memory hierarchy)
TLB
TLB miss
Fill TLB
CPU
is executing application
CPU’s MMU
1 cycle
10s-100s of cycles
(and pid)

## Slide 18: Virtual-to-Physical Address Translation, with TLB (shown: software page table walker)
A running program (process)
virtual address
Software Page Table Walker
physical address
translate virtual address to physical address
Access L1 I/D caches (entry point to memory hierarchy)
TLB
TLB miss exception
TLB-write instruction puts translation into TLB
CPU
is executing application
CPU
is executing O/S TLB miss exception handler
1 cycle
10s-100s of cycles
(and pid)

## Slide 19: TLB Organization
TLB organization
  Can be direct-mapped, set-associative, or fully-associative
Unified versus split TLBs
  Unified: One TLB for both instruction and data address translation
  Split: Separate TLBs for instruction and data address translation
    I-TLB: TLB for instruction address translation (program counter). I-TLB sits alongside L1 I-cache.
    D-TLB: TLB for data address translation (loads and stores). D-TLB sits alongside L1 D-cache.

## Slide 20: Using the TLB for translation
=?
6
3
1
2
=?
3
0
1
1
Example: Fully-associative TLB
valid bit
virtual page number (VPN)
physical page number (PPN)
pid=2, VPN=3
PPN=5
=?
8
1
1
1
=?
3
5
1
2
process id (pid)
Example from slide 7:
Note: including process ids (pid) in TLB entries means we don’t have to clear the TLB on context switches (CPU switching to a different process).

## Slide 21: TLB increases hit time
virtual address
TLB
1 cycle
L1 Cache
1 cycle
physical address
L1 Cache
1 cycle
address
Without Virtual Memory
With Virtual Memory

## Slide 22: Using the TLB for translation: A closer look
Observation: What if index bits were entirely contained in page offset bits?
  Then first part of cache access (indexing) would not wait on TLB
Ex: page size = 4KB
# page offset bits = log2(4KB) = 12
This is how cache interprets
the physical address
virtual page number
page offset
31
12
11
0
TLB
tag
block
offset
index
physical page number
page offset
31
12
11
0
31
0
virtual address
physical address

## Slide 23: Accessing TLB and Cache in Parallel
Cache hit time reduces from two cycles to one!
  Because cache can now be indexed in parallel with TLB access (only the final tag match uses the output from TLB)
  But some constraints...
data array
word select
tag array
=?
virtual page number
page offset
31
12
11
0
TLB
tag
physical page number
31
12
index
block offset
11
0
31
12

## Slide 24: Constraint: Size of 1 cache way
Constraint for “physically-indexed cache with parallel cache/TLB access”
  Index and block offset bits contained within page offset bits
  Therefore: Total amount of storage in 1 way of the cache should not exceed page size
Way 1
Way 2
Way N
…
N-way set-assoc. cache
# sets
block size
set

## Slide 25: Page size / associativity tradeoff
From previous slide:
Cache size equation:
Therefore:
Example: MC88110
  Page size = 4KB
  I$, D$ both: 8KB 2-way set-associative
  (8KB/4KB) = 2 ways
Example: VAX series
  Page size = 512B
  For a 16KB cache, need assoc. = (16KB / 512B) = 32-way set-associative!
  Moral: sometimes associativity is thrust upon you

## Slide 26: Physically-indexed vs. virtually-indexed caches
 | hit time impact | cache constraints | synonym problem
physically-indexed cache accessed after TLB | negative: increase hit time because TLB must be accessed first | positive: no constraints on size or associativity | positive: no synonym problem
physically-indexed cache accessed in parallel with TLB | positive: minimize hit time because don’t wait for TLB (except for final tag comparisons) | negative: constraints on size or associativity | positive: no synonym problem
virtually-indexed cache | positive: minimize hit time because don’t wait for TLB (except for final tag comparisons) | positive: no constraints on size or associativity | negative: synonym problem, requires anti-synonym solutions

## Slide 27: Virtually-indexed cache
data array
word select
tag array
=?
virtual page number
page offset
31
12
11
0
TLB
tag
physical page number
31
12
block offset
11
0
31
12
index
12
13
upper two bits of index are virtual (low two bits of untranslated VPN)

## Slide 28: Synonym Problem
Synonyms: two different virtual addresses that map to the same physical address
  May lead to a cache coherence issue – multiple copies of the same block – within the same cache
  These multiple copies become an issue if there is a write to one of the virtual addresses (one copy is updated, the other is not)

## Slide 29: Synonym Example
000000000000000000 0000000000 0000
first virtual address X
16B block
4KB page
virtually-indexed 16KB direct-mapped cache (1024 sets, 10 index bits)
110000000000000000 0100000000 0000
second virtual address Y
000000000000001111 1100000000 0000
L1 cache
set 0:
set 256:
set 512:
set 768:
block A
block A
physical address A
4 block offset bits
10 index bits (top 2 are virtual)
12 page offset bits

## Slide 30: Anti-synonym solutions
Software
  Allow O/S to use synonyms, but require O/S to ensure the same virtual index for synonyms (O/S needs to know cache configuration of the machine)
Hardware
  Before installing a cache-missed block at the virtual index, search for another copy at all possible other sets (e.g., 3 other sets if there are two virtual index bits) and invalidate that copy if found. Ensures there is only one copy at all times.

## Slide 31: VI-PT vs. VI-VT
Virtually-indexed physically-tagged (VI-PT)
  Note that physical tags must be the full PPN (all bits of the physical address minus the page offset), because the untranslated upper bits of the virtual index may differ from their physical counterpart.
  ECE 506 cache coherence stuff: To correctly snoop invalidation/updation requests from other cores, which use physical addresses, need to search multiple sets (e.g., 4 sets if there are two untranslated virtual index bits)
Virtually-indexed virtually-tagged (VI-VT)
  TLB is accessed only on a cache miss, to know which physical block address to demand from the next level in the memory hierarchy
  Solutions to the synonym problem involve an additional step
    Hardware solution: We still handle the synonym problem on a cache miss, using the physical block address of the missing block. For the alternate sets that are searched for a synonym, we need to translate all the virtual block addresses (VT || VI) in these sets to physical block addresses and compare them with the physical block address of the cache-missed block. Also, the same must be done even within this set (where we intend to install the block), because a presumed miss using virtual block address may actually be a hit using physical block address (if there is a synonym even within this set).
    Software solution: The trick of forcing the same virtual index among synonyms is helpful but not complete. The trick ensures synonyms map to the same set, but without further hardware intervention, multiple copies of the same physical block might exist in the same set (assuming set-associativity) due to having different virtual tags. The fix is to use the hardware solution above; all that the software measure did was eliminate checking alternate sets and now we just need to check the same set.
  Homonym problem: Homonyms are the same VPN in two different processes pointing to different PPNs (which is the major motivation for Virtual Memory): {pid=1, VPN=3  PPN=0}, {pid=2, VPN=3  PPN=5} link: homonyms in TLB
    Alternative solutions are the same as those put forth for the TLB
    Solution #1: Flush the VI-VT cache on context switches
    Solution #2: Include process id (pid) as part of the tag to differentiate homonyms
  ECE 506 cache coherence stuff: To correctly snoop invalidation/updation requests from other cores, which use physical addresses, need a reverse-TLB to translate physical addresses to {pid, virtual address}! (to search the VI-VT cache)