## Slide 1: ECE 463/563 Fall `20
Write Buffers
Prof. Eric Rotenberg

## Slide 2: Write misses and the processor
Processor doesn’t need to wait for write miss
  It’s not asking for data
Don’t stall processor
  Do the write in the background
  Need a write buffer
  Processor delegates responsibility to the write buffer, for performing the write to the memory hierarchy

## Slide 3: Write buffer in WBWA Scenario 1: write hit
L1 cache
WBWA policy
write request from processor
Next level in mem. hier.
(L2 cache or main memory)
write hit

## Slide 4: Write buffer in WBWA Scenario 2: write miss
L1 cache
WBWA policy
data
write request from processor
read block from next level
address
Next level in mem. hier.
(L2 cache or main memory)
write miss
merge

## Slide 5: Write buffer in WTNA Scenario 1: write hit
L1 cache
WTNA policy
data
write request from processor
write to next level
address
Next level in mem. hier.
(L2 cache or main memory)
write hit

## Slide 6: Write buffer in WTNA Scenario 2: write miss
L1 cache
WTNA policy
data
write request from processor
write to next level
address
Next level in mem. hier.
(L2 cache or main memory)
write miss

## Slide 7: Complication: write followed by dependent read
A read that hits in the cache is ok
  Since the block is in the cache, any previous writes to the block have completed
A read that misses in the cache needs special treatment
  It must check the write buffer for any pending writes that it depends on
  If its address matches a pending write’s address, read gets data directly from write buffer
    Otherwise it could get stale data from the next level if the younger read completes before the older write

## Slide 8: Read miss checks if it depends on any pending writes in the write buffer
L1 cache
(WBWA or WTNA)
data
read request from processor
address
Next level in mem. hier.
(L2 cache or main memory)
=?
=?
=?
=?
read address
read miss