## Slide 1: ECE 463/563 Microprocessor Architecture
Overview
Prof. Eric Rotenberg

## Slide 2
Computer Architecture & Systems
  Microprocessor Architecture (CPUs)
Easy:
Correct CPU
Hard:
Correct & Fast CPU

## Slide 3: Review: Types of Instructions
ALU type
  ALU = Arithmetic/Logic Unit
  add r3, r1, r2 // RF[r3] = RF[r1] + RF[r2]; PC = PC + 4
  xor r5, r3, r4 // RF[r5] = RF[r3] xor RF[r4]; PC = PC + 4
Memory types (loads and stores)
  lw r1, #4(r2) // addr = RF[r2] + 4
  // RF[r1] = MEM[addr]; PC = PC + 4
  sw #4(r2), r1 // addr = RF[r2] + 4
  // MEM[addr] = RF[r1]; PC = PC + 4
Conditional branch (and other branch types)
  beq r1, r2, #offset // cond = (RF[r1] == RF[r2]) // NPC = PC + 4 // PC = (cond ? (NPC + offset) : NPC)

## Slide 4: Simple Processor Datapath
IF
(instr. fetch)
ID
(instr. decode)
EX
(execute)
MEM
(memory)
WB
(writeback)
Register File
Memory (DRAM & Disk)
1

## Slide 5: Pipelining
Register File
Memory (DRAM & Disk)
IF
(instr. fetch)
ID
(instr. decode)
EX
(execute)
MEM
(memory)
WB
(writeback)
1
2
3
4
5
6
Invention #1

## Slide 6: Problem: Data-Dependent Instructions
Register File
Memory (DRAM & Disk)
IF
(instr. fetch)
ID
(instr. decode)
EX
(execute)
MEM
(memory)
WB
(writeback)
1
2
3
4
5
6

## Slide 7: Register File Bypasses
Register File
Memory (DRAM & Disk)
IF
(instr. fetch)
ID
(instr. decode)
EX
(execute)
MEM
(memory)
WB
(writeback)
Invention #2
1
2
3
4
5
6

## Slide 8: Problem: Branch Instructions
Register File
Memory (DRAM & Disk)
IF
(instr. fetch)
ID
(instr. decode)
EX
(execute)
MEM
(memory)
WB
(writeback)
1
2
2
?

## Slide 9: Branch Prediction
Register File
Memory (DRAM & Disk)
IF
(instr. fetch)
ID
(instr. decode)
EX
(execute)
MEM
(memory)
WB
(writeback)
1
2
2
?
Invention #3
Branch Predictor
3
4

## Slide 10: Problem: “Memory Wall”
Register File
Memory (DRAM & Disk)
IF
(instr. fetch)
ID
(instr. decode)
EX
(execute)
MEM
(memory)
WB
(writeback)
Branch Predictor

## Slide 11: Caches
Register File
Memory (DRAM & Disk)
IF
(instr. fetch)
ID
(instr. decode)
EX
(execute)
MEM
(memory)
WB
(writeback)
Invention #4
Branch Predictor
Instr. Cache
Data Cache

## Slide 12: Caches (cont.)
Locality of reference
  Temporal locality: If you access an item, likely to access it again in near future
  Spatial locality: If you access an item, likely to access a nearby item in the near future

## Slide 13: Problem: Stalled Instructions
Register File
Memory (DRAM & Disk)
IF
(instr. fetch)
ID
(instr. decode)
EX
(execute)
MEM
(memory)
WB
(writeback)
Branch Predictor
Instr. Cache
Data Cache
4
3
2
1
cache miss

## Slide 14: Out-of-Order Execution
Register File
Memory (DRAM & Disk)
IF
(instr. fetch)
ID
(instr. decode)
EX
(execute)
MEM
(memory)
WB
(writeback)
Branch Predictor
Instr. Cache
Data Cache
cache miss
Invention #5
Dynamic Scheduler
1
2
3
4
5
6
7

## Slide 15: Superscalar Execution
Register File
Memory (DRAM & Disk)
IF
(instr. fetch)
ID
(instr. decode)
EX
(execute)
MEM
(memory)
WB
(writeback)
Branch Predictor
Instr. Cache
Data Cache
Dynamic Scheduler
1
2
3
4
5
6
7
8
9

## Slide 16: Deep Pipelining
Register File
Memory (DRAM & Disk)
ID1
EX1
M1
W1
Branch Predictor
Instr. Cache
Data Cache
IF2
IF1
ID2
EX2
M2
W2
Dynamic Scheduler

## Slide 17
BRANCH PREDICTION
OOO EXECUTION
SUPPORT
R.F. BYPASSES
R.F. BYPASSES
L1 Instr. Cache
L1 Data Cache

## Slide 18: Computer System
I/O system
Processor
Compiler
Operating
System
Application
Digital Design
Circuit Design
Instruction Set
Architecture
Firmware
Datapath & Control
Layout
Mem.
Machine Organization
ECE 211, 403
ECE 546
ECE 212
ECE 310, 464/564
ECE 109, 463/563
ECE 466/566
(ECE 506, 786)
ECE 306, CSC 501 or ECE 465/565
ECE 209, 309
Computer Architecture = Instruction Set Architecture + Machine Organization
(Microarchitecture)
ECE 721

## Slide 19: What is Computer Architecture?
Computer Architecture =
Instruction Set Architecture +
Machine Organization
Programmable storage (registers, memory)
Data types and their encodings (integer, floating-point, SIMD)
Instruction set
Instruction formats and encodings
Modes of addressing and accessing data and instructions
Exceptions and interrupts
Virtual memory
Memory consistency model
Capabilities and performance characteristics of principal components
  e.g., register files, ALUs, memory system, etc.
Ways in which these components are interconnected
Choreography of components to realize the ISA
Performance-enhancing techniques and components
  e.g., pipelining, caches, predictors, dynamic scheduling, superscalar execution, etc.

## Slide 20: CPU time equation (brief version)
CPU time = time to execute a program on CPU
Two factors
  # cycles = number of clock cycles to execute a program
  Cycle Time (CT) = clock period = 1 / (clock frequency)
CPU time = (# cycles)x(CT)
# cycles = 109 cycles (1 billion cycles)
clock frequency (f) = 1 GHz = 109 Hz = 109 cycles/s
CT = 1/f = 10-9 s/cycle = 1 ns/cycle
Example:
CPU time = (109 cycles) x (10-9 s/cycle ) = 1 s

## Slide 21: Static vs. Dynamic Instructions
a5: starts with address of first element of array a[] (&a[0])
a3: contains address just after last element of array a[] (&a[1000000])
a1: contains on-going sum, initialized to 0
1a538: ld a4,0(a5) // a4 = a[i]
1a53c: addi a5,a5,8 // increment address to point to next element of a[]
1a540: add a1,a1,a4 // sum += a[i]
1a544: bne a5,a3,1a538 <main+0x34> // branch to top of loop if not after last element of a[]
#include <stdio.h>
#include <inttypes.h>
#define HUGE 1000000
int main(int argc, char *argv[]) {
uint64_t a[HUGE];
uint64_t sum = 0;
// I know, a[] uninitialized... just a demo.
for (uint64_t i = 0; i < HUGE; i++)
sum += a[i];
printf("sum = %lu\n", sum);
return(0);
}
Loop has 4 static instructions.
Dynamically, at run-time, the loop executes 1 million times.
# static instructions = 4
# dynamic instructions = 4 million
Dynamic instruction count influences number of cycles.

## Slide 22: Influence on CPU time
Programmer influence
  Algorithm affects dynamic instruction count: more (fewer) instructions to fetch and execute may cause more (fewer) cycles
  Algorithm affects temporal and spatial locality: more (fewer) cache misses may cause more (fewer) cycles
Compiler influence
  Compiler optimizations affect dynamic instruction count (up or down): more (fewer) instructions to fetch and execute may cause more (fewer) cycles
  Instruction scheduling aims to increase instruction level parallelism and hence reduce cycles
Influence of instruction-set architecture (ISA)
  Complex interactions between ISA, compiler, and microarchitecture. Unresolved debate on whether ISA (e.g., CISC vs. RISC) influences performance as much as microarchitecture.
Microarchitecture influence
  Pipeline optimizations aim to reduce cycles, by increasing instruction-level parallelism (ILP) (the number of concurrently executing instructions and the extent of their overlapped execution)
  Pipeline optimizations may increase CT due to increased logic complexity
  Deeper pipelining aims to decrease CT
Circuit design influence
  Faster circuits aim to decrease CT
Technology influence
  Faster transistors and wires aim to decrease CT
(e.g., pipelining, data bypassing, branch prediction, caches,
dynamic scheduling,
superscalar, etc.)
CYCLES
CYCLES
CYCLES, CT
CT
CT
?

## Slide 23: Overview of Topics in 463/563
Measuring Performance and Cost
Caches and Memory Hierarchies
Instruction-Set Architecture (ISA)
  Defines software/hardware interface
Simple Pipelining
  Data and control (branch) dependencies
  Register file bypasses
  Branch prediction

## Slide 24: Overview of Topics in 463/563
Complex Pipelining and Instruction-Level Parallelism (ILP)
  Data hazards
  Issue Queue (IQ): from in-order to out-of-order scheduling
  Reorder Buffer (ROB): speculation and register renaming
  Precise interrupts
  Superscalar, VLIW, and vector processors

## Slide 25: Projects
Three projects
  Cache simulator
  Branch predictor simulator
  Superscalar pipeline simulator
Programming for projects is harder than anything many of you have encountered before

## Slide 26: Course Grading
40% projects
  Project 1, caches: 15%
  Project 2, branch predictors: 10%
  Project 3, superscalar pipeline: 15%
20% Moodle quizzes
  Can be thought of as homework assignments
  Each quiz tests a unit of knowledge or a whole topic, or gives practice on manually doing a computer architecture simulation
  The current plan is 10 quizzes but there could be more
  A quiz may be assigned with a group of lectures (most common) or a pre-recorded video
20% Midterm
  Covers Performance/Cost, Caches
20% Final (NOT comprehensive)
  Covers ISA, Simple and Complex Pipelining, ILP

## Slide 27: Course Web Page
wolfware.ncsu.edu
  Login
  Select ECE 463/563
Content
  Link to Panopto for live-stream (webcast) and recordings
  Syllabus
  Schedule
  Contact information and office hours
  Q&A and discussion forums
  Projects: specifications, benchmark traces, validation runs, etc.
  Moodle (on-line) quizzes and exams
Check frequently (I announce updates)
Moodle site