## Slide 1: ECE 463/563 Fall `21
Performance and Cost
Prof. Eric Rotenberg

## Slide 2: Outline of topics
Static instructions vs. dynamic instructions
CPU time equation
Influence of programmer, compiler, microarchitecture, circuit design, and technology on CPU time
Comparing performance of two processors
  What we mean by “n times faster”
Benchmarks
  Choice of benchmarks
  Summarizing performance (arithmetic, harmonic, and geometric means)
Speedup
Amdahl’s Law
Cost
  Area
  Power

## Slide 3: Static vs. Dynamic Instructions
a5: starts with address of first element of array a[] (&a[0])
a3: contains address just after last element of array a[] (&a[1000000])
a1: contains on-going sum, initialized to 0
1a538: ld a4,0(a5) // a4 = a[i]
1a53c: addi a5,a5,8 // increment address to point to next element of a[]
1a540: add a1,a1,a4 // sum += a[i]
1a544: bne a5,a3,1a538 <main+0x34> // branch to top of loop if not after last element of a[]
#include <stdio.h>
#include <inttypes.h>
#define HUGE 1000000
int main(int argc, char *argv[]) {
uint64_t a[HUGE];
uint64_t sum = 0;
// I know, a[] uninitialized... just a demo.
for (uint64_t i = 0; i < HUGE; i++)
sum += a[i];
printf("sum = %lu\n", sum);
return(0);
}
Loop has 4 static instructions.
Dynamically, at run-time, the loop executes 1 million times.
# static instructions = 4
# dynamic instructions = 4 million
Dynamic instruction count influences number of cycles.

## Slide 4: CPU time equation
CPU time = time to execute a program on CPU
# cycles = number of clock cycles to execute a program
Cycle Time (CT) = clock period = 1 / (clock frequency)
CPU time = (# cycles)x(CT)
Instruction Count (IC) = number of instructions executed
Cycles-per-Instruction (CPI) = (# cycles)/(IC)  (# cycles) = (IC)x(CPI)
CPU time = (IC)x(CPI)x(CT)
CPU time = IC x CPI x CT

## Slide 5: Influence on CPU time
Programmer influence (IC, CPI)
  Algorithm affects IC
  Algorithm affects temporal and spatial locality. E.g., tiling -> lower D$ miss rates -> fewer cycles per load -> lower CPI
Compiler influence (IC, CPI)
  Compiler optimizations affect IC
  Compiler affects temporal and spatial locality. E.g., tiling -> lower D$ miss rates -> fewer cycles per load -> lower CPI
  Instruction scheduling aims to increase instruction-level parallelism (ILP) -> increase IPC -> decrease CPI
Microarchitecture influence (CPI, CT)
  Pipeline optimizations aim to increase instruction-level parallelism (ILP) (the number of concurrently executing instructions and the extent of their overlapped execution) -> increase IPC -> decrease CPI
  Pipeline optimizations may increase CT due to increased logic complexity
  Deeper pipelining aims to decrease CT
Circuit design influence (CT)
  Faster circuits aim to decrease CT
Technology influence (CT)
  Faster transistors and wires aim to decrease CT
(e.g., pipelining, data bypassing, branch prediction, caches,
dynamic scheduling,
superscalar, etc.)

## Slide 6: Comparing performance of two processors
Run benchmark program on both processors
  Measure CPU time
When we say “Computer X is n times faster than Computer Y”, it means:
  n = Time(Y) / Time(X)

## Slide 7: Benchmarks
Benchmark
  Test program
  Measure time it takes for processor to execute it
Why use benchmarks
  Processor designer: Evaluate performance impact of proposed mechanisms, enhancements, etc.
    Run benchmark on processor without enhancement
    Run benchmark on processor with enhancement
    Observe speedup
  Customer: Compare performance of different computers
    Run benchmark on computer A
    Run benchmark on computer B
    Observe which one takes less time to run benchmark

## Slide 8: Benchmarking Challenges
Choice of benchmark
  Which benchmark is a good testcase?
    Good means representative of real usage
    Benchmarking pitfall:
      Observe big speedup on benchmark due to gizmo
      Conclude gizmo is good idea
      Gizmo doesn’t speedup applications actually run by users, maybe even slows them down (and consumes power, increases cost, etc.)
  One benchmark is probably not representative of all usage scenarios. Use benchmark suite (collection of benchmarks targeting a certain computing market).
    SPEC CPU: PCs, laptops, smart phones (application processors)
    SPEC WEB: web servers
    TPC: database servers
    EEMBC: embedded systems

## Slide 9: Benchmarking Challenges (cont.)
Summarizing performance of benchmark suite as a whole
  Processor designer:
    A proposed microarch. technique may speedup some benchmarks and slow down others
    Or, it may give big speedup on a few benchmarks and no effect on most benchmarks
    Should the proposed microarch. technique be used?
  Customer:
    Some benchmarks run faster on Computer A and some run faster on Computer B
    Which computer should customer buy?

## Slide 10: Summarizing performance
A is 10 x faster than B for P1
B is 10 x faster than A for P2
A is 20 x faster than C for P1
C is 50 x faster than A for P2
etc.
Total execution time gives clearest picture:
  B is 1001/110 = 9.1 x faster than A for both programs
  C is 25 x faster than A for both programs
  C is 2.75 x faster than B for both programs
  Which would you buy? (Answer: C is fastest, overall)
Arithmetic mean of times is good too (A:500.5, B:55, C:20)

## Slide 11: Applying weights
Some benchmarks may be more valuable than others (relative importance, frequency of use, etc.)
Use weighted time or weighted arithmetic mean

## Slide 12: Definitions
metric acronym | description | unit
IC | “dynamic instruction count” i.e., # instructions executed at run-time (different from “static instruction count”, which is # compiled instr. in the program binary) | instr.
CPI | “cycles-per-instruction” CPI = 1/IPC | cycles/instr.
IPC | “instructions-per-cycle” IPC = 1/CPI | instr./cycle
CT | “cycle time”, a.k.a., “clock period” CT = 1/f | s/cycle
f | “clock frequency” or “frequency” f = 1/CT | cycles/s (Hz)
IPS | “instructions-per-second” IPS = IPC · f | instr./s

## Slide 13: On the use of IPC and IPS
Time is the only true measure of performance
When is it valid to compare computers based on IPC alone?
  Only if IC and CT are the same
When is it valid to compare computers based on IPS alone?
  Only if IC is the same
CPU time = IC x CPI x CT
= IC x (1/IPC) x (1/f)
= IC / (IPC x f)
= IC / IPS

## Slide 14: On the proper use of means for summarizing metrics of a benchmark suite
What | Example | Proper mean | Formula | Formula with all weights 1
A quantity | time (s), cycles, CPI, energy (J) | Arithmetic mean |  | 
A rate (quantity per unit time) | IPS (1/s), IPC (1/cycle), power (J/s) | Harmonic mean |  | 
A ratio (unitless) | Speedup w.r.t. a reference computer | Geometric mean |  | 

## Slide 15: Speedup
Enhance a processor with some new mechanism
speedup = TimeOLD / TimeNEW

## Slide 16: Amdahl’s law
Performance improvement (“speedup”) is limited by the part you cannot improve.
x
TOLD
(1-f)TOLD
(f)TOLD
x’
TNEW
(1-f)TOLD
(f)TOLD / s
speedup fraction f by a factor of s

## Slide 17: Amdahl’s law: Example #1
Suppose a novel microarchitecture technique provides a speedup of 1000 (pretty amazing), but only applies 80% of the time to a given benchmark. What is the overall speedup for this benchmark?
  s=1000, f=0.8
  What if s = ∞ ?
  What if s = 100 ?
First interpretation of Amdahl’s Law: Overall speedup is limited by the part you cannot improve.
(20% of time is not reduced, so you are limited to an overall speedup of no more than 5.)

## Slide 18: Amdahl’s law: Example #2
Which is better:
  Invention A: gives a speedup of 10 when it applies (give the inventor a Nobel Prize!), and it applies 5% of the time for a benchmark of interest.
  Invention B: gives a speedup of 1.10 when it applies (how mundane!), and it applies 95% of the time for a benchmark of interest.
  The boring invention is better!
Second interpretation of Amdahl’s Law: The common case matters most. (It was better to do an incremental idea that applied frequently.)
(even for s = ∞ : 1.053)
(close to 1.10)

## Slide 19: Cost of a Chip
100s of engineers:
Microarchitecture
Performance modeling
RTL design
Design-for-test
Verification (functional, timing, phys. design)
Physical design (RTL to layout)
Layout in GDSII:
Patterns for many layers. These patterns guide lithographic fabrication of the layers of the chip.
Masks: quartz plates with patterns on them. A mask for one or several fabrication steps.

## Slide 20: Cost of a Chip (cont.)
Designing a chip means designing and manufacturing a tool (masks) to fabricate that chip
NRE cost of the tool
  e.g., 5 years of salaries and benefits of 100s of engineers
  Cost of the masks themselves (expensive, too)
Example:
  Suppose the NRE cost of the tool is $10,000,000 (includes 5 years of design effort and cost of mask set).
  Suppose we fabricate only 1 chip. What is the cost to the consumer of that 1 chip? Answer: $10,000,000!
  So we have to fabricate many chips to bring the cost per chip down.
Cost has a time factor to it
  A given CPU design has an expiration date, which is the time at which the next generation of CPU is going to come out.
  We have until this expiration date to mass-produce chips for the current generation of CPU.
  This is why “yield” from each silicon wafer is a critical factor in the cost of a chip. Yield is how many working chips we get out of each wafer, which affects how many working chips are produced in, say, a week.
(NRE cost: non-recurring engineering cost, i.e., one-time cost)

## Slide 21: Cost of a Chip (cont.)
yield example for chip design 1: 10 working chips from each wafer
yield example for chip design 2: 5 working chips from each wafer (1/2 the yield of above)
Example: cost of tool = $10,000,000 (5 years design effort + cost of masks)
lifetime of current CPU generation = 2 years
wafers processed per week = 50 wafers/week
2 years of useful manufacturing lifetime

## Slide 22: Cost of a Chip (cont.)
Cost is exponential with die area
  Cost depends on yield: average number of working die from each wafer
  Yield is very sensitive to die area
Two effects as die area increases:
1. Fewer die per wafer.
2. Lower percentage yield among die for the same defect pattern.

## Slide 23: Other costs: Energy and Power
Energy
  Energy is a quantity
  Why we care
    Battery-powered devices: Battery contains finite amount of charge (Q), hence, finite amount of energy (E=QV)
    Plugged-in devices: Utility bill
Power
  Power is a rate
    Power is the rate at which energy is consumed
    P = E / time
  Why we care
    Sustained power
      Higher sustained power results in higher temperature
      Cooling technology limits the sustained power of the chip, called the thermal design power (TDP)
      This means power has become a performance limiter in the semiconductor industry
      Microarchitects need to be inventive to increase performance without exceeding TDP
    Instantaneous power
      Inductive noise problem, Δv = L(di/dt)
      Spike in current draw can cause a transient fluctuation in Vdd, unreliable operation

## Slide 24: CMOS Dynamic Power
See ECE 546 (or lower level circuits courses?) for formal derivation. Here’s a naïve derivation:
  Energy consumed in 1 processor cycle: E = QV = αCV2
  Multiply by frequency to convert to a rate
α = switching activity factor (fraction of devices switching each cycle, on average)
  Number between 0 and 1
C = total capacitance of all devices on chip
V = supply voltage
f = clock frequency (rate of switching)

## Slide 25: CMOS Static Power
Static power
  Power consumed even when there is no switching activity
  In CMOS, this is due to leakage currents in MOSFETs that are supposedly turned off (cut-off region)
CMOS technology scaling
  Lowering Vt with each technology generation
    Increase # transistors being switched (C) + Increase clock frequency (f) = Too much dynamic power !
    Lower Vdd (supply voltage) to help dynamic power
    Lowering Vdd without also lowering Vt slows down transistors (see ECE 546, etc.)
    So must also lower Vt
  But lowering Vt exponentially increases leakage current
  Whereas 10 years ago most power was dynamic, now as much as half of chip power may be static
  Circuit and microarchitectural tricks are being used to keep static power in check

## Slide 26: Energy

## Slide 27: Remarks
Consider which power-related metric applies in a particular scenario
Consider dynamic and static energy in your design decisions
  How much will enhancement increase performance?
  How much will enhancement increase dynamic energy?
  How much will enhancement increase area (more devices which leak), hence, static energy?
  How much additional energy are you willing to pay for the performance increase?
What am I concerned with? (scenario) |  | Relevant metric | Comment
Battery lifetime |  | energy | Important for battery-operated devices (smart phones, tablets, and other mobile devices).
Utility cost |  | energy | Important for large data centers (e.g., Google, cloud computing, etc.).
Reliability | inductive noise | instantaneous power | Current spikes cause Vdd fluctuation (Δv = L di/dt) which can cause faulty operation. Power supply takes time to recover.
 | TDP | sustained power | Running too hot for the cooling technology causes overheating of chip which may lead to failure. TDP has become a performance-limiter in the computing industry and has contributed to frequency stagnating.

## Slide 28: Efficiency
A processor enhancement will increase power consumption
Is this necessarily a bad thing?
  Recall that power is the rate at which energy is consumed
  P = E/t
What higher power could mean:
  IDEAL: Same energy consumption, less time
    The higher power is due to consuming same energy in less time
    The performance enhancement came at the price of no extra energy consumption. This is fantastic.
  NON-IDEAL: Higher energy consumption, less time
    The higher power is due to consuming more energy in less time
    The performance enhancement came at the price of extra energy consumption. This is more typical, and the goal of the processor designer is to minimize the extra energy cost paid for the higher performance.