## Slide 1: ECE 463/563 Microprocessor Architecture
Pipelining: critical path, pipeline hazards
Prof. Eric Rotenberg

## Slide 2: Critical Path
Critical path
  Longest delay (logic and wire delay) between any two flip-flops (Q output to D input)
  Dictates the minimum cycle time (clock period), hence, maximum clock frequency
Going from unpipelined datapath to pipelined datapath reduces cycle time
Deeper pipelining reduces cycle time even further

## Slide 5: Example #1
Unpipelined datapath:
  Critical path = 50 ns
  THEREFORE: CT ≥ 50 ns (freq ≤ 20 MHz)
Pipelined datapath:
  “Local” critical path of IF stage: 10 ns
  “Local” critical path of ID stage: 10 ns
  “Local” critical path of EX stage: 10 ns
  “Local” critical path of MEM stage: 10 ns
  “Local” critical path of WB stage: 10 ns
  (Notice 10+10+10+10+10 = 50)
  THEREFORE: CT ≥ 10 ns (freq ≤ 100 MHz)
Somewhat idealistic
  Stages are perfectly balanced in this example!

## Slide 6: Example #2
Unpipelined datapath:
  Critical path = 50 ns
  THEREFORE: CT ≥ 50 ns (freq ≤ 20 MHz)
Pipelined datapath:
  “Local” critical path of IF stage: 10 ns
  “Local” critical path of ID stage: 12 ns
  “Local” critical path of EX stage: 8 ns
  “Local” critical path of MEM stage: 13 ns
  “Local” critical path of WB stage: 7 ns
  (Notice 10+12+8+13+7 = 50)
  THEREFORE: CT ≥ 13 ns (freq ≤ 77 MHz)
STILL somewhat idealistic
  Ignores delay of intervening pipeline registers!
  Latches/flip-flops have delay: overhead of pipelining

## Slide 7: Example #3
Unpipelined datapath:
  Critical path = 50 ns
  THEREFORE: CT ≥ 50 ns (freq ≤ 20 MHz)
Pipelined datapath:
  Assume worst-case flip-flop delay is 1 ns
  “Local” critical path of IF stage: 11 ns
  “Local” critical path of ID stage: 13 ns
  “Local” critical path of EX stage: 9 ns
  “Local” critical path of MEM stage: 14 ns
  “Local” critical path of WB stage: 8 ns
  (Notice 11+13+9+14+8 = 55)
  THEREFORE: CT ≥ 14 ns (freq ≤ 71 MHz)

## Slide 8
 | 0 | 1 | 2
i | IF ID EX MEM WB |  | 
i+1 |  | IF ID EX MEM WB | 
i+2 |  |  | IF ID EX MEM WB
cycle
instr.
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
i | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  |  |  | 
i+1 |  |  |  |  |  | IF | ID | EX | MEM | WB |  |  |  |  | 
i+2 |  |  |  |  |  |  |  |  |  |  | IF | ID | EX | MEM | WB
Unpipelined datapath:
Long cycle time (CT)
CPI = 1
Example: CT=50ns TPI=CPI*CT
=1*50
=50ns/instr.
Pipelined datapath, but no instr. overlap:
Short cycle time (CT)
CPI = 5
Example: CT=10ns
TPI=CPI*CT
=5*10 =50ns/instr.
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
i | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  |  |  | 
i+1 |  | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  |  | 
i+2 |  |  | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  | 
Pipelined datapath, instr. overlap:
Short cycle time (CT)
CPI = 1 (pipelining)
Example: CT=10ns
TPI=CPI*CT
=1*10 =10ns/instr.

## Slide 9: Summary: Pipelined RISC-V
Isolate each of IF, ID, EX, MEM, WB with latches or flip-flops (“pipeline registers”)
When instruction i is in WB, i+1 is in MEM, etc.
Graphically:
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
i | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  |  |  | 
i+1 |  | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  |  | 
i+2 |  |  | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  | 
i+3 |  |  |  | IF | ID | EX | MEM | WB |  |  |  |  |  |  | 
i+4 |  |  |  |  | IF | ID | EX | MEM | WB |  |  |  |  |  | 
i+5 |  |  |  |  |  | IF | ID | EX | MEM | WB |  |  |  |  | 

## Slide 10: Pipeline Hazards
A hazard reduces the performance of the pipeline
Three kinds:
  Structural hazards: Not enough hardware resources for all combinations of concurrent instructions
  Control hazards: Mispredicted branches incur a misprediction penalty
  Data hazards: Dependencies between instructions prevent their overlapped execution

## Slide 11: Structural Hazards
Uncommon for our pipeline example
Consider a pipeline with a unified data+instruction cache:
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
A (a load) | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  |  |  | 
B |  | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  |  | 
C |  |  | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  | 
D |  |  |  | stall | IF | ID | EX | MEM | WB |  |  |  |  |  | 
E |  |  |  |  |  | IF | ID | EX | MEM | WB |  |  |  |  | 
F |  |  |  |  |  |  | IF | ID | EX | MEM | WB |  |  |  | 
uses cache
make instr. D wait (cache resource busy)

## Slide 12: Control Hazards
PC = PC+4 (sequential) not always correct
Taken branch incurs 3-cycle penalty
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
A | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  |  |  | 
B |  | IF | ID | EX | - | - |  |  |  |  |  |  |  |  | 
C |  |  | IF | ID | - | - | - |  |  |  |  |  |  |  | 
D |  |  |  | IF | - | - | - | - |  |  |  |  |  |  | 
X |  |  |  |  | IF | ID | EX | MEM | WB |  |  |  |  |  | 
Y |  |  |  |  |  | IF | ID | EX | MEM | WB |  |  |  |  | 
A: bne r1,r2,X
B: …
C: …
D: …
E: …
…
X: …
Y: …
Suppose r1 != r2
(branch is taken)
squash
redirect