## Slide 1: ECE 463/563 Microprocessor Architecture
Pipelining: dynamic branch prediction
Prof. Eric Rotenberg

## Slide 2: Introducing: Branch Prediction
Current policy in the IF stage
  Sequential fetch only (PC = PC + 4), until redirected by a taken branch in the MEM (branch completion) stage
  Fetch unit implicitly predicts that there is not a branch or, if there is one, that it is not-taken
  Good: no penalty for not-taken branches
  Bad: 3-cycle penalty for all taken branches
Solution
  Explicit branch prediction in IF stage
  Predict three things in IF stage:
    Is the instruction that is being fetched a branch?
    If so, what is its taken target?
    Is the branch taken or not-taken?
  No penalty when prediction is correct
  3-cycle penalty when prediction is incorrect (“branch misprediction”)

## Slide 3: Branch Target Buffer (BTB)
Branch Target Buffer (BTB)
  Predicts branches in the IF stage
  PC-indexed cache that contains information about previously seen branches
  May be direct-mapped, set-associative, or fully associative
INDEX
TAG
00
Program Counter (PC)
branch type
taken target
TAG
V
prev. outcome
TAG
V
Use this info. to decide what to do
Hit Logic
MEM stage updates the BTB with branches

## Slide 4: Training the BTB (“update”)
Each instruction carries with it a flag that indicates whether it hit or missed in the BTB during IF stage
When a conditional branch reaches the branch completion stage (MEM in our case), the BTB is updated with information about the branch
  If the branch is not already in the BTB (i.e., it missed during the IF stage, as indicated by the flag above), then allocate the branch into the BTB:
    Valid bit and tag (upper bits of PC for identifying the branch)
    The branch’s type
    The branch’s taken target
    The branch’s outcome (taken or not-taken)
  If the branch is already in the BTB (i.e., it hit during the IF stage, as indicated by the flag above), then only need to update the branch’s “prev. outcome” field and only if it differs:
    The branch’s outcome (taken or not-taken)

## Slide 5: Using the BTB (“predict”)
IF stage looks up the current PC in the BTB
  BTB Hit:
    The instruction being fetched is definitely a branch
    Use previous outcome to predict the branch’s direction
      If previously not-taken, then predict not-taken this time
      If previously taken, then predict taken this time
    If predicted taken, we have the taken target from the BTB
  BTB Miss:
    Assume the instruction being fetched is either not a branch at all or a not-taken branch, hence, predict not-taken.

## Slide 6: Detecting and recovering from mispredictions
Taken/not-taken prediction made in the IF stage flows with the instruction down the pipeline
  BTB miss: Prediction is not-taken.
  BTB hit: Prediction is either not-taken or taken, depending on the “previous outcome” field of the BTB entry.
When a branch reaches the MEM stage (branch completion stage), it compares its prediction against its actual outcome
  If its prediction does not match its actual outcome, then a misprediction is detected and recovery is initiated: squash younger instructions in IF, ID, and EX, and redirect the fetch unit to the correct PC.
  If prediction was ‘not-taken’ (used NPC when the branch was predicted in IF) and actual outcome is ‘taken’, redirect the PC to taken target.
  If prediction was ‘taken’ (used taken target from BTB when the branch was predicted in IF) and actual outcome is ‘not-taken’, redirect the PC to NPC.

## Slide 7: Next-PC MUX
PC
NPC in IF stage
TAKEN_TARGET from BTB in IF stage
0
1
prediction
in IF stage
NPC in MEM stage
TAKEN_TARGET in MEM stage (computed in EX stage)
0
1
outcome in MEM stage (computed in EX stage)
prediction = (BTB_hit && (previous_outcome==1))
misprediction in MEM stage
misprediction = (is_branch && (prediction != outcome))
0
1

## Slide 8: Predicting direction of conditional branches (taken vs. not-taken)
It’s fairly easy to (1) know that you have a branch and (2) know its taken target
  This is a matter of caching branches in the BTB
  More branches can be cached by increasing BTB capacity: this is a resource issue and a cycle time issue, not a fundamental accuracy issue
It’s much harder to (3) know which direction to take (taken or not-taken?)
  Why is this part hard?
    This is not just a capacity issue. Even if all static branches fit in the BTB, the directions of dynamic instances of these branches will still be mispredicted.
    All you have is past history, and history is not a perfect indicator of the future
  Predicting the direction of conditional branches has been the subject of much research, in academia and industry

## Slide 9: Branch History Table (BHT)
Recall the BTB has a 1-bit field which is the branch’s “previous outcome”
  More generally referred to as “branch history” since it reflects the branch’s most recent history
  Can be thought of as a “saturating 1-bit counter”
    Increment if branch was taken, but saturate at max value of 1
    Decrement if branch was not-taken, but saturate at min value of 0
Let’s consider some modifications to branch history
  Generalize to “saturating n-bit counter”
    Better accuracy
  Move the branch history out of the BTB into a separate table called a Branch History Table (BHT)
    Gives us freedom to develop better taken/not-taken predictors that use other context for indexing (besides just the PC)
    Better accuracy

## Slide 10: Combined vs. Separate BTB / BHT
combined BTB/BHT:
PC
valid bit
type
taken target
tag
branch history:
previous outcome = “saturating 1-bit counter”
or generalize to “saturating n-bit counter”
separate BTB/BHT:
PC
PC
BTB
BHT
valid bit
type
taken target
tag
Now let’s innovate on this:
more context for indexing

## Slide 11: 1-bit counter
How 1-bit counter works
  Set counter = 1 if branch was taken, 0 if branch was not-taken
  At IF stage, check the 1-bit counter of the branch:
    if counter = 1 then predict taken
    else predict not-taken
  Essentially predicts the branch will do the same thing it did the last time
  Problems:
    Some branches don’t do what they did the last time!
    Need more sophisticated predictor

## Slide 12: Example
4->5 5!=10
void some_function() {
for (i = 0; i < 10; i++) {
...
...
}
}
int main() {
while (1)
some_function();
}
r1 = 0, r2 = 10
LOOP: ...
...
addi r1, r1, #1
bne r1, r2, LOOP
bne r1, r2, LOOP
Actual Outcome |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | N |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | N |  | T | 
1-bit counter | 0 |  | 1 |  | 1 |  | 1 |  | 1 |  | 1 |  | 1 |  | 1 |  | 1 |  | 1 |  | 0 |  | 1 |  | 1 |  | 1 |  | 1 |  | 1 |  | 1 |  | 1 |  | 1 |  | 1 |  | 0 |  | 
Prediction |  | N |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | N |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | N | 
2 mispredicted branches for every 10 branches:
20% misprediction rate (80% accuracy)
Mispredicts fall-through of loop AND first instance
0->1 1!=10
9->10 10==10
8->9 9!=10
3->4 4!=10
2->3 3!=10
1->2 2!=10
7->8 8!=10
6->7 7!=10
5->6 6!=10
0->1 1!=10

## Slide 13: Problem with 1-bit counter
Changes mind too quickly
  Some branches are highly biased taken or not-taken, with a few isolated changes
  Perhaps shouldn’t change prediction after a single change
Consider the previous loop example
  After mispredicting the not-taken branch that exits the loop, the 1-bit counter again mispredicts the first instance of the branch the next time the loop is visited
    Exiting the loop causes two mispredictions instead of just one
  Exiting the loop (single not-taken instance) is not the norm, so should predict taken for the first instance of the branch the next time the loop is visited

## Slide 14: Smith 2-bit counter
Replace prediction bit with 2-bit counter:
11
10
01
00
T
T
T
T
N
N
N
N
predict taken
predict not-taken
initial state
(using NT
heuristic)

## Slide 15: Weak vs. Strong States
Middle states are referred to as “weak states”
  01: “weakly not-taken”
  10: “weakly taken”
Saturated states are referred to as “strong states”
  00: “strongly not-taken”
  11: “strongly taken”
The distinction reflects the fact that:
  From a strong state, it takes two mispredictions to change prediction
  From a weak state, it takes only one misprediction to change prediction
Makes sense to initialize counters to a weak state
  Don’t have any training yet
  Want to train quickly
  Quicker to change prediction when in weak state

## Slide 16: Revisit Example with 2-bit counter
void some_function() {
for (i = 0; i < 10; i++) {
...
...
}
}
int main() {
while (1)
some_function();
}
Actual Outcome |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | N |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | N |  | T | 
2-bit counter | 01 |  | 10 |  | 11 |  | 11 |  | 11 |  | 11 |  | 11 |  | 11 |  | 11 |  | 11 |  | 10 |  | 11 |  | 11 |  | 11 |  | 11 |  | 11 |  | 11 |  | 11 |  | 11 |  | 11 |  | 10 |  | 
Prediction |  | N |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T | 
1 mispredicted branch for every 10 branches:
10% misprediction rate (90% accuracy)
Mispredicts fall-through of loop
Isolated misprediction (due to initial state)
r1 = 0, r2 = 10
LOOP: ...
...
addi r1, r1, #1
bne r1, r2, LOOP
bne r1, r2, LOOP

## Slide 17: Smith n-bit counter
In general, can use n-bit counter
  Potential problems with n > 2
  Smith called it “inertia”

## Slide 18: Another Example: Toggle Branch
Suppose initial state = 10 (weakly taken)
Actual Outcome |  | T |  | N |  | T |  | N |  | T |  | N |  | T |  | N |  | T |  | N | 
2-bit counter | 10 |  | 11 |  | 10 |  | 11 |  | 10 |  | 11 |  | 10 |  | 11 |  | 10 |  | 11 |  | 10
Prediction |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T |  | T | 
5 mispredicted branches for every 10 branches: 50% misprediction rate (50% accuracy)
(Not so bad for an unbiased branch.)
Suppose initial state = 01 (weakly not-taken)
Actual Outcome |  | T |  | N |  | T |  | N |  | T |  | N |  | T |  | N |  | T |  | N | 
2-bit counter | 01 |  | 10 |  | 01 |  | 10 |  | 01 |  | 10 |  | 01 |  | 10 |  | 01 |  | 10 |  | 01
Prediction |  | N |  | T |  | N |  | T |  | N |  | T |  | N |  | T |  | N |  | T | 
10 mispredicted branches for every 10 branches: 100% misprediction rate (0% accuracy)
(Pretty bad.)

## Slide 19: Next Leap in Accuracy
First wave of branch prediction, circa 1980
  Smith counter
Second wave of branch prediction, circa 1990
  Yeh & Patt; Pan et al.; McFarling
  Global branch history
    Exploit correlation among different branches
    Exploit recurring patterns in the global branch history (all branches)
  Local branch history
    Exploit recurring patterns in local branch histories (individual branches)

## Slide 20: gselect branch predictor
global branch history register
n-1
0
behavior of last branch
(shift in most recent outcome)
low order bits of
branch’s PC
...
each entry is a two-bit counter
(or perhaps simpler)
BHR

## Slide 21: dual toggle-branch example
r1=0, r2=0
A: beq r1,r2,D
B: ...
C: ...
D: beq r1,r2,F
E: ...
F: xori r1,r1,#1
G: jump A
PC | A | D | A | D | A | D | A | D
outcome | T | T | N | N | T | T | N | N

## Slide 22: example gselect predictor
Select row using branch PC
  In simulation that follows, only the two rows indexed by A and D are shown for clarity
Select column using a global branch history register (BHR) of length two bits (arbitrary design choice)
  BHR contains the taken/not-taken outcomes of the two most-recent dynamic branches
  Therefore, this gselect predictor has four columns (indexed by two bits of global branch history)

## Slide 23: gselect example
1
0
BHR
matrix
00
01
10
11
A: T, pred N
New BHR = 01
D: T, pred N
New BHR = 11
01
01
01
01
A:
D:
BHR = 00
01
01
01
01
00
01
10
11
10
01
01
01
A:
D:
BHR = 01
01
01
01
01
00
01
10
11
10
01
01
10
A:
D:
BHR = 11
01
01
01
01
00
01
10
11
A: N, pred N
New BHR = 10
D: N, pred N
New BHR = 00
A: T, pred T
New BHR = 01
10
01
01
10
A:
D:
BHR = 10
01
01
01
00
00
01
10
11
10
01
01
10
A:
D:
BHR = 00
00
01
01
00
00
01
10
11
11
01
01
10
A:
D:
BHR = 01
00
01
01
00
00
01
10
11
D: T, pred T
New BHR = 11
11
01
01
11
A:
D:
BHR = 11
00
01
01
00
00
01
10
11
11
01
01
11
A:
D:
BHR = 10
00
01
01
00
00
01
10
11
A: N, pred N
New BHR = 10
underlined means entry
was updated due to last
branch execution

## Slide 24: gselect example (1)
Predict 1st instance of A:
  Predict not-taken (MISPREDICTION)
  Update for 1st instance of A
    Actually taken
  Update the BHR to set up next prediction
 |  | BHR is 00 |  |  | 
 |  | 00: | 01: | 10: | 11:
PC is A | A: | 01 | 01 | 01 | 01
 | D: | 01 | 01 | 01 | 01
 |  | BHR is 00 |  |  | 
 |  | 00: | 01: | 10: | 11:
PC is A | A: | 10 | 01 | 01 | 01
 | D: | 01 | 01 | 01 | 01
0 0
0 1
0
1 (A was actually taken)

## Slide 25: gselect example (2)
 |  | BHR is 01 |  |  | 
 |  | 00: | 01: | 10: | 11:
PC is D | A: | 10 | 01 | 01 | 01
 | D: | 01 | 01 | 01 | 01
 |  | BHR is 01 |  |  | 
 |  | 00: | 01: | 10: | 11:
PC is D | A: | 10 | 01 | 01 | 01
 | D: | 01 | 10 | 01 | 01
0 1
1 1
0
1 (D was actually taken)
Predict 1st instance of D:
  Predict not-taken (MISPREDICTION)
  Update for 1st instance of D
    Actually taken
  Update the BHR to set up next prediction

## Slide 26: gselect example (3)
 |  | BHR is 11 |  |  | 
 |  | 00: | 01: | 10: | 11:
PC is A | A: | 10 | 01 | 01 | 01
 | D: | 01 | 10 | 01 | 01
 |  | BHR is 11 |  |  | 
 |  | 00: | 01: | 10: | 11:
PC is A | A: | 10 | 01 | 01 | 00
 | D: | 01 | 10 | 01 | 01
1 1
1 0
1
0 (A was actually not-taken)
Predict 2nd instance of A:
  Predict not-taken (CORRECT)
  Update for 2nd instance of A
    Actually not-taken
  Update the BHR to set up next prediction

## Slide 27: gselect example (4)
 |  | BHR is 10 |  |  | 
 |  | 00: | 01: | 10: | 11:
PC is D | A: | 10 | 01 | 01 | 00
 | D: | 01 | 10 | 01 | 01
 |  | BHR is 10 |  |  | 
 |  | 00: | 01: | 10: | 11:
PC is D | A: | 10 | 01 | 01 | 00
 | D: | 01 | 10 | 00 | 01
1 0
0 0
1
0 (D was actually not-taken)
Predict 2nd instance of D:
  Predict not-taken (CORRECT)
  Update for 2nd instance of D
    Actually not-taken
  Update the BHR to set up next prediction

## Slide 28: gselect example (5)
 |  | BHR is 00 |  |  | 
 |  | 00: | 01: | 10: | 11:
PC is A | A: | 10 | 01 | 01 | 00
 | D: | 01 | 10 | 00 | 01
 |  | BHR is 00 |  |  | 
 |  | 00: | 01: | 10: | 11:
PC is A | A: | 11 | 01 | 01 | 00
 | D: | 01 | 10 | 00 | 01
0 0
0 1
0
1 (A was actually taken)
Predict 3rd instance of A:
  Predict taken (CORRECT)
  Update for 3rd instance of A
    Actually taken
  Update the BHR to set up next prediction

## Slide 29: gselect example (6)
 |  | BHR is 01 |  |  | 
 |  | 00: | 01: | 10: | 11:
PC is D | A: | 11 | 01 | 01 | 00
 | D: | 01 | 10 | 00 | 01
 |  | BHR is 01 |  |  | 
 |  | 00: | 01: | 10: | 11:
PC is D | A: | 11 | 01 | 01 | 00
 | D: | 01 | 11 | 00 | 01
0 1
1 1
0
1 (D was actually taken)
Predict 3rd instance of D:
  Predict taken (CORRECT)
  Update for 3rd instance of D
    Actually taken
  Update the BHR to set up next prediction

## Slide 30: gselect example (7)
 |  | BHR is 11 |  |  | 
 |  | 00: | 01: | 10: | 11:
PC is A | A: | 11 | 01 | 01 | 00
 | D: | 01 | 11 | 00 | 01
 |  | BHR is 11 |  |  | 
 |  | 00: | 01: | 10: | 11:
PC is A | A: | 11 | 01 | 01 | 00
 | D: | 01 | 11 | 00 | 01
1 1
1 0
1
0 (A was actually not-taken)
Predict 4th instance of A:
  Predict not-taken (CORRECT)
  Update for 4th instance of A
    Actually not-taken
  Update the BHR to set up next prediction

## Slide 31: gselect example (8)
 |  | BHR is 10 |  |  | 
 |  | 00: | 01: | 10: | 11:
PC is D | A: | 11 | 01 | 01 | 00
 | D: | 01 | 11 | 00 | 01
 |  | BHR is 10 |  |  | 
 |  | 00: | 01: | 10: | 11:
PC is D | A: | 11 | 01 | 01 | 00
 | D: | 01 | 11 | 00 | 01
1 0
0 0
1
0 (D was actually not-taken)
Predict 4th instance of D:
  Predict not-taken (CORRECT)
  Update for 4th instance of D
    Actually not-taken
  Update the BHR to set up next prediction

## Slide 32: gselect implementation
gselect’s indexing method is tantamount to concatenating PC and BHR
each entry is a two-bit counter
(or perhaps simpler)
lower bits of PC
BHR
index

## Slide 33: gshare branch predictor
BHR
outcome
of last branch
each entry is a two-bit counter
(or perhaps simpler)
+
index
lower bits of PC

## Slide 34: gshare vs. gselect: rationale
Compared to gselect, gshare enables using more PC bits and more BHR bits, for the same total number of index bits
Hopefully combining bits with XOR preserves valuable information from both PC and BHR

## Slide 35: Yeh/Patt branch predictor
pattern history table
2-bit counters
(indexed by pattern)
1110111
shift registers
local branch history table
00
PC of
branch

## Slide 36: Yeh/Patt Example: toggle branch
A: TNTNTNTNTNTNTNTNTNTN
B: TTTTTTTTTTTTTTTTTTTTTT
01
01
01
01
PT
00
00
00
00
HT
00
01
10
11
A:
B:
A: T, pred N
10
01
01
01
PT
01
00
00
00
HT
00
01
10
11
A:
B:
11
01
01
01
PT
01
01
00
00
HT
00
01
10
11
A:
B:
B: T, pred T
11
00
01
01
PT
10
01
00
00
HT
00
01
10
11
A:
B:
A: N, pred N
B: T, pred N
11
01
01
01
PT
10
11
00
00
HT
00
01
10
11
A:
B:
11
01
10
01
PT
01
11
00
00
HT
00
01
10
11
A:
B:
A: T, pred N
B: T, pred N
11
01
10
10
PT
01
11
00
00
HT
00
01
10
11
A:
B:
A: N, pred N
11
00
10
10
PT
10
11
00
00
HT
00
01
10
11
A:
B:
11
00
10
11
PT
10
11
00
00
HT
00
01
10
11
A:
B:
B: T, pred T
A: T, pred T
11
00
11
11
PT
01
11
00
00
HT
00
01
10
11
A:
B:
PT entries 01, 10 are “trained” for A
and 11 is “trained” for B
In general: provides 96-98% accuracy for integer code

## Slide 37: hybrid predictors
Both predictors supply a prediction. Fetch unit uses only one as selected by chooser.
Chooser updated based on which predictor was correct
  Increment chooser counter if #1 was correct, decrement if #2 was correct
  For detailed implementation, see Project #2 spec.
Predictor
#1
(e.g., gshare)
Predictor
#2
(e.g., bimodal)
Chooser
array of 2-bit
counters
PC of
branch
prediction