## Slide 1: ECE 463/563 Fall `20
RISC-V instruction formats
Design RISC-V unpipelined datapath
Introduce RISC-V pipelined datapath
Prof. Eric Rotenberg

## Slide 2: Designing a processor
Classify instructions for RISC-V:
  Memory references (loads and stores)
  Register-Register ALU Operations
  Register-Immediate ALU Operations
  Branches
Work out the execution for each instruction class
Design appropriate hardware
Look for opportunities to improve…
…while maintaining correct execution

## Slide 3: RISC-V General-Purpose Integer Registers
Note: RISC-V also has an optional floating-point extension that defines 32 general-purpose floating-point registers (f0-f31) and instructions that operate on them.
RISCV32: XLEN = 32
RISCV64: XLEN = 64

## Slide 4: RISC-V Instruction Formats
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
func7 |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | func3 |  |  | rd |  |  |  |  | opcode |  |  |  |  |  | 
imm[11:0] |  |  |  |  |  |  |  |  |  |  |  | rs1 |  |  |  |  | func3 |  |  | rd |  |  |  |  | opcode |  |  |  |  |  | 
imm[11:5] |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | func3 |  |  | imm[4:0] |  |  |  |  | opcode |  |  |  |  |  | 
 | imm[10:5] |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | func3 |  |  | imm[4:1] |  |  |  |  | opcode |  |  |  |  |  | 
imm[31:12] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | rd |  |  |  |  | opcode |  |  |  |  |  | 
 | imm[10:1] |  |  |  |  |  |  |  |  |  |  | imm[19:12] |  |  |  |  |  |  |  | rd |  |  |  |  | opcode |  |  |  |  |  | 
I-type
R-type
S-type
B-type
U-type
J-type
imm[12]
imm[11]
imm[11]
imm[20]

## Slide 5: Some Observations
The formats were designed with various pipeline design considerations in mind, for example…
RISC-V architects wanted to keep rs1, rs2, and rd, in the same locations across all formats that use them, so that reading from the register file can proceed in parallel with decoding the opcode.*
Across all formats with imm, the most-significant-bit (msb) of imm is always at bit 31, so that sign-extension of imm to a full 32-bit (RV32) or 64-bit (RV64) immediate operand can begin before decoding the opcode
* This mostly helps simple pipelines. My opinion: for superscalars, decode and register renaming will likely be serialized anyway to facilitate renaming a bundle of instructions in parallel.

## Slide 6
format | instruction class | notation | effect
R-type | register-register ALU operations | op rd, rs1, rs2 (e.g., add) | RF[rd] = RF[rs1] op RF[rs2]
I-type | register-immediate ALU operations | op rd, rs1, #imm (e.g., addi) | RF[rd] = RF[rs1] op sign_extend(imm)
 | loads | lsize rd, #imm(rs1) (sizes: lb, lh, lw, ld) (also: signed or unsigned) | addr = RF[rs1] + sign_extend(imm) RF[rd] = MEM[addr]
 | JR, JALR |  | 
S-type | stores | ssize #imm(rs1), rs2 (sizes: sb, sh, sw, sd) | addr = RF[rs1] + sign_extend(imm) MEM[addr] = RF[rs2]
B-type | conditional branches | bop rs1, rs2, #imm (e.g., beq, bne, blt, etc.) | condition = (RF[rs1] op RF[rs2]) target = PC + 4 + sign_extend(imm) PC = (condition ? target : PC + 4)
U-type | LUI, AUIPC |  | 
J-type | J, JAL |  | 

## Slide 7: How to Execute an Instruction
Instruction fetch (“IF”)
  IR = MEM[PC]
  NPC = PC + 4
Instruction decode/Register read (“ID”)
  A = RF[rs1]
  B = RF[rs2]
  IMM = sign_extend(imm)
  control = decode(opcode, func3, func7)
    Resulting decoded control signals flow with instr. to later units, to orchestrate the datapath

## Slide 8: Executing an Instruction (cont.)
Execute (“EX”)
  load or store:
    ALUOutput = A + IMM
  register-register ALU operation:
    ALUOutput = A op B
  register-immediate ALU operation:
    ALUOutput = A op IMM
  branch:
    ALUOutput = NPC + IMM
  In addition, evaluate whether to branch or not:
    branch = (is_branch_inst) && (A op B)

## Slide 9: Executing an Instruction (cont.)
Memory access/Branch completion (“MEM”)
  Memory access:
    Load_Mem_Data = MEM[ALUOutput] /* load */
    MEM[ALUOutput] = B /* store */
  Branch completion:
    PC = (branch ? ALUOutput : NPC)
Write back (“WB”)
  register-register or register-immediate ALU operation:
    RF[rd] = ALUOutput
  load instruction:
    RF[rd] = Load_Mem_Data

## Slide 10
0: don’t branch
1: branch