## Slide 1: ECE 463/563 Fall `20
pipelining: static branch prediction
Prof. Eric Rotenberg

## Slide 2: Static Branch Prediction: Rationale
Simple embedded processors
  Low cost and low power
  Die area and power are at a premium
  May not have area and power budget for a dynamic branch predictor
Static branch prediction
  Compiler gives hint to hardware as to most likely direction of branch
  Advantages:
    More accurate than always predicting not-taken
    No area or power cost for making predictions
  Disadvantages:
    Lower accuracy than dynamic branch prediction because branch always chooses one direction (cannot adapt to different behavior, exploit patterns, etc.)
    Hidden power cost: fetch more incorrect instructions

## Slide 3: Static Branch Prediction: ISA Support
Change branch encoding to add a likely bit
If compiler thinks branch is frequently taken
  Compiler sets likely bit = 1
If compiler thinks branch is frequently not-taken
  Compiler sets likely bit = 0

## Slide 4: Methods for setting likely bit
Heuristics
Profiling

## Slide 5: Heuristics
Example: BTFNT
  “backward-taken, forward-not-taken”
  Predict backward branches to be taken and forward branches to be not-taken
  Anticipates that most backward branches are loop branches
  Notes:
    Since branch target is PC relative, sign bit of offset = the prediction
    Jim Smith reports 70% accuracy for this scheme for scientific workloads

## Slide 6: Profiling
Three steps:
  Run the program multiple times with diverse inputs
  Record the average preferred direction (taken or not-taken) for each conditional branch
  Recompile to set the likely bits of conditional branches
Problems:
  A branch’s prediction is fixed for entire run
  What if inputs used for profiling are not representative?